| Project | ZigBee Alliance |  |
| --- | --- | --- |
| Title | ZigBee PRO Green Power feature Protocol Implementation Conformance (PICS) Proforma |
| Document | 105850r20 |  |
| Date Submitted | December 22, 2012 |  |
| Source | Bozena Erdmann (Technical Editor) Philips | Voice: +31 621 29 22 08 bozena.erdmann@philips.com |
| Re: | PICS for the Green Power feature of ZigBee |
| Abstract | As a part of formal conformance testing, manufacturers will be asked to submit a statement of protocol conformance with respect to the appropriate ZigBee devices required by the application profile under test. This document is intended to provide the form of that statement of conformance for the Green Power feature. |
| Purpose | This document, provides a form whereby developers can proffer a statement of protocol conformance to be tested under profile testing. |
| Notice | This document has been prepared to assist the ZigBee Alliance. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution will be posted in the member area of the ZigBee web site. |

Legal

Notice

Copyright © ZigBee Alliance, Inc. (2012). All rights Reserved. This information within this document is the property of the ZigBee Alliance and its use and disclosure are restricted.

Elements of ZigBee Alliance specifications may be subject to third party intellectual property rights, including without limitation, patent, copyright or trademark rights (such a third party may or may not be a member of ZigBee). ZigBee is not responsible and shall not be held responsible in any manner for identifying or failing to identify any or all such third party intellectual property rights.

This document and the information contained herein are provided on an “AS IS” basis and ZigBee DISCLAIMS ALL WARRANTIES EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO (A) ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OF THIRD PARTIES (INCLUDING WITHOUT LIMITATION ANY INTELLECTUAL PROPERTY RIGHTS INCLUDING PATENT, COPYRIGHT OR TRADEMARK RIGHTS) OR (B) ANY IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, TITLE OR NON-INFRINGEMENT. IN NO

EVENT WILL ZIGBEE BE LIABLE FOR ANY LOSS OF PROFITS, LOSS OF BUSINESS, LOSS OF USE OF DATA, INTERRUPTION OF BUSINESS, OR FOR ANY OTHER DIRECT, INDIRECT, SPECIAL OR EXEMPLARY, INCIDENTIAL, PUNITIVE OR CONSEQUENTIAL DAMAGES OF ANY KIND, IN CONTRACT OR IN TORT, IN CONNECTION WITH THIS DOCUMENT OR THE INFORMATION CONTAINED HEREIN, EVEN IF ADVISED OF THE POSSIBILITY OF SUCH LOSS OR DAMAGE. All Company, brand and product names may be trademarks that are the sole property of their respective owners.

The above notice and this paragraph must be included on all copies of this document that are made.

ZigBee Alliance, Inc.

2694 Bishop Drive, Suite 275

San Ramon, CA 94583

1	References

The following standards contain provisions, which, through reference in this document, constitute provisions of this standard. All the standards listed are normative references. At the time of publication, the editions indicated were valid. All standards are subject to revision, and parties to agreements based on this standard are encouraged to investigate the possibility of applying the most recent editions of the standards indicated below.

1.1  ZigBee Alliance documents

[R1]	ZigBee document 053474r19: ZigBee Specification 2007

[R2]	ZigBee document 08006r03: ZigBee 2007 Layer PICS and Stack Profiles

[R3]	ZigBee document 075123r04, ZigBee Cluster Library Specification

[R4]	ZigBee document 095499r24: Green Power Specification [R5]	ZigBee document 105521r21: Green Power test specification [R6]	ZigBee document 064113r08: ZigBee Cluster Library PICS

[R7]	ZigBee document 120624, Errata for GP 1.0 specification (095499)

[R8]	ZigBee document 120625, Errata for GP 1.0 Test specification (105521) [R9]	ZigBee document 120626, Errata for GP 1.0 PICS (105850)

1.2  IEEE documents

[R10]	IEEE Standard for Part 15.4: Wireless Medium Access Control (MAC) and Physical Layer (PHY)

specifications for Low Rate Wireless Personal Area Networks (LR-WPANs), 2003.

Table of Contents

1	References............................................................................................................................ 3

1.1	ZigBee Alliance documents ............................................................................................... 3

1.2	IEEE documents................................................................................................................. 3

Table of Contents ......................................................................................................................... 4

2	Introduction ........................................................................................................................... 5

2.1	Scope.................................................................................................................................. 5

2.2	Purpose............................................................................................................................... 5

3	Green Power certification status............................................................................................ 6

3.1	Not certified GP functionality............................................................................................ 6

3.2	Certified GP functionality .................................................................................................. 7

4	Abbreviations and special symbols........................................................................................ 9

5	Instructions for completing the PICS proforma .....................................................................10

6	Identification of the implementation ......................................................................................11

7	Identification of the protocol..................................................................................................13

8	Global statement of conformance.........................................................................................14

9	ZigBee stack profile [R2] errata ............................................................................................15

9.1	Modify the Table in “8.6.3.1.5 ZigBee Device Objects functions”, p.89, of 08006r03 .. 15

9.1.1	After AZD18, add ...................................................................................................... 15

9.2	Modify the Table in “8.4.2.2 Network layer frames” to include alias usage for Tx and

Rx, p.47, 15

9.2.1	after NDF4, add ......................................................................................................... 15

10	Green Power  feature ...........................................................................................................16

10.1	Green Power Device Types ............................................................................................. 16

11	Functionality of Green Power infrastructure device ..............................................................17

11.1	Green Power stub capabilities of GP infrastructure devices............................................ 17

11.2	Green Power: Support of minimal proxy functionality ................................................... 18

11.3	Functionality of GreenPower cluster ............................................................................... 19

11.3.1	GreenPower cluster: items common to client and server........................................... 23

11.3.2	Server side.................................................................................................................. 23

11.3.3	Client side .................................................................................................................. 26

11.3.4	Support of GP functionality ....................................................................................... 29

11.4	GPS application functionality .......................................................................................... 31

11.4.2	GPD command support by GPS ................................................................................ 32

12	Green Power Device functionality ........................................................................................35

12.1	GPD device description support ...................................................................................... 35

12.2	GPD functionality ............................................................................................................ 35

12.2.1	GPD Bidirectional operation...................................................................................... 36

12.2.2	GPD commissioning support ..................................................................................... 37

12.3	GPD application functionality ......................................................................................... 39

12.3.1	GPD command support by GPD ................................................................................ 39

12.3.2	ZigBee attribute support by GPD sensor devices ...................................................... 41

2	Introduction

To evaluate conformance of a particular implementation, it is necessary to have a statement of which capabilities and options have been implemented for a given standard. Such a statement is called a protocol implementation conformance statement (PICS).

2.1  Scope

This document provides the protocol implementation conformance statement (PICS) proforma for the ZigBee specifications cited in Reference [R4] in compliance with the relevant requirements.

This document addresses the Green Power feature of the ZigBee core stack, together with the necessary cluster-level components (Green Power cluster).

2.2  Purpose

The supplier of a protocol implementation claiming to conform to the Green Power feature shall complete the following PICS proforma and accompany it with the information necessary to identify fully both the supplier and the implementation.

The PICS is in the form of answers to a set of questions in the PICS proforma. The questions in a proforma consist of a systematic list of protocol capabilities and options as well as their implementation requirements. The implementation requirement indicates whether implementation of a capability is mandatory, optional, or conditional depending on options selected. When a protocol implementer answers questions in a PICS proforma, they would indicate whether an item is implemented or not, and provide explanations if an item is not implemented.

3  Green Power certification status 	 The current status of the certification and golden unit availability for GreenPower functionality is listed in the tables below.

3.1  Not certified GP functionality

Table 1 – Not certified GP functionality

| Item number |  | Item description | Reference |
| --- | --- | --- | --- |
| GPPCSF6 GPPCCF6 | Lightweight unicast communication functionality | [R4] A.3.2.8 |
| GPPCSF20 GPPCCF20 | GPD IEEE address functionality |  | [R4] A.3.2.8 |
| GPCF12B GPCF13B | TC-LK encryption of the GPD key exchanged during commissioning | [R4] A.3.9, A.1.5.9 |
| GPD0 GPS1A | GP Simple Generic 1-state Switch | [R4] A.4.3 |
| GPD1 GPS1B | GP Simple Generic 2-state Switch | [R4] A.4.3 |
| GPD3 GPS3 | GP Level Control Switch |  | [R4] A.4.3 |
| GPD4 GPS4 | GP Simple Sensor |  | [R4] A.4.3 |
| GPD5 GPS14A | GP Advanced Generic 1-state Switch | [R4] A.4.3 |
| GPD6 GPS14B | GP Advanced Generic 2-state Switch | [R4] A.4.3 |
| GPD10 GPS5 | GP Color Dimmer Switch |  | [R4] A.4.3 |
| GPD11 GPS6 | GP Light Sensor |  | [R4] A.4.3 |
| GPD12 GPS7 | GP Occupancy Sensor |  | [R4] A.4.3 |
| GPD20 GPS8 | GP Door Lock Controller |  | [R4] A.4.3 |
| GPD30 GPS9 | GP Temperature Sensor |  | [R4] A.4.3 |
| GPD31 GPS10 | GP Pressure Sensor |  | [R4] A.4.3 |
| GPD32 GPS11 | GP Flow Sensor |  | [R4] A.4.3 |
| GPD33 GPS12, GPS13, GPS9, GPS6 | GP Indoor Environment Sensor |  | [R4] A.4.3 |

3.2  Certified GP functionality

Table 2 – To-date certified device types

| Item number | Item description | Reference |
| --- | --- | --- |
| GPDT0 | Green Power Device (GPD) functionality | [R4] A.1.6, A.1.7 |
| GPDT2f | GP proxy functionality of Green Power Proxy (GPP) device | [R4] A.3.2.3 |
| GPDT2c | GP proxy functionality of Green Power Combo (GPC) device | [R4] A.3.2.4 |
| GPDT3t+ | GP sink functionality of Green Power Target+ (GPT+) device | [R4] A.3.2.2 |
| GPDT3c | GP sink functionality of Green Power Combo (GPC) device | [R4] A.3.2.4 |
| GPDT3cm | GP sink functionality of Green Power Combo minimum (GPCm) device | [R4] A.3.2.7 |

Table 3 – To-date certified GP functionality

| Item number | Item description | Reference |
| --- | --- | --- |
| GPPCSF1 GPPCCF1 | GP feature | [R4] A.3.2.8 |
| GPPCSF2 GPPCCF2 GPF4A | Direct communication (via GP stub) functionality | [R4] A.3.2.8 |
| GPPCSF3 GPPCCF3 | Derived groupcast communication functionality | [R4] A.3.2.8 |
| GPPCSF4 GPPCCF4 | Pre-commissioned groupcast communication functionality | [R4] A.3.2.8 |
| GPPCSF5 GPPCCF5 | Unicast communication functionality | [R4] A.3.2.8 |
| GPPCSF7 GPPCCF7 GPF9A GPF100 GPF102 GPF108 | Single-hop (in sink’s range) bidirectional operation functionality | [R4] A.3.2.8 |
| GPPCSF8 GPPCCF8 GPF9A GPF100 GPF102 GPF108 | Multi-hop (Proxy-based) bidirectional operation functionality | [R4] A.3.2.8 |
| GPPCSF9 GPPCCF9 | Proxy Table maintenance (active and passive) functionality | [R4] A.3.2.8 |
| GPPCSF10 GPPCCF10 GPCF1 GPCF2 GPCF4 GPCF10 GPCF11 GPCF12A GPCF13A | Single-hop (in sink’s range) commissioning (unidirectional and bidirectional) functionality | [R4] A.3.2.8 |

| Item number | Item description | Reference |
| --- | --- | --- |
| GPPCSF11 GPPCCF11 GPCF1 GPCF2 GPCF4 GPCF10 GPCF11 GPCF12A GPCF13A | Multi-hop (Proxy-based) commissioning (unidirectional and bidirectional) functionality | [R4] A.3.2.8 |
| GPPCSF12 GPPCCF12 GPCF1 GPCF2 GPCF4 GPCF10 GPCF11 GPCF12A GPCF13A | CT-based commissioning functionality | [R4] A.3.2.8 |
| GPPCSF13 GPPCCF13 GPF9A GPF100 GPCF7 | Maintenance of GPD (deliver channel/key during operation) functionality | [R4] A.3.2.8 |
| GPPCSF14 GPPCCF14 GPF8 | gpdSecurityLevel = 0b00 functionality | [R4] A.3.2.8 |
| GPPCSF15 GPPCCF15 GPF7 | gpdSecurityLevel = 0b01 functionality | [R4] A.3.2.8 |
| GPPCSF16 GPPCCF16 GPF6 | gpdSecurityLevel = 0b10 functionality | [R4] A.3.2.8 |
| GPPCSF17 GPPCCF17 GPF5 | gpdSecurityLevel = 0b11 functionality | [R4] A.3.2.8 |
| GPPCSF18 | Sink Table-based groupcast forwarding functionality | [R4] A.3.2.8 |
| GPPCSF19 | Translation Table functionality | [R4] A.3.2.8 |
| GPD2 GPS2 | GP On/Off switch functionality | [R4] A.4 |

4   Abbreviations and special symbols

Notations for requirement status:

| M | Mandatory |
| --- | --- |
| O | Optional |
| O.n | Optional, but support of at least one or only one (as indicated in the footnote to the O.n label) of the group of options labeled O.n is required. (Clarification - the number „n‟ is a label for the group, not a count of the number of options within the group, or the ordinal number of the option within the group. All options in the group are indicated identically as O.n) |
| N/A | Not applicable |
| X | Prohibited |
| Item label: Status | Status is conditional on support of the item with the given item label. |

Examples

1/  If items labeled A and B are both marked “O.n” this indicates that the status is optional for both A and B, but at least one of the two features described by items A and B is required to be implemented.

2/ If m items are each marked A: O.n, this indicates that, if item A is implemented, the status is optional for all of them, but at least one of the m features described by the items is required to be implemented.

5   Instructions for completing the PICS proforma

If a given implementation is claimed to conform to this standard, the actual PICS proforma to be filled in by a supplier shall be technically equivalent to the text of the PICS proforma in this annex, and shall preserve the numbering and naming and the ordering of the PICS proforma.

A PICS which conforms to this document shall be a conforming PICS proforma completed in accordance with the instructions for completion given in this annex.

The main part of the PICS is a fixed-format questionnaire, divided into five tables. Answers to the questionnaire are to be provided in the rightmost column, either by simply marking an answer to indicate a restricted choice (such as Yes or No), or by entering a value, set, or range of values.

6   Identification of the implementation

Implementation under test (IUT) identification

IUT name:

IUT version:

System under test (SUT) identification

SUT name: NXP HA-GP Combo Min Device

Software Version: JN-AN-1189 svn 12484 on HA-GP SDK v 1006

Hardware Version: DR 1192 0v3

Operating system (optional):

ZigBee stack revision and profile (should be PRO r20 or later): R20

Product supplier

Name:  NXP Semiconductor

Address:  Furnival Works Furnival Street Sheffield, UK S1 4QT

Telephone number:  +44(0) 114 281 2655

Facsimile number:

Email address:

Additional information:

Client

Name:  Paul Chilton

Address:  Furnival Works Furnival Street Sheffield, UK S1 4QT

Telephone number:  +44(0) 114 281 2655

Facsimile number:

Email address:  paul.chilton@nxp.com

Additional information:

PICS contact person

Name:

Address:

Telephone number:

Facsimile number:

Email address:

Additional information:

PICS/System conformance statement

7   Identification of the protocol

This PICS proforma applies to the Green Power feature, cited in Reference [R4].

8   Global statement of conformance

The implementation described in this PICS proforma meets all of the mandatory requirements of the referenced standards:

Green Power – 095499r24ZB

Note -- Answering „No‟ indicates non-conformance to the specified protocol standard. Non- supported mandatory capabilities are to be identified in the following tables, with an explanation by the implementer explaining why the implementation is non-conforming.

The supplier will have fully complied with the requirements for a statement of conformance by completing the statement contained in this subclause. That means, by clicking the above, the statement of conformance is complete.

9   ZigBee stack profile [R2] errata

9.1  Modify the Table in “8.6.3.1.5 ZigBee Device Objects functions”,

p.89, of 08006r03

9.1.1 After AZD18, add

| AZD19 | Does the device support conflict checking with its own short address, on reception of Device_annce with IEEE address 0xffffffffffffffff? | [R4] A.2 | M | Yes |
| --- | --- | --- | --- | --- |

9.2  Modify the Table in “8.4.2.2 Network layer frames” to include alias

usage for Tx and Rx, p.47,

9.2.1 after NDF4, add

| NDF5 | Does the device support reception of ZigBee NWK frames with non-incremental sequence number in the NWK header Sequence Number field? | ZigBe e | GPDT4: M | Yes |
| --- | --- | --- | --- | --- |
|  |  | Zi g B e e- | M |  |
| NDF6 | Does the device support transmission of ZigBee NWK frames with AliasSrcAddr and AliasSeqNumb, as supplied by next higher layer? | Zig Bee | GPDT4: O |  |
|  |  | ZigBee-PRO | GPDT2: M GPDT3t: X GPDT3t+: X GPDT3c: X GPDT3cm: M GPDT4: M | Yes |

10 Green Power  feature

The following tables are composed of the detailed questions to be answered, which make up the

PICS proforma.

10.1 Green Power Device Types

Table 4 – Green Power device types

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPDT0 | Does the product support GPD functionality? | [R4] A.1.6, A.1.7 | O.61 |  |
| GPDT1 | Does the product support the functionality of GP infrastructure device? | [R4] A.3.2 | O.6 | Yes |
| GPDT2 | Does the product support GPP functionality? | [R4] A.3.2.3 | GPDT1: O.72 | Yes |
| GPDT2f | Is the product programmed as a GPP? | [R4] A.3.2.3 | GPDT2: O.83 |  |
| GPDT2m | Is the product programmed as a GPPm? | [R4] A.3.2.6 | GPDT2: O.8 |  |
| GPDT2c4 | Is the product programmed as a GPC? | [R4] A.3.2.4 | GPDT2: O.8 |  |
| GPDT3 | Does the product support GPS functionality? | [R4] A.3.2 | GPDT1: O.7 |  |
| GPDT3t | Is the product programmed as a GPT? | [R4] A.3.2.1 | GPDT3: O.105 |  |
| GPDT3t+ | Is the product programmed as a GPT+? | [R4] A.3.2.2 | GPDT3: O.10 |  |
| GPDT3c | Is the product programmed as a GPC? | [R4] A.3.2.4 | GPDT3: O.10 |  |
| GPDT3cm | Is the product programmed as a GPCm? | [R4] A.3.2.7 | GPDT3: O.10 | Yes |
| GPDT4 | Does the product support GP commissioning tool functionality | [R4] A.3.2.5 | GPDT1: O.7 |  |
| GPDT4ct | Is the product programmed as a GP Commissioning Tool? | [R4] A.3.2.5 | GPDT1: O |  |

Please note: all PICS items applicable for all the GPP and GPS subtypes, use the generic item

label: GPDT2 or GPDT3, respectively.

The sub-type specific item labels (GPDT2f, GPDT2m, GPDT2c, GPDT3t, GPDT3t+, GPDT3c, GPDT3cm) are used for sub-type specific requirements.

1 O.6 - Device under test shall select only one of these options.

2 O.7 - Device under test shall select at least one of these options.

3 O.8 - Device under test shall select only one of these options.

4 Note: this item covers only the client side, i.e. proxy functionality of the GPC.

5 O.10 – Device under test shall select only one of these options.

11 Functionality of Green Power infrastructure device

11.1 Green Power stub capabilities of GP infrastructure devices

This PICS table applies to GP infrastructure devices GPDT1, GPDT2, GPDT3 and GPDT4.

All PICS items applicable for all the generic GP device types, use the generic item label: GPDT1 if applicable to all devices, or GPDT2, GPDT3, and GPDT4, if applicable in general  to GPP, GPS or GPCT functionality, respectively.

The sub-type specific item labels (GPDT2f, GPDT2m, GPDT2c, GPDT3t, GPDT3t+, GPDT3c, GPDT3cm) are used for sub-type specific requirements.

Since GPDT0 are not ZigBee-PRO devices, their functionality is not discussed here. Please see ZCL PICS for GPDT0 compliance requirements.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPF1 | Does the device implement cGP stub? | [R4] A.1 | GPDT2: M GPDT3t: X GPDT3t+: M GPDT3c: M GPDT3cm: M GPDT4: M | Yes |
| GPF2 | Does the device implement dGP stub? | [R4] A.1 | GPDT2: M GPDT3t: X GPDT3t+: M GPDT3c: M GPDT3cm: M GPDT4: M | Yes |
| GPF3 | Does the device support the general Green Power Device Frame format? | [R4] A.1.4 | GPDT2: M GPDT3t: X GPDT3t+: M GPDT3c: M GPDT3cm: M GPDT4: M | Yes |
| GPF3A | Does the device support nwkcProtocolVersion = 0x3? | [R4] A.1.4 | GPDT2: M GPDT3t: X GPDT3t+: M GPDT3c: M GPDT3cm: M GPDT4: M | Yes |
| GPF4A | Does the device support receiving GPDF frame format with ApplicationID sub-field of the Extended NWK Frame Control field set to 0b000? | [R4] A.1.4 | GPDT2: M GPDT3t: X GPDT3t+: M GPDT3c: M GPDT3cm: M GPDT4: M | Yes |
| GPF4B | Does the device support receiving GPDF frame format with ApplicationID sub-field of the Extended NWK Frame Control field set to 0b010? | [R4] A.1.4 | GPDT2: O GPDT3: O GPDT4: M | Yes |
| GPF5 | Does the device’s dGP stub support GPDF SecurityLevel=0b11? | [R4] A.1.5.4; A.3.7.2 | GPDT2m: O GPDT2f: M GPDT2c: M GPDT3t: X GPDT3t+: O.46 GPDT3c: M GPDT3cm: O.4 GPDT4: M |  |
| GPF6 | Does the device’s dGP stub support GPDF SecurityLevel=0b10? | [R4] A.1.5.4; A.3.7.2 | GPDT2: M GPDT3t: X GPDT3t+: O.4 GPDT3c: M GPDT3cm: O.4 GPDT4: M |  |

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPF7 | Does the device’s dGP stub support GPDF SecurityLevel=0b01? | [R4] A.1.5.4; A.3.7.2 | GPDT2m: O GPDT2f: M GPDT2c: M GPDT3t: X GPDT3t+: O.4 GPDT3c: M GPDT3cm: O.4 GPDT4: M |  |
| GPF8 | Does the device’s dGP stub support GPDF SecurityLevel=0b00? | [R4] A.1.5.4; A.3.7.2 | GPDT2m: M GPDT2f: M GPDT2c: M GPDT3t: X GPDT3t+: O.4 GPDT3c: M MGPDT3cm: O.4 GPDT4: M | Yes |
| GPF9A | Does the device support transmitting GPDF frame format with ApplicationID sub-field of the Extended NWK Frame Control field set to 0b000? | [R4] A.1 | GPDT2m: O GPDT2f: M GPDT3t: X GPDT3t+: M GPDT3c: M GPDT3cm: M GPDT4: M | Yes |
| GPF9B | Does the device support transmitting GPDF frame format with ApplicationID sub-field of the Extended NWK Frame Control field set to 0b010? | [R4] A.1 | GPDT2: O GPDT3: O GPDT4: M | Yes |
| GPSF1 | Does the device support gpTxQueue? | [R4] A.1 | GPDT2m: O GPDT2f: M GPDT3t: X GPDT3t+: M GPDT3c: M GPDT3cm: M GPDT4: M |  |

11.2 Green Power: Support of minimal proxy functionality

This PICS table applies to GP infrastructure devices GPDT1, GPDT2, GPDT3 and GPDT4.

All PICS items applicable for all the generic GP device types, use the generic item label: GPDT1 if applicable to all devices, or GPDT2, GPDT3, and GPDT4, if applicable in general  to GPP, GPS or GPCT functionality, respectively.

The sub-type specific item labels (GPDT2f, GPDT2m, GPDT2c, GPDT3t, GPDT3t+, GPDT3c, GPDT3cm) are used for sub-type specific requirements.

Since GPDT0 are not ZigBee-PRO devices, their functionality is not discussed here. Please see ZCL PICS for GPDT0 compliance requirements.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPC0 | Does the device support minimum GP proxy functionality? | [R4] A.3.2.6 | GPDT2m: M GPDT2f: M GPDT2c: M GPDT3t: X GPDT3t+: O GPDT3c: M MGPDT3cm: M GPDT4: O | Yes |
| GPPC1 | Is the GreenPower cluster supported? | [R4] A.3 | GPPC0: M | Yes |
| GPPC2 | Does the device support Green Power End Point (GPEP)? | [R4] A.3.1 | GPPC0: M | Yes |
| GPPC3 | Does the device support GPEP duplicate filtering? | [R4] A.3.6.1 | GPPC0: M | Yes |
| GPPCC1 | Is the GreenPower cluster supported as a client? | [R4] A.3.4 | GPPC0: O.57 GPPC0&GPDT2m: M | Yes |

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCC2 | Is the gppMaxProxyTableEntries attribute supported? | [R4] A.3.4.2.1 | GPPCC1: M |  |
| GPPCC3A | Is the Proxy Table attribute supported? | [R4]A.3.4.2.2 | GPPCC1: M |  |
| GPPCC3B | Is the minimum number of 10 entries in the Proxy Table attribute supported? | [R4]A.3.4.2.2 | GPPCC1: M |  |
| GPPCC8 | Is the gppFunctionality attribute supported? | [R4]A.3.4.2.7 | GPPCC1: M |  |
| GPPCC9 | Is the gppActiveFunctionality attribute supported? | [R4]A.3.4.2.8 | GPPCC1: M |  |
| GPPCS1 | Is the GreenPower cluster supported as a server? | [R4]A.3.3 | GPPC0: O.5 GPPC0&GPDT3cm: M | Yes |
| GPPCS2 | Is the gppMaxSinkTableEntries attribute supported? | [R4]A.3.3.2.1 | GPPCS1: M | Yes |
| GPPCS3A | Is the Sink Table attribute supported? | [R4]A.3.3.2.2 | GPPCS1: M | Yes |
| GPPCS3B | Is the minimum number of 5 entries in the Sink Table attribute supported? | [R4]A.3.3.2.2 | GPPCS1: M | Yes |
| GPPCS8 | Is the gpsFunctionality attribute supported? | [R4]A.3.3.2.7 | GPPCS1: M | Yes |
| GPPCS9 | Is the gpsActiveFunctionality attribute supported? | [R4]A.3.3.2.8 | GPPCS1: M | Yes |
| GPPC101 | Is the gpSharedSecurityKeyType attribute supported? | [R4]A.3.3.3.1 | GPPC0: M |  |
| GPPC102 | Is the gpSharedSecurityKey attribute supported? | [R4]A.3.3.3.2 | GPPC0: M |  |
| GPPC103 | Is the gpLinkKey attribute supported? | [R4]A.3.3.3.3 | GPPC0: M |  |
| GPPCC102 | Is transmission of the GP Notification command in derived groupcast supported? | [R4]A.3.3.4.1 | GPDT2m: M GPDT3cm: O | Yes |
| GPPCC103 | Is transmission of the GP Notification command in commissioned groupcast supported? | [R4]A.3.3.4.1 | GPDT2m: M GPDT3cm: M | Yes |
| GPPCC110 | Is reception of the GP Pairing command supported? | [R4] A.3.3.5.2 | GPPCC1: M |  |
| GPPCS110 | Is reception of the GP Pairing Configuration command supported? | [R4] A.3.3.4.7 | GPPCS1: M | Yes |

11.3 Functionality of GreenPower cluster

The	GPPCCF$	items	refer	ONLY	to	the	PROXY	functionality	of	the	DUT. Analogously, the GPPCSF$ items refer ONLY to the SINK functionality of the DUT.

Thus, for a GPC, each item set covers only a part of GPC’s functionality. Therefore, for the two functional parts of the GPC, both PICS items sets have to be checked independently.

Table 5 – GreenPower cluster feature support

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCSF1 | Is GP feature supported as a server? (GP feature sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: M GPDT4: M | Yes |
| GPPCSF2 | Is Direct communication (via GP stub) supported as a server? (Direct communication sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: X GPDT3t+: M GPDT3c: M GPDT3cm: M GPDT4: M | Yes |
| GPPCSF3 | Is Derived groupcast communication supported as a server? (Derived groupcast communication sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: O.118 GPDT3t+: O.11 GPDT3c: O.11 GPDT3cm: M GPDT4: O | Yes |

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCSF4 | Is Pre-commissioned groupcast communication supported as a server? (Pre-commissioned groupcast communication sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: O.11 GPDT3t+: O.11 GPDT3c: O.11 GPDT3cm: M (GPDT3 & GPPCSF3: M) GPDT4: O | Yes |
| GPPCSF5 | Is Unicast communication supported as a server? (Unicast communication sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: O.11 GPDT3t+: O.11 GPDT3c: O.11 GPDT3cm: X GPDT4: O |  |
| GPPCSF6 | Is Lightweight unicast communication supported as a server? (Lightweight unicast communication sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: O.11 GPDT3t+: O.11 GPDT3c: O.11 GPDT3cm: X GPDT4: O |  |
| GPPCSF7 | Is Single-hop (in sink’s range) bidirectional operation supported as a server? (Single-hop bidirectional operation sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: X GPDT3t+: O GPDT3c: O GPDT3cm: O GPDT4: O |  |
| GPPCSF8 | Is Multi-hop (Proxy-based) bidirectional operation supported as a server? (Multi-hop bidirectional operation sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: O GPDT3t+: O GPDT3c: O GPDT3cm: O GPDT4: O |  |
| GPPCSF9 | Is Proxy Table maintenance (active and passive) supported as a server? (Proxy Table maintenance sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: M GPDT3t+: M GPDT3c: M GPDT3cm: O GPDT4: O |  |
| GPPCSF10 | Is Single-hop (in sink’s range) commissioning (unidirectional and bidirectional) supported as a server? (Single-hop commissioning sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: N/A GPDT3t+: M GPDT3c: M GPDT3cm: M GPDT4: M | Yes |
| GPPCSF11 | Is Multi-hop (Proxy-based) commissioning (unidirectional and bidirectional) supported as a server? (Multi-hop commissioning sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: M GPDT3t+: O GPDT3c: O GPDT3cm: O GPDT4: O | Yes |
| GPPCSF12 | Is CT-based commissioning supported as a server? (CT- based commissioning sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: O GPDT3t+: O GPDT3c: O GPDT3cm: M GPDT4: M | Yes |
| GPPCSF13 | Is Maintenance of GPD (deliver channel/key during operation) supported as a server? (Maintenance of GPD sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: O GPDT4: O |  |

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCSF14 | Is gpdSecurityLevel = 0b00 supported as a server? (gpdSecurityLevel = 0b00 sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: O.129 GPDT4: O | Yes |
| GPPCSF15 | Is gpdSecurityLevel = 0b01 supported as a server? (gpdSecurityLevel = 0b01 sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: O.12 GPDT4: O |  |
| GPPCSF16 | Is gpdSecurityLevel = 0b10 supported as a server? (gpdSecurityLevel = 0b10 sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: O.12 GPDT4: O |  |
| GPPCSF17 | Is gpdSecurityLevel = 0b11 supported as a server? (gpdSecurityLevel = 0b11 sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: O.12 GPDT4: O |  |
| GPPCSF18 | Is SinkTable-based groupcast forwarding supported as a server? (SinkTable-based groupcast forwarding sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3t: O GPDT3t+: O GPDT3c: O GPDT3cm: M GPDT4: O | Yes |
| GPPCSF19 | Is Translation Table feature supported as a server? (Translation Table sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: O GPDT4: O | Yes |
| GPPCSF20 | Is GPD IEEE address feature supported as a server? (GPD IEEE address sub-field of the gpsFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: O GPDT4: M |  |
| GPPCCF1 | Is GP feature supported as a client? (GP feature sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: M GPDT3: N/A GPDT4: O |  |
| GPPCCF2 | Is Direct communication (via GP stub) supported as a client? (Direct communication sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: M GPDT3: N/A GPDT4: O |  |
| GPPCCF3 | Is Derived groupcast communication supported as a client? (Derived groupcast communication sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: M GPDT3t: N/A GPDT3t+: N/A GPDT3c: N/A GPDT3cm: M GPDT4: O |  |
| GPPCCF4 | Is Pre-commissioned groupcast communication supported as a client? (Pre-commissioned groupcast communication sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: M GPDT3t: N/A GPDT3t+: N/A GPDT3c: N/A GPDT3cm: M GPDT4: O |  |
| GPPCCF5 | Is Unicast communication supported as a client? (Unicast communication sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2c: M GPDT2f: M GPDT2m: O GPDT3: N/A GPDT4: O |  |
| GPPCCF6 | Is Lightweight unicast communication supported as a client? (Lightweight unicast communication sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: O GPDT3: N/A GPDT4: O |  |
| GPPCCF7 | Is Single-hop (in sink’s range) bidirectional operation supported as a client? (Single-hop bidirectional operation sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: N/A GPDT4: O |  |
| GPPCCF8 | Is Multi-hop (Proxy-based) bidirectional operation supported as a client? (Multi-hop bidirectional operation sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2c: O GPDT2f: O GPDT2m: O GPDT3: N/A GPDT4: O |  |

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCCF9 | Is Proxy Table maintenance (active and passive) supported as a client? (Proxy Table maintenance sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2c: M GPDT2f: M GPDT2m: O GPDT3: N/A GPDT4: O |  |
| GPPCCF10 | Is Single-hop (in sink’s range) commissioning (unidirectional and bidirectional) supported as a client? (Single-hop commissioning sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: N/A GPDT4: O |  |
| GPPCCF11 | Is Multi-hop (Proxy-based) commissioning (unidirectional and bidirectional) supported as a client? (Multi-hop commissioning sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2f: M GPDT2m: O GPDT2c: M GPDT3: N/A GPDT4: O |  |
| GPPCCF12 | Is CT-based commissioning supported as a client? (CT- based commissioning sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2c: M GPDT2f: M GPDT2m: O GPDT3: N/A GPDT4: O |  |
| GPPCCF13 | Is Maintenance of GPD (deliver channel/key during operation) supported as a client? (Maintenance of GPD sub- field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2f: M GPDT2m: O GPDT2c: M GPDT3: N/A GPDT4: O |  |
| GPPCCF14 | Is gpdSecurityLevel = 0b00 supported as a client? (gpdSecurityLevel = 0b00 sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2f: M GPDT2m: M GPDT2c: M GPDT3: N/A GPDT4: O |  |
| GPPCCF15 | Is gpdSecurityLevel = 0b01 supported as a client? (gpdSecurityLevel = 0b01 sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2f: M GPDT2m: O GPDT2c: M GPDT3: N/A GPDT4: O |  |
| GPPCCF16 | Is gpdSecurityLevel = 0b10 supported as a client? (gpdSecurityLevel = 0b10 sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2f: M GPDT2m: M GPDT2c: M GPDT3: N/A GPDT4: O |  |
| GPPCCF17 | Is gpdSecurityLevel = 0b11 supported as a client? (gpdSecurityLevel = 0b11 sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2f: M GPDT2m: O GPDT2c: M GPDT3: N/A GPDT4: O |  |
| GPPCCF18 | Is SinkTable-based groupcast forwarding supported as a client? (SinkTable-based groupcast forwarding sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: N/A GPDT4: N/A |  |
| GPPCCF19 | Is Translation Table feature supported as a client? (Translation Table sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: N/A GPDT3: N/A GPDT4: N/A |  |
| GPPCCF20 | Is GPD IEEE address feature supported as a client? (GPD IEEE address sub-field of the gppFunctionality attribute set?) | [R4] A.3.2.8 | GPDT2: O GPDT3: N/A GPDT4: N/A |  |

11.3.1	GreenPower cluster: items common to client and server

Table 6 – GreenPower cluster items common to client and server

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPC1 | Is the GreenPower cluster supported? | [R4] A.3 | GPDT1: M | Yes |
| GPPC2 | Does the device support Green Power End Point (GPEP)? | [R4] A.3.1 | GPDT1: M | Yes |
| GPPC3 | Does the device support GPEP duplicate filtering? | [R4] A.3.6.1.2 | GPDT1: M | Yes |
| GPPC3r | Does the device support random MAC sequence number for GPD commands’ duplicate filtering? | [R4] A.3.6.1.2 | GPDT1&& GPF8: M | Yes |
| GPPC3i | Does the device support incremental MAC sequence number for GPD commands’ duplicate filtering? | [R4] A.3.6.1.2 | GPDT1&& GPF8: M | Yes |
| GPPC3s | Does the device support GPD security frame counter for GPD commands’ duplicate filtering? | [R4] A.3.6.1.2 | GPDT1&& (GPF5¦¦GPF6¦¦GPF7): M |  |
| GPPC4 | Does the device support transmission of Device_annce for the alias? | [R4] A.3.6.3.3, A.3.6.3.4 | GPDT1: M | Yes |
| GPPC5 | Does the device support conflict checking for the alias on reception of Device_annce? | [R4] A.3.6.3.3, A.3.6.3.4 | GPDT1: M | Yes |
| GPPC101 | Is the gpSharedSecurityKeyType attribute supported? | [R4] A.3.3.3.1 | GPDT1&& (GPF5¦¦GPF6¦¦GPF7): M |  |
| GPPC102 | Is the gpSharedSecurityKey attribute supported? | [R4] A.3.3.3.2 | GPDT1&& (GPF5¦¦GPF6¦¦GPF7): M |  |
| GPPC103 | Is the gpLinkKey attribute supported? | [R4] A.3.3.3.3 | GPDT1&& (GPF5¦¦GPF6¦¦GPF7): M |  |

11.3.2	Server side

Table 7 – GreenPower cluster server capabilities

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCS1 | Is the GreenPower cluster supported as a server? | [R4] A.3.3 | GPDT2: O GPDT3: M GPDT4: M GPPCSF1: M | Yes |
| GPPCS2 | Is the gpsMaxSinkTableEntries attribute supported? | [R4] A.3.3.2.1 | GPDT2: X GPDT3: M GPDT4: O | Yes |
| GPPCS3A | Is the Sink Table attribute supported? | [R4] A.3.3.2.2 | GPDT2: X GPDT3: M GPDT4: O | Yes |
| GPPCS3B | Is the required minimum number of entries in the Sink Table attribute supported?10 | [R4] A.3.3.2.2 | GPDT3: 5 | Yes |
| GPPCS4 | Is the gpsCommunication mode attribute supported? | [R4] A.3.3.2.3 | GPDT2: X GPDT3: M GPDT4: O | Yes |
| GPPCS5 | Is the gpsCommissioningExitMode attribute supported? | [R4] A.3.3.2.4 | GPDT2: X GPDT3: M GPDT4: O | Yes |

10 5 is the default minimum number of entries defined by the GP Proxy cluster [R4]. A particular profiles adopting the cluster may mandate different value.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCS6 | Is the gpsCommissioningWindow attribute supported? | [R4] A.3.3.2.5 | GPDT2: X GPDT3: O GPDT4: O | Yes |
| GPPCS7 | Is the gpsSecurityLevel attribute supported? | [R4] A.3.3.2.6 | GPDT2: X GPDT3: M GPDT4: O | Yes |
| GPPCS8 | Is the gpsFunctionality attribute supported? | [R4] A.3.3.2.7 | GPDT2: X GPDT3: M GPDT4: O | Yes |
| GPPCS9 | Is the gpsActiveFunctionality attribute supported? | [R4] A.3.3.2.8 | GPDT2: X GPDT3: M GPDT4: O | Yes |
| GPPCS99 | Is Translation Table supported? | [R4] A.3.5.2.2 | GPDT2: X GPDT3: O GPDT4: O GPPCSF19: M |  |
| GPPCS100 | Is reception of the GP Notification command supported? | [R4] A.3.2.10 [R4] A.3.3.3 | GPDT2c: M GPDT2f: M GPDT2m: O GPDT3: M GPDT4: O | Yes |
| GPPCS101 | Is reception of the GP Notification command in unicast supported? | [R4] A.3.2.10 [R4] A.3.3.4.1 | GPDT2: X GPDT3t¦¦GPDT3t+¦¦GPDT3c: O.1411 GPDT3cm: X GPPCSF5¦¦GPPCSF6: M GPDT4: O |  |
| GPPCS102 | Is reception of the GP Notification command in derived groupcast supported? | [R4] A.3.2.10 [R4] A.3.3.4.1 | GPDT2& (GPPCCF8¦¦GPPCCF9¦¦GPPCCF13) : M GPDT3cm: O GPDT3t¦¦GPDT3t+¦¦GPDT3c: O.14 GPDT4: O | Yes |
| GPPCS103 | Is reception of the GP Notification command in commissioned groupcast supported? | [R4] A.3.2.10 [R4] A.3.3.4.1 | GPDT2& (GPPCCF8¦¦GPPCCF9¦¦ GPPCCF13): M GPDT3cm: M GPDT3t¦¦GPDT3t+¦¦GPDT3c: O.14 GPPCS102: M GPDT4: O | Yes |
| GPPCS104 | Is reception of the GP Notification command in broadcast supported? | [R4] A.3.2.10 [R4] A.3.3.4.1 [R4] A.5.2.1 | GPDT2:O GPPCCF9: M GPDT3: O GPPCSF9: M GPDT4: O |  |
| GPPCS105 | Is reception of the GP Pairing Search command supported? | [R4] A.3.2.10 [R4] A.3.3.4.2 | GPDT2: O GPPCCF9: O GPDT3cm: O GPDT3t, GPDT3t+, GPDT3c: M GPDT4: O GPPCSF9: M |  |
| GPPCS106 | Is reception of the GP Tunneling Stop command supported? | [R4] A.3.2.10 [R4] A.3.4.4.1 | GPDT2m: O GPPCCF5: M GPDT2f: M GPDT2c: M GPDT3: X GPDT4: O |  |

11 O.14: The device under test shall implement at least one of those options; only one is enabled at any given time.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCS107 | Is reception of the GP Commissioning Notification command supported? | [R4] A.3.2.10 [R4] A.3.3.4.4 | GPDT2m: O (GPPCCF11: M) GPDT2f¦¦GPDT2c: M GPDT3t: M GPDT3t+¦¦GPDT3c¦¦GPDT3cm: O (GPPCSF11: M) GPDT4: O | Yes |
| GPPCS108 | Is reception of the GP Translation Table Update command supported? | [R4] A.3.2.10 [R4] A.3.3.4.6 | GPDT2: X GPDT3: O GPDT4: O GPPCSF19: M |  |
| GPPCS109 | Is reception of the GP Translation Table Request command supported? | [R4] A.3.2.10 [R4] A.3.3.4.5 | GPDT2: X GPDT3: O GPDT4: O GPPCSF19: M |  |
| GPPCS110 | Is reception of the GP Pairing Configuration command supported? | [R4] A.3.2.10 [R4] A.3.3.4.7 | GPDT2: X GPDT3cm: M GPDT3t¦¦GPDT3t+¦¦GPDT3c: O GPDT4: O GPPCSF4 ¦¦ GPPCSF12 ¦¦ GPPCSF18: M | Yes |
| GPPCS150 | Is transmission of the GP Notification Response command supported? | [R4] A.3.2.10 [R4] A.3.3.5.1 | GPDT2: X GPDT3cm: X GPDT3t¦¦GPDT3t+¦¦GPDT3c: O GPDT4: O GPPCSF5¦¦GPPCSF6: M |  |
| GPPCS151 | Is transmission of the GP Response command supported? | [R4] A.3.2.10 [R4] A.3.3.5.4 | GPDT2: X GPDT3: O GPDT4: O GPPCSF8¦¦ GPPCSF11¦¦GPPCSF 13: M | Yes |
| GPPCS152 | Is transmission of the GP Pairing command supported? | [R4] A.3.2.10 [R4] A.3.3.5.2 | GPDT2: X GPDT3: M GPDT4: M | Yes |
| GPPCS153 | Is generation of the GP Pairing command with RemoveGPD sub-field set to 0b1 supported? | [R4] A.3.2.10 [R4] A.3.3.5.2 | GPDT2: X GPDT3: O GPDT4: M | Yes |
| GPPCS154 | Is transmission of the GP Proxy Commissioning Mode command supported? | [R4] A.3.2.10 [R4] A.3.3.5.3 | GPDT2: X GPDT3t: M GPDT3t+¦¦GPDT3c¦¦GPDT3cm: O GPDT4: M GPPCSF11: M | Yes |
| GPPCS155 | Is transmission of the GP Translation Table Response command supported? | [R4] A.3.2.10 [R4] A.3.3.5.5 | GPDT2: X GPDT3: O GPDT3&&GPPCS109:M GPDT4: O GPPCSF19: M |  |
| GPPCS201 | Is persistent storage of Sink Table supported? | [R4] A.3.2.10 [R4] A.3.3.2.2 | GPDT2: X GPDT3: M GPDT4: O | Yes |

11.3.3	Client side

Table 8 – GreenPower cluster client capabilities

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCC1 | Is the GreenPower cluster supported as a client? | [R4] A.3.4 | GPDT2: M GPDT3: O GPDT4: O | Yes |
| GPPCC2 | Is the gppMaxProxyTableEntries attribute supported? | [R4] A.3.4.2.1 | GPDT2: M GPDT3: X GPDT4: O |  |
| GPPCC3A | Is the Proxy Table attribute supported? | [R4] A.3.4.2.2 | GPDT2: M GPDT3: X GPDT4: O |  |
| GPPCC3B | Is the required minimal number of entries in the Proxy Table attribute supported?12 | [R4] A.3.4.2.2 | GPDT2: 10 |  |
| GPPCC3C | Is the required minimal number of entries in the Sink address list per Proxy Table entry supported? | [R4] A.3.4.2.2 | GPDT2 && GPPCSF5: 2 |  |
| GPPCC3D | Is the required minimal number of entries in the Sink group list per Proxy Table entry supported? | [R4] A.3.4.2.2 | GPDT2 && GPPCSF4: 2 |  |
| GPPCC3E | Is the required minimal number of simultaneously used entries in the Sink address list and in the Sink group list per Proxy Table entry supported? | [R4] A.3.4.2.2 | GPDT2 && GPPCSF5 && GPPCSF5: 1+1 |  |
| GPPCC4 | Is the gppNotificationRetryNumber attribute supported? | [R4] A.3.4.2.3 | GPDT2f¦¦GPDT2c: M GPDT2m: O (GPPCCF5¦¦GPPCCF6: M) GPDT3: X GPDT4: O |  |
| GPPCC5 | Is the gppNotificationRetryTimer attribute supported? | [R4] A.3.4.2.4 | GPDT2f¦¦GPDT2c: M GPDT2m: O (GPPCCF5¦¦GPPCCF6: M) GPDT3: X GPDT4: O |  |
| GPPCC6 | Is the gppMaxSearchCounter attribute supported? | [R4] A.3.4.2.5 | GPDT2: O (GPPCCF9: M) GPDT3: X GPDT4: O |  |
| GPPCC7 | Is the gppBlockedSrcID attribute supported? | [R4] A.3.4.2.6 | GPDT2: O (GPPCCF9: M) GPDT3: X GPDT4: O |  |
| GPPCC8 | Is the gppFunctionality attribute supported? | [R4] A.3.4.2.7 | GPDT2: M GPDT3: X GPDT4: O |  |
| GPPCC9 | Is the gppActiveFunctionality attribute supported? | [R4] A.3.4.2.8 | GPDT2: M GPDT3: X GPDT4: O |  |
| GPPCC100 | Is transmission of the GP Notification command supported? | [R4] A.3.2.10 [R4] A.3.3.4.1 | GPDT2: M GPDT3cm: M GPDT3t¦GPDT3t+¦¦GPDT3c: X GPDT4: O |  |
| GPPCC101 | Is transmission of the GP Notification command in unicast supported? | [R4] A.3.2.10 [R4] A.3.3.4.1 | GPDT2f¦¦GPDF2c: M GPDT2m: O GPDT3: X GPPCCF 5¦¦GPPCCF6: M GPDT4: O |  |

12 10 is the default minimum number of entries defined by the GP Proxy cluster [R4]. A particular profiles adopting the cluster may mandate different value.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCC102 | Is transmission of the GP Notification command in derived groupcast supported? | [R4] A.3.2.10 [R4] A.3.3.4.1 | GPDT2: M GPDT3cm: O GPDT4: O | Yes |
| GPPCC103 | Is transmission of the GP Notification command in commissioned groupcast supported? | [R4] A.3.2.10 [R4] A.3.3.4.1 | GPDT2: M GPDT3cm: M GPDT4: O | Yes |
| GPPCC104 | Is transmission of the GP Notification command in broadcast supported? | [R4] A.3.2.10 [R4] A.3.3.4.1 | GPDT2¦¦GPDT3cm: O GPPCCF9:M GPDT4: O |  |
| GPPCC105 | Is transmission of the GP Notification command in multiple communication modes supported? | [R4] A.3.2.10 [R4] A.3.5.2.1 | GPDT2c¦¦GPDT2f: M GPDT2m¦¦GPDT3cm: O GPPCCF 5¦¦GPPCCF6: M GPDT4: O |  |
| GPPCC106 | Is transmission of the GP Pairing Search command supported? | [R4] A.3.2.10 [R4] A.3.4.2 | GPDT2¦¦GPDT3cm: O GPPCCF9: M GPDT3t¦¦GPDT3t+¦¦GPDT3c: X GPDT4: M |  |
| GPPCC107 | Is transmission of the GP Tunneling Stop command supported? | [R4] A.3.2.10 [R4] A.3.4.4.1 | GPDT2c¦¦GPDT2f: M GPDT2m: O GPPCCF5¦¦GPPCCF6: M GPDT3: X GPDT4: O |  |
| GPPCC108 | Is transmission of the GP Commissioning Notification command supported? | [R4] A.3.2.10 [R4] A.3.3.4.4 | GPDT2c¦¦GPDT2f: M GPDT2m¦¦GPDT3cm: O GPPCCF11: M GPDT3t¦¦GPDT3t+¦¦GPDT3c: X GPDT4: O |  |
| GPPCC108 | Is transmission of the GP Translation Table Update command supported? | [R4] A.3.2.10 [R4] A.3.3.4.5 [R4] A.3.2.5 | GPDT2: X GPDT3: O GPDT4: M |  |
| GPPCC109 | Is transmission of the GP Translation Table Request command supported? | [R4] A.3.2.10 [R4] A.3.3.4.6 [R4] A.3.2.5 | GPDT2: X GPDT3: O GPDT4: M |  |
| GPPCC110 | Is transmission of the GP Pairing Configuration command supported? | [R4] A.3.2.10 [R4] A.3.3.4.7 [R4] A.3.2.5 | GPDT2: X GPDT3cm: M GPDT3t¦¦GPDT3t+¦¦GPDT3c: O GPDT4: M GPPCSF4 ¦¦ GPPCSF18: M | Yes |
| GPPCC150 | Is reception of the GP Notification Response command supported? | [R4] A.3.2.10 [R4] A.3.3.5.1 | GPDT2c¦¦GPDT2f: M GPDT2m: O GPPCCF5¦¦GPPCCF6: M GPDT3: X GPDT4: O |  |
| GPPCC151 | Is reception of the GP Pairing command supported? | [R4] A.3.2.10 [R4] A.3.3.5.2 | GPDT2: M GPDT3: X GPDT4: M |  |
| GPPCC152 | Is reception of the GP Pairing command with RemoveGPD sub-field set to 0b1 supported? | [R4] A.3.2.10 [R4] A.3.3.5.2 | GPDT2: M GPDT3: X GPDT4: M |  |
| GPPCC153 | Is reception of the GP Proxy Commissioning Mode command supported? | [R4] A.3.2.10 [R4] A.3.3.5.3 | GPDT2c¦¦GPDT2f: M GPDT2m: O GPPCCF11: M GPDT3: O GPDT4: M | Yes |
| GPPCC154 | Is reception of the GP Response command supported? | [R4] A.3.2.10 [R4] A.3.3.5.4 | GPDT2c¦¦GPDT2f: M GPDT2m¦¦GPDT3cm: O GPPCCF8¦¦GPPCCF11¦¦GPPCCF 13:M GPDT3t¦¦GPDT3t+¦¦GPDT3c: X GPDT4: O |  |

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPPCC155 | Is reception of the GP Translation Table Response command supported? | [R4] A.3.2.10 [R4] A.3.3.5.5 [R4] A.3.2.5 | GPDT2: X GPDT3: O (GPDT3&&GPPCC109:M) GPDT4: M |  |
| GPPCC200 | Is persistent storage of Proxy Table supported? | [R4] A.3.4.2.2 | GPPCC3A: M |  |
| GPPCC201 | Is handling of Proxy Table entries with status other than active and valid supported? | [R4] A.3.5.2.2 | GPDT2: O GPDT3: X GPDT4: O GPPCCF9: M |  |
| GPPCC202 | Is passive discovery supported? | [R4] A.3.5.2.2.3 | GPDT2: O GPDT3: X GPDT4: O GPPCCF9: M |  |
| GPPCC2034 | Is active discovery supported? | [R4] A.3.5.2.2.4 | GPDT2: O GPDT3: X GPDT4: O GPPCCF9: M |  |
| GPPCC204 | Is active re-discovery supported? | [R4] A.3.5.2.2.5 | GPDT2: O GPDT3: X GPDT4: O GPPCCF9: M |  |
| GPPCC205 | Is limiting the number of the transmitted GreenPower cluster messages supported? | [R4] A.3.6.3.1, A.3.6.3.3 | GPDT2: M GPDT3: O GPDT4: O | Yes |
| GPPCC205A | Is distance-based gppTunnelingDelay supported? | [R4] A.3.6.3.1 [R4] A.3.2.8, [R4] A.3.2.9 | GPDT2c¦¦GPDT2f: M GPDT2m¦¦GPDT3cm: O GPPCCF5¦¦GPPCCF8¦¦GPPCCF1 1¦¦GPPCCF13: M GPDT3¦¦GPDT3t+¦¦GPDT3c: X GPDT4: O |  |
| GPPCC205B | Is dropping the scheduled GreenPower cluster message on reception of equivalent message supported? | [R4] A.3.6.3.1 [R4] A.3.2.8, [R4] A.3.2.9 | GPDT2c¦¦GPDT2f: M GPDT2m¦¦GPDT3cm: O GPPCCF5¦¦GPPCCF8¦¦GPPCCF1 1¦¦GPPCCF13: M GPDT3: O GPDT4: O |  |
| GPPCC205C | Is transmission of GreenPower cluster commands with alias supported? | [R4] A.3.6.3.3 [R4] A.3.2.8, [R4] A.3.2.9 | GPDT2: M GPDT3cm: M GPPCCF5¦¦GPPCCF8¦¦GPPCCF1 1¦¦GPPCCF13: M GPDT3t¦¦GPDT3t+¦¦GPDT3c: O GPDT4: O | Yes |
| GPPCC206 | Is updating TargetList field of the ProxyTable attribute on reception of Device_annce supported? | [R4] A.3.5.2.1 | GPDT2c¦¦GPDT2f: M GPDT2m: O GPPCC3A&&(GPPCCF5¦¦GPPC CF6): M GPDT3: N/A GPDT4: O |  |

11.3.4	Support of GP functionality

11.3.4.1	Bidirectional operation

Table 9 –  Support for Green Power bidirectional operation

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPF101 | Is transmission of GPD Read Attributes command supported? | [R4] A.4.2.5 [R4] A.3.6.1.5 | GPPCCF8: M.913 GPPCSF7¦¦GPPCSF8: O |  |
| GPF102 | Is reception of GPD Read Attributes command supported? | [R4] A.4.2.5 [R4] A.3.6.1.5 | GPPCCF8: M.16 GPPCSF7¦¦GPPCSF8: X |  |
| GPF103 | Is transmission of GPD Read Attributes Response supported? | [R4] A.4.2.5 [R4] A.3.6.1.5 | GPPCCF8: M.16 GPPCSF7¦¦GPPCSF8: X |  |
| GPF104 | Is reception of GPD Read Attributes Response command supported? | [R4] A.4.2.5 [R4] A.3.6.1.5 | GPPCCF8: M.16 (GPPCSF7¦¦GPPCSF8)&&GPF1 01: M |  |
| GPF105 | Is transmission of GPD Request Attributes command supported? | [R4] A.4.2.5 [R4] A.3.6.1.5 | GPPCCF8: M.16 GPPCSF7¦¦GPPCSF8: X |  |
| GPF106 | Is reception of GPD Request Attributes command supported? | [R4] A.4.2.5 [R4] A.3.6.1.5 | GPPCCF8: M.16 GPPCSF7¦¦GPPCSF8: M |  |
| GPF107 | Is transmission of GPD Write Attributes command supported? | [R4] A.4.2.5 [R4] A.3.6.1.5 | GPPCCF8: M.16 GPPCSF7¦¦GPPCSF8: O |  |
| GPF108 | Is reception of GPD Write Attributes command supported? | [R4] A.4.2.5 [R4] A.3.6.1.5 | GPPCCF8: M.16 GPPCSF7¦¦GPPCSF8: X |  |

11.3.4.2	Green Power Commissioning Support

Table 10 – GP Commissioning Support

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPCF1 | Does the device support pairing with Data GPDF with Auto-Commissioning bit set to 0b1? | [R4] A.3.9 | GPPCCF11: M GPDT3: O GPDT4: M | Yes |
| GPCF2 | Does the device support pairing with Commissioning GPDF? | [R4] A.3.9 | GPPCCF11: M GPDT3: M GPDT4: M | Yes |
| GPCF3A | Does the device support transmission of GPD Commissioning command? | [R4] A.4.2.1.1 | GPDT2: X GPDT3: X |  |
| GPCF3B | Does the device support reception of GPD Commissioning command? | [R4] A.4.2.1.1 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M GPDT4: M | Yes |
| GPCF4 | Does the device support bidirectional communication in commissioning mode? | [R4] A.3.9 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M GPDT4: M |  |
| GPCF5A | Does the device support transmission of the GPD Channel Request command in commissioning mode? | [R4] A.3.9 | GPDT1: X |  |
| GPCF5B | Does the device support reception of the GPD Channel Request command in commissioning mode? | [R4] A.3.9 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M |  |
| GPCF6 | Does the device support transmission of the GPD Channel Configuration command? | [R4] A.3.9 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M GPDT4: M |  |

13 M.16: Note: the bidirectional operation is transparent to the proxy. It just needs to act add the command received in GP Response to its zgpTxQueue and send it upon reception of GPDF frame with RxAfterTx set; it doesn’t care about the type of the command.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPCF6A | Does the device support transmission of the GPD Channel Configuration command in commissioning mode? | [R4] A.3.9 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M GPDT4: M |  |
| GPCF6B | Does the device support transmission of the GPD Channel Configuration command in operational mode? | [R4] A.3.9 | GPPCCF8¦¦GPPCCF13: M GPPCSF13:M GPDT4: O |  |
| GPCF7 | Does the device support reception of the GPD Channel Configuration command? | [R4] A.3.9 | GPDT1: X |  |
| GPCF8 | Does the device support transmission of the GPD Commissioning Reply command? | [R4] A.4.2.1.2 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M GPDT4: M |  |
| GPCF8A | Does the device support transmission of the GPD Commissioning Reply command in commissioning mode? | [R4] A.4.2.1.2 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M GPDT4: M |  |
| GPCF8B | Does the device support transmission of the GPD Commissioning Reply command in operational mode? | [R4] A.4.2.1.2 | GPPCCF8¦¦GPPCCF13: M GPPCSF13:M GPDT4: O |  |
| GPCF9 | Does the device support reception of the GPD Commissioning Reply command? | [R4] A.4.2.1.2 | GPDT1: X |  |
| GPCF10 | Is GPD removal via GPD Decommissioning command supported? | [R4] A.4.2.1.3 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M GPDT4: M | Yes |
| GPCF11 | Does the device come with pre-configured GPD key? | [R4] A.3.9 | GPDT1: X |  |
| GPCF12A | Does the device support GPD key exchange in GPD Commissioning command? | [R4] A.3.9 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M GPDT4: M |  |
| GPCF12B | Does the device support exchange of encrypted GPD key in GPD Commissioning command? | [R4] A.3.9 | GPPCCF11: O GPPCSF10¦¦GPPCSF11: O GPDT4: O |  |
| GPCF13A | Does the device support GPD key exchange in GPD Commissioning Reply command? | [R4] A.3.9 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M GPDT4: M |  |
| GPCF13B | Does the device support exchange of encrypted GPD key in GPD Commissioning Reply command? | [R4] A.3.9 | GPPCCF11: O GPPCSF10¦¦GPPCSF11: O GPDT4: O |  |
| GPCF14 | Does the device support out-of-band GPD key configuration? | [R4] A.3.9 | GPDT2: O GPDT3: O GPDT4: O |  |
| GPCF15A | Does the device support transmission of GPD Success command in commissioning mode? | [R4] A.3.9 | GPDT1: X |  |
| GPCF15B | Does the device support reception of GPD Success command in commissioning mode? | [R4] A.3.9 | GPPCCF11: M GPPCSF10¦¦GPPCSF11: M GPDT4: M |  |
| GPCF16 | Does the device support in-band configuration of PANId (via GPD Commissioning Reply command)? | [R4] A.3.9 | GPDT1: O |  |
| GPCF100 | Is writing into Sink Table attribute via generic ZCL command supported during commissioning mode? | [R4] A.3.3.2 | GPPCCF12: N/A GPPCSF12: X GPDT4: X |  |
| GPCF101 | Is writing into Sink Table attribute via generic ZCL command supported during operational mode? | [R4] A.3.3.2 | GPPCCF12: N/A GPPCSF12: X GPDT4: X |  |
| GPCF102 | Is writing into Proxy Table attribute via generic ZCL command supported during commissioning mode? | [R4] A.3.4.2 | GPPCCF12: X GPPCSF12: N/A GPDT4: X |  |
| GPCF103 | Is writing into Proxy Table attribute via generic ZCL command supported during operational mode? | [R4] A.3.4.2 | GPPCCF12: X GPPCSF12: N/A GPDT4: X |  |

11.4 GPS application functionality

11.4.1.1	GPS device description support

In Table 11, device descriptions for the GPS (GPDT3, i.e. GPDT3t, GPDT3t+, GPDT3c and

GPDT3cm) are given.

These PICS items are not applicable to the other GP device types (i.e. GPDT0: X, GPDT1: X, GPDT2: X, GPDT4: X).

Table 11 – GPS device description support

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPS1A | Is the product programmed with support for GP Simple generic 1-state switch functionality? | [R4] A.4.3 | GPDT3: O.1714 |  |
| GPS1B | Is the product programmed with support for GP Simple generic 2-state switch functionality? | [R4] A.4.3 | GPDT3: O.17 |  |
| GPS2 | Is the product programmed with (GP-controllable) server- side On/Off cluster? | [R4] A.4.3 | GPDT3: O.17 | Yes |
| GPS3 | Is the product programmed with (GP-controllable) server- side Level Control cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS4 | Is the product programmed with (GP-controllable) client-side Binary Input cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS5 | Is the product programmed with (GP-controllable) server- side Color control cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS6 | Is the product programmed with (GP-controllable) client-side Illuminance Measurement cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS7 | Is the product programmed with (GP-controllable) client-side Occupancy Sensing cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS8 | Is the product programmed with (GP-controllable) server- side Door Lock cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS9 | Is the product programmed with (GP-controllable) client-side Temperature measurement cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS10 | Is the product programmed with (GP-controllable) client-side Pressure Measurement cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS11 | Is the product programmed with (GP-controllable) client-side Flow Measurement cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS12 | Is the product programmed with (GP-controllable) client-side Relative Humidity Measurement cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS13 | Is the product programmed with (GP-controllable) client-side CO2 cluster? | [R4] A.4.3 | GPDT3: O. 17 |  |
| GPS14A | Is the product programmed with support for GP Advanced generic 1-state switch functionality? | [R4] A.4.3 | GPDT3: O.17 |  |
| GPS14B | Is the product programmed with support for GP Advanced generic 2-state switch functionality? | [R4] A.4.3 | GPDT3: O.17 |  |

11.4.2	GPD command support by GPS

Note: all the commands below are transparent to GPP, thus GPDT2: X. For GPDT0: X.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPDRX20 | Is reception of GPD Off command supported? | [R4] A.4.3 | GPS2: O.2015 | Yes |
| GPDRX21 | Is reception of GPD On command supported? | [R4] A.4.3 [R4] A.4.1 | GPS2 && GPDRX21: M | Yes |
| GPDRX22 | Is reception of GPD Toggle command supported? | [R4] A.4.3 [R4] A.4.1 | GPS2: O.20 | Yes |
| GPDRX23 | Is reception of GPD Release command supported? | [R4] A.4.3 [R4] A.4.1 | GPS2: M |  |
| GPDRX30 | Is reception of GPD Move up command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.2116 |  |
| GPDRX31 | Is reception of GPD Move Down command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3 && GPDRX30: M |  |
| GPDRX32 | Is reception of GPD Step UP command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.21 |  |
| GPDRX33 | Is reception of GPD Step Down command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3 && GPDRX32: M |  |
| GPDRX34 | Is reception of GPD Stop command supported? | [R4] A.4.3 [R4] A.4.1 | GPS3 && (GPDRX30 ¦¦ GPDRX35): M |  |
| GPDRX35 | Is reception of GPD Move Up (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.21 | Yes |
| GPDRX36 | Is reception of GPD Move Down (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.21 &&GPDRX35 | Yes |
| GPDRX37 | Is reception of GPD Step Up (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.21 | Yes |
| GPDRX38 | Is reception of GPD Step Down (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.21 &&GPDRX37 | Yes |
| GPDRX40 | Is reception of GPD Move Hue command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.2217 |  |
| GPDRX41 | Is reception of GPD Move Hue Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |
| GPDRX42 | Is reception of GPD Move Hue Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5 && GPDRX41 |  |
| GPDRX43 | Is reception of GPD Step Hue Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |
| GPDRX44 | Is reception of GPD Step Hue Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5 && GPDRX43 |  |
| GPDRX45 | Is reception of GPD Move Saturation command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |
| GPDRX46 | Is reception of GPD Move Saturation Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |
| GPDRX47 | Is reception of GPD Move Saturation Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5 && GPDRX46 |  |
| GPDRX48 | Is reception of GPD Step Saturation Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPDRX20 | Is reception of GPD Off command supported? | [R4] A.4.3 | GPS2: O.2015 | Yes |
| GPDRX21 | Is reception of GPD On command supported? | [R4] A.4.3 [R4] A.4.1 | GPS2 && GPDRX21: M | Yes |
| GPDRX22 | Is reception of GPD Toggle command supported? | [R4] A.4.3 [R4] A.4.1 | GPS2: O.20 | Yes |
| GPDRX23 | Is reception of GPD Release command supported? | [R4] A.4.3 [R4] A.4.1 | GPS2: M |  |
| GPDRX30 | Is reception of GPD Move up command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.2116 |  |
| GPDRX31 | Is reception of GPD Move Down command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3 && GPDRX30: M |  |
| GPDRX32 | Is reception of GPD Step UP command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.21 |  |
| GPDRX33 | Is reception of GPD Step Down command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3 && GPDRX32: M |  |
| GPDRX34 | Is reception of GPD Stop command supported? | [R4] A.4.3 [R4] A.4.1 | GPS3 && (GPDRX30 ¦¦ GPDRX35): M |  |
| GPDRX35 | Is reception of GPD Move Up (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.21 | Yes |
| GPDRX36 | Is reception of GPD Move Down (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.21 &&GPDRX35 | Yes |
| GPDRX37 | Is reception of GPD Step Up (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.21 | Yes |
| GPDRX38 | Is reception of GPD Step Down (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPS3: O.21 &&GPDRX37 | Yes |
| GPDRX40 | Is reception of GPD Move Hue command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.2217 |  |
| GPDRX41 | Is reception of GPD Move Hue Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |
| GPDRX42 | Is reception of GPD Move Hue Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5 && GPDRX41 |  |
| GPDRX43 | Is reception of GPD Step Hue Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |
| GPDRX44 | Is reception of GPD Step Hue Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5 && GPDRX43 |  |
| GPDRX45 | Is reception of GPD Move Saturation command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |
| GPDRX46 | Is reception of GPD Move Saturation Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |
| GPDRX47 | Is reception of GPD Move Saturation Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5 && GPDRX46 |  |
| GPDRX48 | Is reception of GPD Step Saturation Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |

Table 12 – GPD commands support - reception

[R4] A.4.1

15 O.20: DUT shall implement exactly one of those options.

16 O.21: DUT shall implement at least one of those options.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPDRX49 | Is reception of GPD Step Saturation Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5 && GPDRX48 |  |
| GPDRX4a | Is reception of GPD Move Color command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |
| GPDRX4b | Is reception of GPD Step Color command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPS5: O.22 |  |
| GPDRX50 | Is reception of GPD Lock Door command supported? | [R4] A.4.3 [R4] A.4.1 | GPS8: M |  |
| GPDRX51 | Is reception of GPD Unlock Door command supported? | [R4] A.4.3 [R4] A.4.1 | GPS8: M |  |
| GPDRX60 | Is reception of GPD Press 1 of 1 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPS1A: M GPS14A: M |  |
| GPDRX61 | Is reception of GPD Release 1 of 1 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPS1A: M GPS14A: M |  |
| GPDRX62 | Is reception of GPD Press 1 of 2 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPS1B: M GPS14B: M |  |
| GPDRX63 | Is reception of GPD Release 1 of 2 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPS1B: M GPS14B: M |  |
| GPDRX64 | Is reception of GPD Press 2 of 2 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPS1B: M GPS14B: M |  |
| GPDRX65 | Is reception of GPD Release 2 of 2 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPS1B: M GPS14B: M |  |
| GPDRX66 | Is reception of GPD Short press 1 of 1 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPS14A: M |  |
| GPDRX67 | Is reception of GPD Short press 1 of 2 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPS14B: M |  |
| GPDRX68 | Is reception of GPD Short press 2 of 2 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPS14B: M |  |
| GPDRXA0 | Is reception of GPD Attribute reporting command supported? | [R4] A.4.3 [R4] A.4.2.3 | GPS4, GPS6, GPS7, GPS12, GPS13, GPS14, GPS15 GPS16, GPS17, GPS18, GPS19, GPS20: M |  |

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPDRXA1 | Is reception of GPD Manufacturer-specific attribute reporting command supported? | [R4] A.4.3 [R4] A.4.2.3 | GPS4, GPS6, GPS7, GPS12, GPS13 GPS14, GPS15 GPS16, GPS17, GPS18, GPS19, GPS20: O |  |
| GPDRXA2 | Is reception of GPD Multi-cluster reporting command supported? | [R4] A.4.3 [R4] A.4.2.3 | GPS4, GPS6, GPS7, GPS12, GPS13, GPS14, GPS15 GPS16, GPS17, GPS18, GPS19, GPS20: O |  |
| GPDRXA3 | Is reception of GPD manufacturer-specific multi-cluster reporting command supported? | [R4] A.4.3 [R4] A.4.2.3 | GPS4, GPS6, GPS7, GPS12, GPS13, GPS14, GPS15 GPS16, GPS17, GPS18, GPS19, GPS20: O |  |

12 Green Power Device functionality

The    PICS    items    in    section    12    are    only    applicable    to    the    GPD    (GPDT0). They are not applicable to the other GP device types (i.e. GPDT1: X, GPDT2: X, GPDT3: X, GPDT4: X).

12.1 GPD device description support

In Table 13, device descriptions for the GPD (GPDT0) are given.

Table 13 – GPD device description support

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPD0 | Is the product programmed as a GP Simple Generic 1-state Switch? | [R4] A.4.3 | GPDT1: O.2318 |  |
| GPD1 | Is the product programmed as a GP Simple Generic 2-state Switch? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD2 | Is the product programmed as a GP On/Off Switch? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD3 | Is the product programmed as a GP Level Control Switch? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD4 | Is the product programmed as a GP Simple Sensor? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD5 | Is the product programmed as a GP Advanced Generic 1-state Switch? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD5B | What is the value of the short press time threshold? | [R4] A.4.2.2 | Implementation-specific |  |
| GPD6 | Is the product programmed as a GP Advanced Generic 2-state Switch? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD6B | What is the value of the short press time threshold? | [R4] A.4.2.2 | Implementation-specific |  |
| GPD10 | Is the product programmed as a GP Color Dimmer Switch? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD11 | Is the product programmed as a GP Light Sensor? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD12 | Is the product programmed as a GP Occupancy Sensor? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD20 | Is the product programmed as a GP Door Lock Controller? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD30 | Is the product programmed as a GP Temperature Sensor? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD31 | Is the product programmed as a GP Pressure Sensor? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD32 | Is the product programmed as a GP Flow Sensor? | [R4] A.4.3 | GPDT1: O.23 |  |
| GPD33 | Is the product programmed as a GP Indoor Environment Sensor? | [R4] A.4.3 | GPDT1: O.23 |  |

12.2 GPD functionality

Table 14 –GPD functionality

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPSF1 | Does the device implement cGP stub? | [R4] A.1 | GPDT0: X |  |
| GPSF2 | Does the device implement dGP stub? | [R4] A.1 | GPDT0: X |  |
| GPPC1 | Does the device support Green Power End Point (GPEP)? | [R4] A.3.1 | GPDT0: X |  |

18 O.23: DUT shall implement exactly one of those options.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPF4A | Does the device support transmitting GPDF frame format with ApplicationID sub-field of the Extended NWK Frame Control field set to 0b000? | [R4] A.1.4.1.3 | GPDT0: O.2219 |  |
| GPF4B | Does the device support transmitting GPDF frame format with ApplicationID sub-field of the Extended NWK Frame Control field set to 0b010? | [R4] A.1.4.1.3 | GPDT0: O.22 |  |
| GPF5 | Does the device support SecurityLevel=0b11? | [R4] A.1.5.4 [R4] A.3.7.2.1 | GPDT0: O.2420 |  |
| GPF6 | Does the device support SecurityLevel=0b10? | [R4] A.1.5.4 [R4] A.3.7.2.1 | GPDT0: O.24 |  |
| GPF7 | Does the device support SecurityLevel=0b01? | [R4] A.1.5.4 [R4] A.3.7.2.1 | GPDT0: O.24 |  |
| GPF8 | Does the device support SecurityLevel=0b00? | [R4] A.1.5.4 [R4] A.3.7.2.1 | GPDT0: O.24 |  |
| GPF9A | Does the device support receiving GPDF frame format with ApplicationID sub-field of the Extended NWK Frame Control field set to 0b000? | [R4] A.1.4.1.3 | GPDT0&&GPF4A: O (GPF4B: X) |  |
| GPF9B | Does the device support receiving GPDF frame format with ApplicationID sub-field of the Extended NWK Frame Control field set to 0b010? | [R4] A.1.4.1.3 | GPDT0&&GPF4B: O (GPF4A: X) |  |
| GPDF1 | Does the device support random MAC sequence number for GPD commands? | [R4] A.1.6, A.1.7 | GPDT0 && GPF8: O.2521 |  |
| GPDF2 | Does the device support incremental MAC sequence number for GPD commands? | [R4] A.1.6, A.1.7 | GPDT0 && GPF8: O.25 |  |
| GPDF3 | Is the FixedLocation flag in the Commissioning GPD command set? | [R4] A.1.6, A.1.7 | GPDT0: O |  |

12.2.1	GPD Bidirectional operation

Table 15 –  Support for GreenPower functionality

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPF100 | Does the device support bidirectional communication in operational mode? | [R4] A.1.6.3 [R4] A.3.6.1.5 | GPDT0: O |  |
| GPF101 | Is transmission of GPD Read Attributes command supported? | [R4] A.4.2.5 | GPDT0: X |  |
| GPF102 | Is reception of GPD Read Attributes command supported? | [R4] A.4.2.5 | GPDT0&&GPF100: M |  |
| GPF103 | Is transmission of GPD Read Attributes Response supported? | [R4] A.4.2.5 | GPDT0&&GPF100: M |  |
| GPF104 | Is reception of GPD Read Attributes Response command supported? | [R4] A.4.2.5 | GPDT0: X |  |
| GPF105 | Is transmission of GPD Request Attributes command supported? | [R4] A.4.2.5 | GPDT0&&GPF100: O |  |
| GPF106 | Is reception of GPD Request Attributes command supported? | [R4] A.4.2.5 | GPDT0: X |  |
| GPF107 | Is transmission of GPD Write Attributes command supported? | [R4] A.4.2.5 | GPDT0: X |  |
| GPF108 | Is reception of GPD Write Attributes command supported? | [R4] A.4.2.5 | GPDT0&&GPF100: O |  |

19 O.22: Device under test shall implement only one of those options

20 O.24: Device under test shall implement at least one of those options.

21 O.25: Device under test shall implement only one of those options.

12.2.2	GPD commissioning support

Table 16 – GP Commissioning Feature Support

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPCF1 | Does the device support pairing with Data GPDF with Auto-Commissioning bit set to 0b1? | [R4] A.3.9 [R4] A.1.4, A.1.6 | GPDT0: O.2622 |  |
| GPCF2 | Does the device support pairing with Commissioning GPDF? | [R4] A.3.9 [R4] A.4.2.1.1 | GPDT0: O.26 GPDT0 && (GPD4¦¦ GPD11¦¦ GPD12¦¦ GPD30¦¦ GPD31¦¦ GPD32¦¦ GPD33): M |  |
| GPCF3A | Does the device support transmission of GPD Commissioning command? | [R4] A.4.2.1.1 | GPDT0&&GPCF2: M |  |
| GPCF3B | Does the device support reception of GPD Commissioning command? | [R4] A.4.2.1.1 | GPDT0: X |  |
| GPCF4 | Does the device support bidirectional communication in commissioning mode? | [R4] A.3.9 | GPDT0: O |  |
| GPDF10 | Does the device support configuration of operational channel when in commissioning mode? | [R4] A.3.9 | GPDT0: O |  |
| GPDF10A | Does the device support out-of-band configuration of operational channel? | [R4] A.3.9 | GPDT0: O.2723 (GPDT0 &&GPCF4: X) |  |
| GPDF10B | Does the device support configuration of operational channel via channel toggling (GPD Commissioning command with RxAfterTx = 0b0)? | [R4] A.3.9 | GPDT0: O.27 (GPDT0 &&GPCF4: X) |  |
| GPDF10C | Does the device support in-band configuration of operational channel (via GPD Channel Request/Channel Configuration command)? | [R4] A.3.9 | GPDT0: O.27 (GPDT0 &&GPCF4: M) |  |
| GPDF10D | Does the device support the recommended channel set (11, 15, 20, 25)? | [R4] A.1.6, A.1.7 | GPDT0&&GPCF16: M |  |
| GPCF5A | Does the device support transmission of the GPD Channel Request command in commissioning mode? | [R4] A.3.9 [R4] A.4.2.1.4 [R4] A.1.4 | GPDT0: O GPDT0 &&(GPCF4¦¦GPDF10C): M |  |
| GPCF5B | Does the device support reception of the GPD Channel Request command in commissioning mode? | [R4] A.3.9 [R4] A.4.2.1.4 [R4] A.1.4 | GPDT0: X |  |
| GPCF6 | Does the device support transmission of the GPD Channel Configuration command? | [R4] A.3.9 [R4] A.4.2.1.5 [R4] A.1.4 | GPDT0: X |  |
| GPCF7 | Does the device support reception of the GPD Channel Configuration command? | [R4] A.3.9 [R4] A.4.2.1.5 [R4] A.1.4 | GPDT0: O |  |
| GPCF7A | Does the device support reception of the GPD Channel Configuration command in commissioning mode? | [R4] A.3.9 [R4] A.4.2.1.5 [R4] A.1.4 | GPDT0: O GPDT0 &&(GPCF4¦¦GPDF10C): M |  |
| GPCF7B | Does the device support reception of the GPD Channel Configuration command in operational mode? | [R4] A.6 [R4] A.4.2.1.5 [R4] A.1.4 | GPDT0: O GPDT0 &&GPF9: O |  |
| GPCF8 | Does the device support transmission of the GPD Commissioning Reply command? | [R4] A.4.2.1.2 | GPDT0: X |  |

22 O.26: DUT should implement exactly one of those methods. Hull test event comment #81 (ZigBee document docs-

11-5603)

23 O.27: device under test shall support at least one of the methods.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPCF9 | Does the device support reception of the GPD Commissioning Reply command? | [R4] A.4.2.1.2 | GPDT0 && GPCF2: O |  |
| GPCF9A | Does the device support reception of the GPD Commissioning Reply command in commissioning mode? | [R4] A.4.2.1.2 | GPDT0 && GPCF4: M |  |
| GPCF9B | Does the device support reception of the GPD Commissioning Reply command in operational mode? | [R4] A.6 | GPDT0 && GPF9: O |  |
| GPCF10 | Is GPD removal via GPD Decommissioning command supported? | [R4] A.4.2.1.3 | GPDT0: O |  |
| GPCF11 | Does the device come with pre-configured GPD key? | [R4] A.3.9 | GPDT0 && (GPF5¦¦GPF6¦¦GPF7): O.2824 |  |
| GPCF12A | Does the device support GPD key exchange in GPD Commissioning command? | [R4] A.3.9 | GPDT0 && GPCF2: O GPDT0 && GPCF11: M |  |
| GPCF12B | Does the device support exchange of encrypted GPD key in GPD Commissioning command? | [R4] A.3.9 [R4] A.1.5 | GPDT0 && GPCF11: O |  |
| GPCF13A | Does the device support GPD key exchange in GPD Commissioning Reply command? | [R4] A.3.9 | GPDT0 && (GPF5¦¦GPF6¦¦GPF7): O.28 GPDT0 && GPCF9: O |  |
| GPCF13B | Does the device support exchange of encrypted GPD key in GPD Commissioning Reply command? | [R4] A.3.9 [R4] A.1.5 | GPDT0 && GPCF13A: O |  |
| GPCF14 | Does the device support out-of-band GPD key configuration? | [R4] A.3.9 | GPDT0 && (GPF5¦¦GPF6¦¦GPF7): O.28 |  |
| GPCF15A | Does the device support transmission of GPD Success command in commissioning mode? | [R4] A.3.9 [R4] A.4.1 | GPDT0: O GPDT0 && GPCF4: M |  |
| GPCF15B | Does the device support reception of GPD Success command when in commissioning mode? | [R4] A.3.9 [R4] A.4.1 | GPDT0: X |  |
| GPCF16 | Does the device support in-band configuration of PANId (via GPD Commissioning Reply command)? | [R4] A.3.9 [R4] A.4.2.1.2 | GPDT0 && GPCF4: O |  |
| GPCF100 | Is writing into Sink Table attribute via generic ZCL command supported during commissioning mode? | [R4] A.3.3.2.2 | GPDT0: X |  |
| GPCF101 | Is writing into Sink Table attribute via generic ZCL command supported during operational mode? | [R4] A.3.3.2.2 | GPDT0: X |  |
| GPCF102 | Is writing into Proxy Table attribute via generic ZCL command supported during commissioning mode? | [R4] A.3.3.2.2 | GPDT0: X |  |
| GPCF103 | Is writing into Proxy Table attribute via generic ZCL command supported during operational mode? | [R4] A.3.3.2.2 | GPDT0: X |  |

24 O.28: DUT shall support at least one of those options.

12.3 GPD application functionality

12.3.1	GPD command support by GPD

Table 17 – GPD commands support - transmission

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPDTX20 | Is transmission of GPD Off command supported? | [R4] A.4.3 [R4] A.4.1 | GPD2: O.2925 |  |
| GPDTX21 | Is transmission of GPD On command supported? | [R4] A.4.3 [R4] A.4.1 | GPD2 && GPDTX20: M |  |
| GPDTX22 | Is transmission of GPD Toggle command supported? | [R4] A.4.3 [R4] A.4.1 | GPD2: O.29 |  |
| GPDTX23 | Is transmission of GPD Release command supported? | [R4] A.4.3 [R4] A.4.1 | GPD2: O |  |
| GPDTX30 | Is transmission of GPD Move Up command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPD3: O.3026 |  |
| GPDTX31 | Is transmission of GPD Move Down command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPD3 && GPDTX30: M |  |
| GPDTX32 | Is transmission of GPD Step Up command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPD3: O.30 |  |
| GPDTX33 | Is transmission of GPD Step Down command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPD3 && GPDTX32: M |  |
| GPDTX34 | Is transmission of GPD Stop command supported? | [R4] A.4.3 [R4] A.4.1 | GPD3 && (GPDTX30 ¦¦ GPDTX35): M |  |
| GPDTX35 | Is transmission of GPD Move Up (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPD3: O.30 |  |
| GPDTX36 | Is transmission of GPD Move Down (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPD3&&GPDTX35: M |  |
| GPDTX37 | Is transmission of GPD Step Up (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPD3: O.30 |  |
| GPDTX38 | Is transmission of GPD Step Down (with On/Off) command supported? | [R4] A.4.3 [R4] A.4.2.4 | GPD3&&GPDTX37: M |  |
| GPDTX40 | Is transmission of GPD Move Hue command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10: O.3127 |  |
| GPDTX41 | Is transmission of GPD Move Hue Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10: O.31 |  |
| GPDTX42 | Is transmission of GPD Move Hue Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10 && GPDTX41: M |  |
| GPDTX43 | Is transmission of GPD Step Hue Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10: O.31 |  |
| GPDTX44 | Is transmission of GPD Step Hue Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10 && GPDTX43: M |  |
| GPDTX45 | Is transmission of GPD Move Saturation command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10: O.31 |  |
| GPDTX46 | Is transmission of GPD Move Saturation Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10: O.31 |  |
| GPDTX47 | Is transmission of GPD Move Saturation Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10 && GPDTX46: M |  |
| GPDTX48 | Is transmission of GPD Step Saturation Up command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10: O.31 |  |

25 O.29: Device under test shall support only one of those options.

26 O.30: Device under test has to implement exactly one of those commands

27 O.31: Device under test has to implement exactly one of those commands

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPDTX49 | Is transmission of GPD Step Saturation Down command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10 && GPDTX48: M |  |
| GPDTX4a | Is transmission of GPD Move Color command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10: O.31 |  |
| GPDTX4b | Is transmission of GPD Step Color command supported? | [R4] A.4.3 [R4] A.4.2.5 | GPD10: O.31 |  |
| GPDTX50 | Is transmission of GPD Lock Door command supported? | [R4] A.4.3 [R4] A.4.1 | GPD20: M |  |
| GPDTX51 | Is transmission of GPD Unlock Door command supported? | [R4] A.4.3 [R4] A.4.1 | GPD20: M |  |
| GPDTX60 | Is transmission of GPD Press 1 of 1 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPD0: M GPD5: M |  |
| GPDTX61 | Is transmission of GPD Release 1 of 1 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPD0: M GPD5: M |  |
| GPDTX62 | Is transmission of GPD Press 1 of 2 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPD1: M GPD6: M |  |
| GPDTX63 | Is transmission of GPD Release 1 of 2 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPD1: M GPD6: M |  |
| GPDTX64 | Is transmission of GPD Press 2 of 2 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPD1: M GPD6: M |  |
| GPDTX65 | Is transmission of GPD Release 2 of 2 command supported? | [R4] A.4.3 [R4] A.4.1 [R4] A.4.2.2 | GPD1: M GPD6: M |  |
| GPDTX66 | Is transmission of GPD Short press 1 of 1 command supported? | [R4] Table 43 | GPD5: M |  |
| GPDTX67 | Is transmission of GPD Short press 1 of 2 command supported? | [R4] Table 43 | GPD6: M |  |
| GPDTX68 | Is transmission of GPD Short press 2 of 2 command supported? | [R4] Table 43 | GPD6: M |  |
| GPDTXA0 | Is transmission of GPD Attribute reporting command supported? | [R4] A.4.3 [R4] A.4.2.3 | GPD4, GPD11, GPD12, GPD30, GPD31, GPD32 GPD33: O.3228 |  |
| GPDTXA1 | Is transmission of GPD Manufacturer-specific attribute reporting command supported? | [R4] A.4.3 [R4] A.4.2.3 | GPD4, GPD11, GPD12, GPD30, GPD31, GPD32 GPD33: O.32 |  |
| GPDTXA2 | Is transmission of GPD Multi-cluster reporting command supported? | [R4] A.4.3 [R4] A.4.2.3 | GPD11, GPD12, GPD30, GPD31, GPD32 GPD33: O.32 |  |

28 O.32: Device under test shall implement at least one of those commands.

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| GPDTXA3 | Is transmission of GPD manufacturer-specific multi-cluster reporting command supported? | [R4] A.4.3 [R4] A.4.2.3 | GPD11, GPD12, GPD30, GPD31, GPD32 GPD33: O.32 |  |

Note: all the commands below are transparent to GPP, thus GPDT2: X. For GPDT1: X.

12.3.2	ZigBee attribute support by GPD sensor devices

In Table 18 – Table 20, ZigBee attributes supported by the GPD devices are listed. These PICS items are not applicable to the other GP device types.

Table 18 – Reported ZigBee attributes per GPD device

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| AREP1 | Does the GPD support reporting of the 0x0055: PresentValue attribute from Binary Input Cluster? | [R4] A.4.3 | GPD4: M |  |
| AREP2 | Does the GPD support reporting of the 0x0000: MeasuredValue attribute from Illuminance Measurement Cluster? | [R4] A.4.3 | GPD11: M GPD33: M |  |
| AREP3 | Does the GPD support reporting of the 0x0000: Occupancy attribute from Occupancy Sensing Cluster? | [R4] A.4.3 | GPD12: M |  |
| AREP4 | Does the GPD support reporting of the 0x0000: MeasuredValue attribute from Temperature Measurement Cluster? | [R4] A.4.3 | GPD30: M GPD33: M |  |
| AREP5 | Does the GPD support reporting of the 0x0000: MeasuredValue attribute from Pressure Measurement Cluster? | [R4] A.4.3 | GPD31: M |  |
| AREP6 | Does the GPD support reporting of the 0x0000: MeasuredValue attribute from Flow Measurement Cluster? | [R4] A.4.3 | GPD32: M |  |
| AREP7 | Does the GPD support reporting of the 0x0000: MeasuredValue attribute from Relative Humidity Measurement Cluster? | [R4] A.4.3 | GPD33: M |  |

Table 19 – Readable ZigBee attributes per GPD device

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| AREAD1 | Does the GPD support reading of the 0x0051: OutOfService attribute from Binary Input Cluster? | [R4] A.4.3 | GPD4 && GPF102: M |  |
| AREAD2 | Does the GPD support reading of the 0x0055: PresentValue attribute from Binary Input Cluster? | [R4] A.4.3 | GPD4 && GPF102: M |  |
| AREAD3 | Does the GPD support reading of the 0x006F: StatusFlags attribute from Binary Input Cluster? | [R4] A.4.3 | GPD4 && GPF102: M |  |
| AREAD4 | Does the GPD support reading of the 0x0000: MeasuredValue attribute from Illuminance Measurement Cluster? | [R4] A.4.3 | GPD11 && GPF102: M GPD33 && GPF102: M |  |
| AREAD5 | Does the GPD support reading of the 0x0001: MinMeasuredValue attribute from Illuminance Measurement Cluster? | [R4] A.4.3 | GPD11 && GPF102: M GPD33 && GPF102: M |  |

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| AREAD6 | Does the GPD support reading of the 0x0002: MaxMeasuredValue attribute from Illuminance Measurement Cluster? | [R4] A.4.3 | GPD11 && GPF102: M GPD33 && GPF102: M |  |
| AREAD7 | Does the GPD support reading of the 0x0000: Occupancy attribute from Occupancy Sensing Cluster? | [R4] A.4.3 | GPD12 && GPF102: M |  |
| AREAD8 | Does the GPD support reading of the 0x0000: Occupancy Sensor Type attribute from Occupancy Sensing Cluster? | [R4] A.4.3 | GPD12 && GPF102: M |  |
| AREAD9 | Does the GPD support reading of the 0x0000: MeasuredValue attribute from Temperature Measurement Cluster? | [R4] A.4.3 | GPD30 && GPF102: M GPD33 && GPF102: M |  |
| AREAD10 | Does the GPD support reading of the 0x0001: MinMeasuredValue attribute from Temperature Measurement Cluster? | [R4] A.4.3 | GPD30 && GPF102: M GPD33 && GPF102: M |  |
| AREAD11 | Does the GPD support reading of the 0x0002: MaxMeasuredValue attribute from Temperature Measurement Cluster? | [R4] A.4.3 | GPD30 && GPF102: M GPD33 && GPF102: M |  |
| AREAD12 | Does the GPD support reading of the 0x0000: MeasuredValue attribute from Pressure Measurement Cluster? | [R4] A.4.3 | GPD31 && GPF102: M |  |
| AREAD13 | Does the GPD support reading of the 0x0000: MeasuredValue attribute from Flow Measurement Cluster? | [R4] A.4.3 | GPD32 && GPF102: M GPD33 && GPF102: M |  |
| AREAD14 | Does the GPD support reading of the 0x0001: MinMeasuredValue attribute from Flow Measurement Cluster? | [R4] A.4.3 | GPD32 && GPF102: M GPD33 && GPF102: M |  |
| AREAD15 | Does the GPD support reading of the 0x0002: MaxMeasuredValue attribute from Flow Measurement Cluster? | [R4] A.4.3 | GPD32 && GPF102: M GPD33 && GPF102: M |  |
| AREAD16 | Does the GPD support reading of the 0x0000: MeasuredValue attribute from Relative Humidity Cluster? | [R4] A.4.3 | GPD33 && GPF102: M |  |
| AREAD17 | Does the GPD support reading of the 0x0001: MinMeasuredValue attribute from Relative Humidity Cluster? | [R4] A.4.3 | GPD33 && GPF102: M |  |
| AREAD18 | Does the GPD support reading of the 0x0002: MaxMeasuredValue attribute from Relative Humidity Cluster? | [R4] A.4.3 | GPD33 && GPF102: M |  |

Table 20 – Writable ZigBee attributes per GPD device

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| AWRITE1 | Does the GPD support writing of the 0x0051: OutOfService attribute from Binary Input Cluster? | [R4] A.4.3 | GPD4 && GPF100: M |  |