| Project | ZigBee Alliance |
| --- | --- |
| Title | (Alternate) ZigBee Home Automation Profile: Protocol Implementation Conformance (PICS) Proforma (Alternate) |
| Date Submitted | [24 October 2011] |
| Source | [Jared Lemke] [Vantage/Legrand] [1061 S 800 E, Orem, UT 84062] | Voice: [+1 801 226 4594] Fax: [] E-mail:[jaredl@vantagecontrols.com] |
| Re: | ZigBee PICS for the ZigBee Home Automation Profile |
| Abstract | As a part of formal conformance testing, manufacturers will be asked to submit a statement of protocol conformance with respect to the appropriate ZigBee devices required by the application profile under test. This document is intended to provide the form of that statement of conformance for the Home Automation profile. |
| Purpose | This document, after review by the relevant working groups, should provide a form whereby developers can proffer a statement of protocol conformance to be tested under profile testing. |
| Notice | This document has been prepared to assist the ZigBee Alliance. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution will be posted in the member area of the ZigBee web site. |

| Legal Notice | Copyright © ZigBee Alliance, Inc. (2006). All rights Reserved. This information within this document is the property of the ZigBee Alliance and its use and disclosure are restricted. Elements of ZigBee Alliance specifications may be subject to third party intellectual property rights, including without limitation, patent, copyright or trademark rights (such a third party may or may not be a member of ZigBee). ZigBee is not responsible and shall not be held responsible in any manner for identifying or failing to identify any or all such third party intellectual property rights. This document and the information contained herein are provided on an “AS IS” basis and ZigBee DISCLAIMS ALL WARRANTIES EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO (A) ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OF THIRD PARTIES (INCLUDING WITHOUT LIMITATION ANY INTELLECTUAL PROPERTY RIGHTS INCLUDING PATENT, COPYRIGHT OR TRADEMARK RIGHTS) OR (B) ANY IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, TITLE OR NON-INFRINGEMENT. IN NO EVENT WILL ZIGBEE BE LIABLE FOR ANY LOSS OF PROFITS, LOSS OF BUSINESS, LOSS OF USE OF DATA, INTERRUPTION OF BUSINESS, OR FOR ANY OTHER DIRECT, INDIRECT, SPECIAL OR EXEMPLARY, INCIDENTIAL, PUNITIVE OR CONSEQUENTIAL DAMAGES OF ANY KIND, IN CONTRACT OR IN TORT, IN CONNECTION WITH THIS DOCUMENT OR THE INFORMATION CONTAINED HEREIN, EVEN IF ADVISED OF THE POSSIBILITY OF SUCH LOSS OR DAMAGE. All Company, brand and product names may be trademarks that are the sole property of their respective owners. The above notice and this paragraph must be included on all copies of this document that are made. ZigBee Alliance, Inc. 2694 Bishop Drive, Suite 275 San Ramon, CA 94583 |
| --- | --- |

# References

The following standards contain provisions, which, through reference in this document, constitute provisions of this standard. All the standards listed are normative references. At the time of publication, the editions indicated were valid. All standards are subject to revision, and parties to agreements based on this standard are encouraged to investigate the possibility of applying the most recent editions of the standards indicated below.

## ZigBee Alliance documents

Document 053474r17: ZigBee Specification,

ZigBee document 064321r08, ZigBee Stack Profile

Document 053520r26:  ZigBee Home Automation Application Profile Specification

ZigBee document 075123r01, ZigBee Cluster Library

Deleted

Deleted

Deleted

Deleted

Deleted

Deleted

ZigBee document 04300r08:  ZigBee Network Layer PICS

ZigBee document 064147r07:  ZigBee Application Layer PICS

ZigBee document 043171r04:  ZigBee Security Layer PICS

ZigBee document 064113r08: ZigBee Cluster Library PICS

## IEEE documents

IEEE Standard for Part 15.4: Wireless Medium Access Control (MAC) and Physical Layer (PHY) specifications for Low Rate Wireless Personal Area Networks (LR-WPANs), 2003.

## ISO documents

ISO/IEC 9646-1:1991, Information technology - Open Systems Interconnection - Conformance testing methodology and framework - Part 1: General concepts.

ISO/IEC 9646-7:1995, Information technology - Open Systems Interconnection - Conformance testing methodology and framework - Part 7. Implementation conformance statements.

# Change history

The following table shows the change history for this specification.

Revision 0 (October, 2006)

Table 1 – Revision change history for revision 0

| Revision | Version | Description |
| --- | --- | --- |
| R00 | - | Initial draft (Converted from the HCL PICS written by Don Sturek) |
| R05 | 0 |  |
| R06 | 0 | Changed to alternate version that references the ZCL PICS and places HA-specific restrictions on them. |
| R07 | 0 | Updated to reflect changes to HA specification and for recertification event. Updated reference documents, devices etc. Revalidated optional and mandatory on devices, update on optional and mandatory on groups, scenes and binding since they are now by device type and not profile wide. |
| R08 | 0 | Revalidated optional and mandatory on devices, update on optional and mandatory on groups, scenes and binding since they are now by device type and not profile wide. |

# Introduction

To evaluate conformance of a particular implementation, it is necessary to have a statement of which capabilities and options have been implemented for a given standard. Such a statement is called a protocol implementation conformance statement (PICS).

## Scope

This document provides the protocol implementation conformance statement (PICS) proforma for the ZigBee specifications cited in Reference [R3] in compliance with the relevant requirements, and in accordance with the relevant guidance, given in ISO/IEC 9646-7.

This document addresses the ZigBee Home Automation Application Profile.

## Purpose

The supplier of a protocol implementation claiming to conform to the ZigBee Home Automation Application Profile shall complete the following PICS proforma and accompany it with the information necessary to identify fully both the supplier and the implementation.

The PICS is in the form of answers to a set of questions in the PICS proforma. The questions in a proforma consist of a systematic list of protocol capabilities and options as well as their implementation requirements. The implementation requirement indicates whether implementation of a capability is mandatory, optional, or conditional depending on options selected. When a protocol implementer answers questions in a PICS proforma, they would indicate whether an item is implemented or not, and provide explanations if an item is not implemented.

# Abbreviations and special symbols

Notations for requirement status:

| M | Mandatory |
| --- | --- |
| O | Optional |
| O.n | Optional, but support of at least one of the group of options labeled O.n is required. |
| N/A | Not applicable |
| X | Prohibited |
| Item Number:Status | Status is conditional on support of item number |

“Item Number”: Conditional, status dependent upon the support marked for the “Item Number”.

For example, FD1: O.1 indicates that the status is optional but at least one of the features described in FD1 is required to be implemented, if this implementation is to follow the standard of which this PICS Proforma is a part.

# Instructions for completing the PICS proforma

If a given implementation is claimed to conform to this standard, the actual PICS proforma to be filled in by a supplier shall be technically equivalent to the text of the PICS proforma in this annex, and shall preserve the numbering and naming and the ordering of the PICS proforma.

A PICS which conforms to this document shall be a conforming PICS proforma completed in accordance with the instructions for completion given in this annex.

The main part of the PICS is a fixed-format questionnaire, divided into five tables. Answers to the questionnaire are to be provided in the rightmost column, either by simply marking an answer to indicate a restricted choice (such as Yes or No), or by entering a value, set, or range of values.

# Identification of the implementation

Implementation under test (IUT) identification

IUT name: ULTI ZB G Plug Adapter Dimmer

_____________________________________________________________________

IUT version: 1.1.0

____________________________________________________________________

______________________________________________________________________________

System under test (SUT) identification

SUT name: Texas Instruments CC2530

______________________________________________________________________________

Software Version: 2.3.0

______________________________________________________________________________

Hardware Version: 1

______________________________________________________________________________

Operating system (optional): ________________________________________________________________

Product supplier

Name: Schneider  Electric ______________________________________________________________________

Address: 4th Floor , Tower 1, Kerry Plaza, No.1 Zhongxin Si Road, Futian District , Shenzhen China______________________________________________________________________

_____________________________________________________________________________

Telephone number: (+86) 755 82753666

_____________________________________________________________

Facsimile number: ______________________________________________________________

Email address: ________________________________________________________________

Additional information: __________________________________________________________

Client

Name: ________________________________________________________________________

Address: ______________________________________________________________________

_____________________________________________________________________________

Telephone number: _____________________________________________________________

Facsimile number: ______________________________________________________________

Email address: ________________________________________________________________

Additional information: __________________________________________________________

PICS contact person

Name: Emily Wang ________________________________________________________________________

Address: 4th Floor , Tower 1, Kerry Plaza, No.1 Zhongxin Si Road, Futian District , Shenzhen China ______________________________________________________________________

_____________________________________________________________________________

Telephone number: (+86) 755 82753666 ext:3754 ______________________________________________________________

Facsimile number: _______________________________________________________________

Email address: bo-emily.wang@schneider-electric.com _________________________________________________________________

Additional information: ___________________________________________________________

PICS/System conformance statement

# Identification of the protocol

This PICS proforma applies to ZigBee Home Automation Application Profile, cited in Reference [R3].

# Global statement of conformance

The implementation described in this PICS proforma meets all of the mandatory requirements of the referenced standards:

Application Profile:  ZigBee Home Automation – 053520r26

Note -- Answering ‘No’ indicates non-conformance to the specified protocol standard. Non-supported mandatory capabilities are to be identified in the following tables, with an explanation by the implementer explaining why the implementation is non-conforming.

The supplier will have fully complied with the requirements for a statement of conformance by completing the statement contained in this subclause. That means, by clicking the above, the statement of conformance is complete.

# PICS proforma tables

The following tables are composed of the detailed questions to be answered, which make up the PICS proforma.

## ZigBee Device Types

Table 2 - Functional device types

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| FDT1 | Is this device capable of acting as a ZigBee coordinator? | [R1]/2.5.5.5.1 | O.1 | Yes |
| FDT2 | Is this device capable of acting as a ZigBee router? | [R1]/2.5.5.5.2 | O.1 | Yes |
| FDT3 | Is this a ZigBee end device? | [R1]/2.5.5.5.3 | O.1 | No |

## ZigBee Stack Profile

Table 3 – ZigBee stack profile

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| ZSP1 | Is the device built on a ZigBee Compliant Platform certified for ZigBee or ZigBee PRO stack profile [R2]/8.3? | [R11]/8 [R2]/8.3 | M | Yes |
| ZSP2 | Does the device implement source binding with a binding table whose number of available entries is greater than or equal to the number of mandatory clusters supported by the device descriptions implemented? | [R3]/5.2 | O By device type | Yes |
| ZSP3 | Does the device adhere to the polling rate specifications given in [R3]/5.1? | [R3]/5.2 | FDT3:M | N/A |
| ZSP4 | Does the device support Trust Center Link Keys including the Default TRUST Center Link Key? | [R3]/5.2 | M | Yes |

## ZigBee Home Automation general requirements support

Table 4 – HA general requirements support

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| HAG1 | Does the device support the ZigBee Cluster Library PICS as defined in [R14]? | [R14]/8 | M | Yes |
| HAG2 | Does the device support at least 16 entries in the group table? | [R3]/6 | O By device type | Yes |
| HAG3 | Does the device support the Scenes cluster as a server? |  | O | Yes |
| HAG4 | Does the device support at least 16 entries in the scenes table? | [R3]/6 | HAG3:M | Yes |
| HAG5 | Does the device support a method for the user to put the device in join mode? |  | By device type | Yes |
| HAG6 | Does the device support a method for the user to use the device to form a network? |  | By device type | Yes |
| HAG7 | Does the device support a method for allowing others to join the network? |  | By device type | Yes |
| HAG8 | Does the device support a method for allowing a user to restore factory settings? |  | By device type | Yes |
| HAG9 | Does the device support a method to pair devices? |  | By device type | No |
| HAG10 | Does the device support a method for the user to enable identify mode? |  | By device type | Yes |

## ZigBee Home Automation device description support

Table 5 – HA device description support

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| HAD1 | Is the product programmed as an On/Off Switch? | [R3]/7.3.4 | O.1 | No |
| HAD2 | Is the product programmed as a Level Control Switch? | [R3]/7.3.5 | O.1 | No |
| HAD3 | Is the product programmed as an On/Off Output? | [R3]/7.3.6 | O.1 | No |
| HAD4 | Is the product programmed as Level Controllable Output? | [R3]/7.3.7 | O.1 | No |
| HAD5 | Is the product programmed as a Scene Selector? | [R3]/7.3.8 | O.1 | No |
| HAD6 | Is the product programmed as a Configuration Tool? | [R3]/7.3.9 | O.1 | No |
| HAD7 | Is the product programmed as a Remote Control? | [R3]/7.3.10 | O.1 | No |
| HAD8 | Is the product programmed as a Combined Interface? | [R3]/7.3.11 | O.1 | No |
| HAD9 | Is the product programmed as a Range Extender? | [R3]/7.3.12 | O.1 | No |
| HAD10 | Is the product programmed as a Mains Power Outlet? | [R3]/7.3.13 | O.1 | No |
| HAD33 | Is the product a Door Lock? | R3/7.3.2 | O.1 | No |
| HAD34 | Is the product a Door Lock Controller? | R3/7.3.3 | O.1 | No |
| HAD32 | Is the product a Simple Sensor? | R3 | O.1 | No |
| HAD11 | Is the product programmed as a On/Off Light? | [R3]/7.4.1 | O.1 | No |
| HAD12 | Is the product programmed as a Dimmable Light? | [R3]/7.4.2 | O.1 | Yes |
| HAD13 | Is the product programmed as a Color Dimmable Light? | [R3]/7.4.3 | O.1 | No |
| HAD14 | Is the product programmed as an On/Off Light Switch? | [R3]/7.4.4 | O.1 | No |
| HAD15 | Is the product programmed as a Dimmer Switch? | [R3]/7.4.5 | O.1 | No |
| HAD16 | Is the product programmed as a Color Dimmer Switch? | [R3]/7.4.6 | O.1 | No |
| HAD17 | Is the product programmed as a Light Sensor? | [R3]/7.4.7 | O.1 | No |
| HAD18 | Is the product programmed as an Occupancy Sensor? | [R3]/7.4.8 | O.1 | No |
| HAD19 | Is the product programmed as a Shade? | [R3]/7.5.1 | O.1 | No |
| HAD20 | Is the product programmed as a Shade Controller? | [R3]/7.5.2 | O.1 | No |
| HAD35 | Is the product a Window Covering Device | R3/7.5.3 | O.1 | No |
| HAD36 | Is the product a Window Covering Controller | R3/7.5.4 | O.1 | No |
| HAD21 | Is the product programmed as a Heating/Cooling Unit? | [R3]/7.6.1 | O.1 | No |
| HAD22 | Is the product programmed as a Thermostat? | [R3]/7.6.2 | O.1 | No |
| HAD23 | Is the product programmed as a Temperature Sensor? | [R3]/7.6.3 | O.1 | No |
| HAD24 | Is the product programmed as a Pump? | [R3]/7.6.4 | O.1 | No |
| HAD25 | Is the product programmed as a Pump Controller? | [R3]/7.6.5 | O.1 | No |
| HAD26 | Is the product programmed as a Pressure Sensor? | [R3]/7.6.6 | O.1 | No |
| HAD27 | Is the product programmed as a Flow Sensor? | [R3]/7.6.7 | O.1 | No |
| HAD28 | Is the product programmed as a Control and Indicating Equipment? | [R3]/7.7.1 | O.1 | No |
| HAD29 | Is the product programmed as an IAS Ancillary Control Equipment? | [R3]/7.7.2 | O.1 | No |
| HAD30 | Is the product programmed as an IAS Zone? | [R3]/7.7.3 | O.1 | No |
| HAD31 | Is the product programmed as an IAS Warning Device? | [R3]/7.7.4 | O.1 | No |

## Home Automation common clusters

Table 6 – Common cluster ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| BCS1 | M |  | Yes |
| ICS1 | M |  | Yes |
| PCCS1 | O |  | No |
| TCCS1 | O |  | No |
| ACS1 | O |  | No |
| SMC1 | O |  |  |
| SMS1 | O |  |  |

Table 7 – Common cluster support

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| HACC1 | Are any clusters that receive attribute reports supported as either server or client? | [R2] 7.1 | O | Yes |
| HACC2 | Are any manufacturer-specific clusters supported? | [R2] 7.1 | O | No |

## ZigBee Home Automation Device Description Capabilities

Tables in the following sub-clauses detail the capabilities specific to a device description.

Simple Sensor device functions

Table 8 – Sinple Sensor ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| BICS1 | HAD32:M |  |  |

### On/Off Switch device functions

Table 8 – On/Off Switch ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| SCCS1 | HAD1:M |  |  |
| OOCC1 | HAD1:M |  |  |
| SCC1 | HAD1:M |  |  |
| GCC1 | HAD1:M |  |  |
| ICC1 | HAD1:M |  |  |
| ZSP2 | HAD1:M |  |  |

### Level Control Switch device functions

Table 9 – Level Control Switch ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| SCCS1 | HAD2:M |  |  |
| OOCC1 | HAD2:M |  |  |
| LCCC1 | HAD2:M |  |  |
| SCC1 | HAD2:M |  |  |
| GCC1 | HAD2:M |  |  |
| ICC1 | HAD2:M |  |  |
| ZSP2 | HAD1:M |  |  |

### On/Off Output device functions

Table 10 – On/Off Output ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| OOCS1 | HAD3:M |  |  |
| SCS1 | HAD3:M |  |  |
| GCS1 | HAD3:M |  |  |

### Level Controllable Output device functions

Table 11 Level Controllable Output ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| OOCS1 | HAD4:M |  |  |
| LCCS1 | HAD4:M |  |  |
| SCS1 | HAD4:M |  |  |
| GCS1 | HAD4:M |  |  |

### Scene Selector device functions

Table 12 – Scene Selector ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| SCC1 | HAD5:M |  |  |
| GCC1 | HAD5:M |  |  |
| ICC1 | HAD5:M |  |  |

### Configuration Tool device functions

Table 13 – Configuration Tool ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| BCC1 | HAD6:O |  |  |
| SCC1 | HAD6:O |  |  |
| GCC1 | HAD6:O |  |  |
| ICC1 | HAD6:O |  |  |
| SCCC1 | HAD6:O |  |  |
| ACC1 | HAD6:O |  |  |
| IMCC1 | HAD6:O |  |  |
| ILSC1 | HAD6:O |  |  |
| TMCC1 | HAD6:O |  |  |
| PMCC1 | HAD6:O |  |  |
| FMCC1 | HAD6:O |  |  |
| OSCC1 | HAD6:O |  |  |
| PCC1 | HAD6:O |  |  |
| SHCC1 | HAD6:O |  |  |
| TUIC1 | HAD6:O |  |  |

### Remote Control device functions

Table 14 – Remote Control ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| BCC1 | HAD7:M |  |  |
| SCC1 | HAD7:M |  |  |
| GCC1 | HAD7:M |  |  |
| ICC1 | HAD7:M |  |  |
| OOCC1 | HAD7:M |  |  |
| LCCC1 | HAD7:M |  |  |
| CCCC1 | HAD7:O |  |  |
| PCC1 | HAD7:O |  |  |
| SHCC1 | HAD7:O |  |  |
| SCCC1 | HAD7:O |  |  |
| TMCC1 | HAD7:O |  |  |
| IMCC1 | HAD7:O |  |  |
| ILSC1 | HAD7:O |  |  |
| WCCC1 | HAD7:O |  |  |
| DLCC1 | HAD7:O |  |  |

### Combined Interface device functions

Table 15 – Combined Interface ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| BCC1 | HAD8:M |  |  |
| SCC1 | HAD8:O |  |  |
| GCC1 | HAD8:O |  |  |
| ICC1 | HAD8:M |  |  |
| OOCC1 | HAD8:O |  |  |
| LCCC1 | HAD8:O |  |  |
| CCCC1 | HAD8:O |  |  |
| PCCCC1 | HAD8:O |  |  |
| SHCC1 | HAD8:O |  |  |
| SCCC1 | HAD8:O |  |  |
| TMCC1 | HAD8:O |  |  |
| IMCC1 | HAD8:O |  |  |
| ILSC1 | HAD8:O |  |  |
| TUIC1 | HAD8:O |  |  |
| WCCC1 | HAD7:O |  |  |
| DLCC1 | HAD7:O |  |  |

### Range Extender device functions

Table 16 – HA: Range Extender capabilities

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| RE1 | Does the device support ONLY those clusters listed as mandatory in the common clusters section? | [R2] 7.2.9 | HAD9:M |  |

### Mains Power Outlet device functions

Table 17 – Mains Power Outlet ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| OOCS1 | HAD10:M |  |  |
| SCS1 | HAD10:M |  |  |
| GCS1 | HAD10:M |  |  |

### On/Off Light device functions

Table 18 – On/Off Light ZCL PICS restrictions/requirements

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| OOCS1 | HAD11:M |  | Yes |
| SCS1 | HAD11:M |  | Yes |
| GCS1 | HAD11:M |  | Yes |
| OSCC1 | HAD11: O |  | No |

### Dimmable Light device functions

Table 19 – Dimmable Light ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| OOCS1 | HAD12:M |  | Yes |
| LCCS1 | HAD12:M |  | Yes |
| SCS1 | HAD12:M |  | Yes |
| GCS1 | HAD12:M |  | Yes |
| OSCC1 | HAD12:O |  | No |

### Color Dimmable Light device functions

Table 20 – Color Dimmable Light ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| OOCS1 | HAD13:M |  |  |
| LCCS1 | HAD13:M |  |  |
| CCCS1 | HAD13:M |  |  |
| SCS1 | HAD13:M |  |  |
| GCS1 | HAD13:M |  |  |
| OSCC1 | HAD13: O |  |  |

### On/Off Light Switch device functions

Table 21 – On/Off Light Switch ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| SCCS1 | HAD14:M |  | No |
| OOCC1 | HAD14:M |  | No |
| SCC1 | HAD14:M |  |  |
| GCC1 | HAD14:M |  |  |
| ICC1 | HAD14:M |  |  |
| ZSP2 | HAD14:M |  |  |

### Dimmer Switch device functions

Table 22 – Dimmer Switch ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| SCCS1 | HAD15:M |  |  |
| OOCC1 | HAD15:M |  |  |
| LCCC1 | HAD15:M |  |  |
| SCC1 | HAD15:M |  |  |
| GCC1 | HAD15:M |  |  |
| ZSP2 | HAD15:M |  |  |

### Color Dimmer Switch device functions

Table 23 – Color Dimmer Switch ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| SCCS1 | HAD16:M |  |  |
| OOCC1 | HAD16:M |  |  |
| LCCC1 | HAD16:M |  |  |
| CCCC1 | HAD16:M |  |  |
| SCC1 | HAD16:M |  |  |
| GCC1 | HAD16:M |  |  |
| ICC1 | HAD16:M |  |  |
| ZSP2 | HAD16:M |  |  |

### Light Sensor device functions

Table 24 – Light Sensor Switch ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| IMCS1 | HAD17:M |  |  |
| GCC1 | HAD17:O |  |  |

### Occupancy Sensor device functions

Table 25 – Occupancy Sensor Switch ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| OSCS1 | HAD18:M |  |  |
| GCC1 | HAD18:O |  |  |

### Shade device functions

Table 26 – Shade ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| SHCS1 | HAD19:M |  |  |
| OOCS1 | HAD19:M |  |  |
| LCCS1 | HAD19:M |  |  |
| SCS1 | HAD19:M |  |  |
| GCS1 | HAD19:M |  |  |

### Shade Controller device functions

Table 27 – Shade Controller ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| SHCC1 | HAD20:M |  |  |
| OOCC1 | HAD20:M |  |  |
| LCCC1 | HAD20:M |  |  |
| SCC1 | HAD20:M |  |  |
| GCC1 | HAD20:M |  |  |
| ICC1 | HAD20:M |  |  |
| ZSP2 | HAD20:M |  |  |

### Heating/Cooling Unit device functions

Table 28 – Heating/Cooling Unit ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| OOCS1 | HAD21:M |  |  |
| GCS1 | HAD21:O |  |  |
| TC1 | HAD21:M |  |  |
| FCCS1 | HAD21:O |  |  |
| LCCS1 | HAD21:O |  |  |

### Thermostat device functions

Table 29 – Thermostat ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| TS1 | HAD22:M |  |  |
| SCS1 | HAD22:M |  |  |
| GCS1 | HAD22:M |  |  |
| TMCC1 | HAD22:O |  |  |
| FCCS1 | HAD22:O |  |  |
| OSCC1 | HAD22:O |  |  |
| RHMC1 | HAD22:O |  |  |
| TUIS1 | HAD22:O |  |  |

Table 30 – HA: Thermostat capabilities

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| TD1 | Are the OccupiedCoolingSetpoint, OccupiedHeatingSetpoint, and SystemMode attributes of the Thermostat cluster supported as extension fields in the Scenes table? | [R2] 7.5.2.5 | HAD22:M |  |

### Temperature Sensor device functions

Table 31 – Temperature Sensor ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| TMCS1 | HAD23:M |  |  |
| GCC1 | HAD23:O |  |  |

### Pump device functions

Table 32 – Pump ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| PCS1 | HAD24:M |  |  |
| OOCS1 | HAD24:M |  |  |
| SCS1 | HAD24:M |  |  |
| GCS1 | HAD24:M |  |  |
| LCCS1 | HAD24:O |  |  |
| ACS1 | HAD24:O |  |  |
| PMCS1 | HAD24:O |  |  |
| TMCS1 | HAD24:O |  |  |
| FMCS1 | HAD24:O |  |  |
| PMCC1 | HAD24:O |  |  |
| TMCC1 | HAD24:O |  |  |
| FMCC1 | HAD24:O |  |  |

### Pump Controller device functions

Table 33 – Pump Controller ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| PCC1 | HAD25:M |  |  |
| OOCC1 | HAD25:M |  |  |
| GCC1 | HAD25:M |  |  |
| SCC1 | HAD25:M |  |  |
| ICC1 | HAD25:M |  |  |
| LCCC1 | HAD25:O |  |  |
| PMCC1 | HAD25:O |  |  |
| TMCC1 | HAD25:O |  |  |
| FMCC1 | HAD25:O |  |  |
| ZSP2 | HAD25:M |  |  |

### Pressure Sensor device functions

Table 34 – Pressure Sensor ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| PMCS1 | HAD26:M |  |  |
| GCC1 | HAD26:O |  |  |

### Flow Sensor device functions

Table 35 – Flow Sensor ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| FMCS1 | HAD27:M |  |  |
| GCC1 | HAD27:O |  |  |

### IAS CIE device functions

Table 36 – IAS CIE ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| IACS1 | HAD28:M |  |  |
| IZCS1 | HAD28:M |  |  |
| SCC1 | HAD28:O |  |  |
| GCC1 | HAD28:O |  |  |
| WDCC1 | HAD28:M |  |  |
| ICC1 | HAD28:M |  |  |

Table 37 –  Intruder Alarm System Control and Indicating Equipment capabilities

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| CIE1 | Is the DeviceEnable attribute of the Basic cluster restricted to read-only? | [R2] 7.6.1.2 |  |  |

### IAS ACE device functions

Table 38 – IAS ACE ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| IACC1 | HAD29:M |  |  |
| IZCS1 | HAD29:M |  |  |
| ICC1 | HAD29:M |  |  |
| SCS1 | HAD29:O |  |  |
| ZSP2 | HAD29:M |  |  |

Table 39 –  Intruder Alarm System Ancillary Control Equipment capabilities

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| ACE1 | Is the DeviceEnable attribute of the Basic cluster restricted to read-only? | [R2] 7.6.2.2 | HAD29:M |  |

### IAS Zone device functions

Table 40 – IAS Zone ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| IZCC1 | HAD30:M |  |  |
| ZSP2 | HAD30:M |  |  |

Table 41 – Intruder Alarm System Zone capabilities

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| IASZ1 | Is the DeviceEnable attribute of the Basic cluster restricted to read-only? | [R2] 7.6.3.2 | HAD30:M |  |

### IAS WD device functions

Table 42 – IAS WD ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| WDCS1 | HAD31:M |  |  |
| IZCC1 | HAD31:M |  |  |
| SCS1 | HAD31:O |  |  |
| GCS1 | HAD31( |  |  |

Table 43 –Intruder Alarm System Warning Device capabilities

| Item number | Item description | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| IWD1 | Is the DeviceEnable attribute of the Basic cluster restricted to read-only? | [R2] 7.6.2.2 | HAD31:M |  |

### Simple Sensor

Table 44 – Simple Sensor ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| BIC1 | HAD32:M |  |  |

### Door Lock

Table 45 – Door Lock ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| DLC1 | HAD33:M |  |  |
| SCS1 | HAD33:M |  |  |
| GCS1 | HAD33:M |  |  |
| ZSP2 | HAD33:M |  |  |

### Door Lock Controller

Table 45 – Door Lock Controller ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| DCC1 | HAD34:M |  |  |
| SCCS1 | HAD34:M |  |  |
| GCCS1 | HAD34:M |  |  |

### Window Covering

Table 45 – Window Covering ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| WCS1 | HAD35:M |  |  |
| SCS1 | HAD35:M |  |  |
| GCS1 | HAD35:M |  |  |

### Window Covering Controller

Table 45 – Window Covering Controller ZCL PICS restrictions

| ZCL PICS Item number [R14] | Status | Additional Constraints | Support |
| --- | --- | --- | --- |
| WCC1 | HAD36:M |  |  |
| SCC1 | HAD36:M |  |  |
| GCC1 | HAD36:M |  |  |
| ICC1 | HAD36:M |  |  |
| ZSP2 | HAD36:M |  |  |