| PICS Pro forma Table |
| --- |
| Item Number | Item description / Additional Constraints | Reference | Status | Support for Communication Hub? | Special comments from document |
| FDT1 | Is this device capable of acting as a ZigBee coordinator? | [R1]/2.5.5.5.1 | O.1 | Y | Functional device types. O.1 – Device under test must select only one of these options. Devices under test supporting multiple ZigBee device types must serially re-test using each supported ZigBee device type. |
| FDT2 | Is this device capable of acting as a ZigBee router? | [R1]/2.5.5.5.2 | O.1 | N |  |
| FDT3 | Is this a ZigBee end device? | [R1]/2.5.5.5.3 | O.1 | N |  |
| ZSP1 | Is the device built on a ZigBee Compliant Platform certified for the ZigBee stack profile [R8]? | [R4] | O.2 | N | Stack Profile. O.2 – Device under test must be deployed on either of the ZigBee or ZigBee PRO stack profiles. |
|  |  | [R2]/5.2 |  |  |  |
| ZSP2 | Is the device built on a ZigBee PRO Compliant Platform certified for the ZigBee PRO stack profile [R8]? | [R8] | O.2 | Y |  |
|  |  | [R2]/5.2 |  |  |  |
| SPE1 | Does the device support Application Link Keys? | [R2]/5.2 | M | Y | Stack profile extensions for SE |
|  |  | [R6]/ASLS6 |  |  |  |
| SPE2 | Does this device use a stack that supports fragmentation? | [R2]/5.2 | M | Y |  |
|  |  | [R5]/ADF5, ADF6 |  |  |  |
| SPE3 | Does this device use any SE Profile Commands that require the use of Fragmentation? | [R2]/5.2 | MC1: M | Y |  |
|  |  | [R5]/ADF5, ADF6 | MS1: M |  |  |
| SPE4 | Does the device adhere to the polling rate specifications given in [R2]/5.2 (i.e. Does your application poll equal to or less often as called out in the specification)? | [R2]/5.2 | FDT3:M | N |  |
| SPE5 | Does this devices support reception of fragmented messages? |  | M | Y |  |
| SPE6 | Does this device support generation of fragmented messages? |  | O | Y |  |
| SEG1 | Does the device support the ZigBee Cluster Library? | [R2]/5.11, 5.12 | M | Y | SE general requirements support |
|  |  | [R3] |  |  |  |
| SEG2 | Does the device support the ZigBee Cluster Library List specified for SE including the mandatory/optional clusters detailed in the ZCL PICs? | [R2]/5.11, 5.12 | M | Y |  |
|  |  | [R7] |  |  |  |
| SEG3 | Does the device support the ZigBee Cluster Library with the parameters for attribute reporting, reporting configuration and read reporting configuration as detailed in the SE Profile clusters? | [R2]/5.11 | M | Y |  |
|  | Editor’s Note: Reporting interval constraints and other parameters are mandatory where attribute reporting is used. Support of attribute reporting may be optional or mandatory based on clusters implemented. | [R3] |  |  |  |
| SEG4 | Is the device capable of joining a ZigBee SE network and does it interact with a consumer ZigBee Home Area Network only through a bridge device? | [R2]/5.1 | FDT2: M | N |  |
|  |  |  | FDT3: M |  |  |
| SEG5 | Does the device support “E-Mode” commissioning? | [R2]/5.1 | FDT2: M | N |  |
|  | SE Profile requirement: Those devices that will join an existing network must support button pushes or simple documented user interfaces to initiate the joining process. |  | FDT3: M |  |  |
|  |  |  | For joining devices |  |  |
| SEG6 | Deleted | [R2]/5.1 |  | N/A |  |
| SEG7 | Does the device support the compatible Startup Attribute Set, Join Parameters, Security Parameters, End Device Parameters, Link Status Parameters, Concentrator Parameters, APS Transport Parameters and Binding Parameters? | [R2]/5.3, 5.3.1, 5.3.2, 5.3.3, 5.3.4, 5.3.5, 5.3.6, 5.3.7, 5.3.8, 5.3.9 | M | Y |  |
| SEG8 | Does the device support joining with pre-installed link keys? | [R2]/5.4.1 | FDT2: M | N |  |
|  | Note: SE specifies use of Install Codes to derive the link key. |  | FDT3: M |  |  |
| SEG9 | Does the device support joining using the key establishment cluster? | [R2]/5.4.7 | FDT2: M | Y |  |
|  |  |  | FDT3: M |  |  |
| SEG10 | Deleted | [R2]/5.5 |  | NA |  |
| SEG11 | Does the device support the list of SE preferred channels? | [R2]/5.8.1 | O | Y |  |
| SEG12 | Does the device support the SE broadcast policy? | [R2]/5.8.2 | O | N |  |
| SEG13 | Does the device support the SE frequency agility policy? | [R2]/5.8.3 | O | N |  |
| SEG14 | Does the device support the security key update policies for SE networks? | [R2]/5.8.4 | M | Y |  |
| SEG15 | Does the device support the ZCL Time Cluster and SE time synchronization? | [R2]/5.12.1.1 | O | Y |  |
|  | Editor’s Note: Support of the ZCL Time Cluster is not mandatory for all SE devices. The SE device descriptions define the required Time cluster support. |  |  |  |  |
| SEG16 | Does the device support discovery of optional attributes? | [R2]/5.12 | M | Y |  |
| SEG17 | Does the device application discover and handle unsupported attributes in other devices? | [R2]/5.12 | M | Y |  |
| SEG18 | Does the device support an indication to the user that the network has formed properly? | [R2]/5.5.1 | O | Y |  |
|  |  |  | . |  |  |
| SEG19 | Does the device support an indication to the user that a device has joined a network successfully? | [R2]/5.5.1 | O | N |  |
| SEG20 | Does the device support the commissioning modes and provide supporting commissioning documentation according to network type? | [R2]/5.5.2, 5.5.3, 5.5.4 | M | Y |  |
| SEG21 | Does the device use the appropriate security key per cluster? | [R2]/5.4.6 | M | Y |  |
| SEG22 | Does the device support the SE Mirrored Device Capacity – Service Discovery? | [R4]/D.3.3.4.1 | O | Y |  |
| SEG23 | Does one of the device support the SE Install Code Formats: 48, 64, 96, or 128 bit number and 16 bit CRC? | [R4]/5.4.8.1.1 | O | N |  |
| SEG24 | Does the device expect to receive unsolicited messages from the DRLC, Messaging, Metering or Pricing clusters? | [R4]/5.4.5.1 | O | Y |  |
| SEG25 | Does the device support rejoining a secured network? | [R4]/5.4.2 | FDT2:M | N |  |
|  |  |  | FDT3:M |  |  |
| SEG26 | Does the device support devices leaving its network? | [R4]/5.4.3 | FDT1:M | Y |  |
| SEG27 | Does the device support updating the Network Key? | [R4]/5.4.4 | M | Y |  |
| SEG28 | Does the device support updating the Link Key? | [R4]/5.4.5 | M | Y |  |
| SEG29 | Does the device support Federated Trust Center functionality? | [R2]/5.6 | O | N |  |
| SEG30 | Does the device support Network Interoperabiity? | [R2]/5.13 | O | N |  |
| SED1 | Is the product programmed as an Energy Service Interface? | [R2]/6.3.1 | O.3 | Y [Int: EP# 3] | SE device description support. O.3 – Device under test must select at least one and may select more than one of the SE device descriptions. If multiple SE device descriptions are supported in the same device then each of the supported device descriptions must be deployed on individual endpoints within the device under test. |
| SED2 | Is the product programmed as a Metering Device? | [R2]/6.3.2 | O.3 | [Y/N] [Int: EP# x] |  |
| SED3 | Is the product programmed as an In-Home Display? | [R2]/6.3.3 | O.3 | N |  |
| SED4 | Is the product programmed as a Programmable Communicating Thermostat (PCT)? | [R2]/6.3.4 | O.3 | N |  |
| SED5 | Is the product programmed as a Load Control? | [R2]/6.3.5 | O.3 | N |  |
| SED6 | Is the product programmed as a Range Extender? | [R2]/6.3.6 | O.3 | N |  |
| SED7 | Is the product programmed as a Smart Appliance? | [R2]/6.3.7 | O.3 | N |  |
| SED8 | Is the product programmed as a Prepayment Terminal? | [R2]/6.3.8 | O.3 | N |  |
| SED9 | Does the product utilize an endpoint using the Physical Device identifier? | [R2]/6.3.9 | O | [Y/N] [Int: EP# x] |  |
| FC100 | ZCL Cluster ID enumeration is mandatory |  | M | Y | Common cluster ZCL PICS restrictions/requirements |
| FC1 | General ZCL Frame Format is mandatory |  | M | Y |  |
| BCC1 | Does the device support the Basic Cluster as a client? |  | O | N |  |
| BCS1 | Does the device support the Basic Cluster as a server? |  | M | Y [Int: EP# 1,2,3] |  |
| GCC1 | Deleted |  | O | NA |  |
| GCS1 | Deleted |  | O | NA |  |
| ACC1 | Does the device support the Alarms Cluster as a client? |  | O | N |  |
| ACS1 | Does the device support the Alarms Cluster as a server? |  | O | N |  |
| TCS1 | Deleted |  |  | NA |  |
| TCC1 | Deleted |  |  | NA |  |
| ASDC1 | Deleted | [R2]/5.10 |  | NA | Common cluster support |
| ASDC2 | Deleted | [R2]/5.10 |  | NA |  |
| ASDC3 | Deleted | [R2]/5.10 |  | NA |  |
| ASDS1 | Deleted |  | O | NA |  |
| ASDS2 | Deleted |  | O | NA |  |
| ASDS3 | Deleted |  | O | NA |  |
| KEC1 | Does the device support the Key Establishment cluster as a client? | [R2]/Annex C.3.1 | M | Y [Int: EP# 1,2,3] |  |
| KES1 | Does the device support the Key Establishment cluster as a server? | [R2]/Annex C.3.1 |  | Y [Int: EP# 1,2,3] |  |
|  |  |  | M |  |  |
| SECC1 | Does the device support clusters with Reporting Capability? | [R2]/6.1.1 | O | N |  |
| SECC2 | Are any manufacturer-specific cluster(s) supported? | [R2]/6.1.2 | O | N |  |
| SECC3 | Are any non-SE ZCL or other application cluster(s) supported? | [R2]/6.1.3 | O | N |  |
| ICS1 | Does the device support the Identify cluster? | [R2]/ 6.1 | O | N |  |
| PCCS1 | Does the device support the Power Configuration cluster? | [R2]/ 6.1 | O | N |  |
| SMC2 | Does the device support the Block Tariffs Metering cluster attributes as a client? | [R2]/ 6.1 | O | N |  |
| SMS2 | Does the device support the Block Tariffs Metering cluster attributes as a server? | [R2]/ 6.1 | O | Y [Int: EP# 2] |  |
| TCSW1 | Does the device support Trust Center Swap-out ? | [R2]/ 6.1 | O | N |  |
| OTAC1 | Does the device support the OTA Upgrade cluster as a client? | [R2]/ 6.1 | O | N |  |
| OTAS1 | Does the device support the OTA Upgrade cluster as a server? | [R2]/ 6.1 | O | Y [Int: EP# 1] |  |
| ALM1 | Does the device support the Alarms as a server? | [R2]/ 6.1 | O | N |  |
| TCS1 | Time Cluster server is mandatory |  | M | Y [Int: EP# 1,3] | Energy Service Interface ZCL PICS restrictions/requirements |
| SMC1 | Metering Cluster client is optional |  | O | Y [Int: EP# 2,3] | Energy Service Interface SE PICS restrictions/requirements |
| SMS1 | Metering Cluster server is optional |  | O | Y [Int: EP# 2] |  |
| MS1 | Messaging Cluster server is mandatory |  | M | Y [Int: EP# 3] |  |
| PS1 | Price Cluster server is mandatory |  | M | Y [Int: EP# 3] |  |
| DRLS1 | Demand Response and Load Cluster server is mandatory |  | M | Y [Int: EP# 3] |  |
| PC1 | Price Cluster client is optional |  | O | N |  |
| TOUS1 | TOU Calendar Cluster server is optional |  | O | Y [Int: EP# 3] |  |
| MS1 | Messaging Cluster client is optional |  | O | N |  |
| PPC1 | Prepayment Cluster client is optional |  | O | Y [Int: EP# 2] |  |
| PPS1 | Prepayment Cluster server is optional |  | O | Y [Int: EP# 2] |  |
| DMS1 | Device Management Cluster server is optional |  | O | Y [Int: EP# 3] |  |
| DMC1 | Device Management Cluster client is optional |  | O | N |  |
| ALM1 | Alarms Cluster server is optional |  | O | N |  |
| EVS1 | Events Cluster server is optional |  | O | Y [Int: EP# 2,3] |  |
| EVC1 | Events Cluster client is optional |  | O | Y [Int: EP# 2] |  |
| MDUS1 | MDU Pairing Cluster server is optional |  | O | N |  |
| MDUC1 | MDU Pairing Cluster client is optional |  | O | N |  |
| EMC1 | Energy Management Cluster client is optional |  | O | N |  |
| TUS1 | Tunneling Cluster server is optional |  | O | Y [Int: EP# 1] |  |
| TCSW1 | Trust Center Swap-out is optional |  | O | N |  |
| OTAS1 | OTA Upgrade Cluster server is optional |  | O | Y [Int: EP# 1] |  |
| TUC1 | Tunneling Cluster client is optional |  | O | Y [Int: EP# 1] |  |
| OTAC1 | OTA Upgrade Cluster client is optional |  | O | N |  |
| TCC1 | Time Cluster client is optional |  | O | N |  |
| BCS1 | Is the Basic Cluster supported as a server? | [R3] | M | Y [Int: EP# 1,2,3] | Smart Energy Application Specific Cluster function capabilities. Basic cluster server capabilities |
| BCS2 | Is the ZCLversion attribute supported? |  | BCS1:M | Y [Int: EP# 1,2,3] |  |
| BCS3 | Is the Powersource attribute supported? |  | BCS1:M | Y [Int: EP# 1,2,3] |  |
| BCS4 | Is the PhysicalEnvironment attribute supported? |  | SEG22:M | Y [Int: EP# 3] |  |
|  |  |  | BCS1:O |  |  |
| BCC1 | Is the Basic Cluster supported as a client? | [R3] | O | N | Smart Energy Application Specific Cluster function capabilities. Basic cluster client capabilities |
| TICS1 | Is the Time Cluster supported as a server? | [R3] | O | [Y/N] [Int: EP# 1,3] | Smart Energy Application Specific Cluster function capabilities. Time cluster server capabilities |
| TICS2 | Is the Time attribute supported? |  | TICS1:M | Y [Int: EP# 1,3] |  |
| TICS3 | Is the TimeStatus attribute supported? |  | TICS1:M | Y [Int: EP# 1,3] |  |
| TICS4 | Is the TimeZone attribute supported? |  | TICS1:O | N |  |
| TICS5 | Is the DstStart attribute supported? |  | TICS1:O | N |  |
| TICS6 | Is the DstEnd attribute supported? |  | TICS1:O | N |  |
| TICS7 | Is the DstShift attribute supported? |  | TICS1:O | N |  |
| TICS8 | Is the StandardTime attribute supported? |  | TICS1:O | N |  |
| TICS9 | Is the LocalTime attribute supported? |  | TICS1:O | Y [Int: EP# 1] |  |
| TICC1 | Is the Time Cluster supported as a client? | [R3] | O | N | Smart Energy Application Specific Cluster function capabilities. Time cluster client capabilities |
| KECS1 | Is the Key Establishment Cluster supported as a server? | [R2]/C.3.1 | M | Y [Int: EP# 1,2,3] | Smart Energy Application Specific Cluster function capabilities. Key Establishment cluster server capabilities |
| KECS2 | Is the KeyEstablishmentSuite attribute supported? | [R2]/C.3.1.2.2.1 | KECS1:M | Y [Int: EP# 1,2,3] |  |
| KECS3 | Is the reception of Initiate Key Establishment Request command supported? | [R2]/C.3.1.2.3.1 | KECS1:M | Y [Int: EP# 1,2,3] |  |
| KECS4 | Is the reception of Ephemeral Data Request command supported? | [R2]/C.3.1.2.3.2 | KECS1:M | Y [Int: EP# 1,2,3] |  |
| KECS5 | Is the reception of Confirm Key Data Request command supported? | [R2]/C.3.1.2.3.3 | KECS1:M | Y [Int: EP# 1,2,3] |  |
| KECS6 | Is the reception of Terminate Key Establishment command supported? | [R2]/C.3.1.2.3.4 | KECS1:M | Y [Int: EP# 1,2,3] |  |
| KECS7 | Is the generation of Initiate Key Establishment Response command supported? | [R2]/C.3.1.2.4 / C.3.1.3.3.1 | KECS1:M | Y [Int: EP# 1,2,3] |  |
| KECS8 | Is the generation of Ephemeral Data Response command supported? | [R2]/C.3.1.2.4 / C.3.1.3.3.2 | KECS1:M | Y [Int: EP# 1,2,3] |  |
| KECS9 | Is the generation of Confirm Key Data Response command supported? | [R2]/C.3.1.2.4 / C.3.1.3.3.3 | KECS1:M | Y [Int: EP# 1,2,3] |  |
| KECS10 | Is the generation of Terminate Key Establishment command supported? | [R2]/C.3.1.2.4 / C.3.1.3.3.4 | KECS1:M | Y [Int: EP# 1,2,3] |  |
| KECC1 | Is the Key Establishment Cluster supported as a client? | [R2]/C.3.1 | M | Y [Int: EP# 1,2,3] | Smart Energy Application Specific Cluster function capabilities. Key Establishment cluster client capabilities |
| KECC2 | Is the KeyEstablishmentSuite attribute supported? | [R2]/C.3.1.3.2.1 | KECC1:M | Y [Int: EP# 1,2,3] |  |
| KECC3 | Is the reception of Initiate Key Establishment Response command supported? | [R2]/C.3.1.3.3.1 | KECC1:M | Y [Int: EP# 1,2,3] |  |
| KECC4 | Is the reception of Ephemeral Data Response command supported? | [R2]/C.3.1.3.3.2 | KECC1:M | Y [Int: EP# 1,2,3] |  |
| KECC5 | Is the reception of Confirm Key Data Response command supported? | [R2]/C.3.1.3.3.3 | KECC1:M | Y [Int: EP# 1,2,3] |  |
| KECC6 | Is the reception of Terminate Key Establishment command supported? | [R2]/C.3.1.3.3.4 | KECC1:M | Y [Int: EP# 1,2,3] |  |
| KECC7 | Is the generation of Initiate Key Establishment Request command supported? | [R2]/C.3.1.3.4 / C.3.1.2.3.1 | KECC1:M | Y [Int: EP# 1,2,3] |  |
| KECC8 | Is the generation of Ephemeral Data Request command supported? | [R2]/C.3.1.3.4 / C.3.1.2.3.2 | KECC1:M | Y [Int: EP# 1,2,3] |  |
| KECC9 | Is the generation of Confirm Key Data Request command supported? | [R2]/C.3.1.3.4 / C.3.1.2.3.3 | KECC1:M | Y [Int: EP# 1,2,3] |  |
| KECC10 | Is the generation of Terminate Key Establishment command supported? | [R2]/C.3.1.3.4 / C.3.1.2.3.4 | KECC1:M | Y [Int: EP# 1,2,3] |  |
| DRLCCS1 | Is the Demand Response and Load Control Cluster supported as a server? | [R2]/D.2 | O | Y [Int: EP# 3] | Smart Energy Application Specific Cluster function capabilities. Demand Response and Load Control cluster server capabilities |
| DRLCCS2 | Is the reception of Report Event Status command supported? | [R2]/D.2.2.4 / D.2.3.3.1 | DRLCCS1:M | Y [Int: EP# 3] |  |
| DRLCCS3 | Is the reception of Get Scheduled Events command supported? | [R2]/D.2.2.4 / D.2.3.3.2 | DRLCCS1:M | Y [Int: EP# 3] |  |
| DRLCCS4 | Is the generation of Load Control Event command supported? | [R2]/D.2.2.3.1 | DRLCCS1:M | Y [Int: EP# 3] |  |
| DRLCCS5 | Is the generation of Cancel Load Control Event command supported? | [R2]/D.2.2.3.2 | DRLCCS1:M | Y [Int: EP# 3] |  |
| DRLCCS6 | Is the generation of Cancel All Load Control Events command supported? | [R2]/D.2.2.3.3 | DRLCCS1:M | Y [Int: EP# 3] |  |
| DRLCCC1 | Is the Demand Response and Load Control Cluster supported as a client? | [R2]/D.2 | O | N | Smart Energy Application Specific Cluster function capabilities. Demand Response and Load Control cluster client capabilities |
| DRLCCC2 | Is the UtilityEnrolmentGroup attribute supported? | [R2]/D.2.3.2.1 | DRLCCC1:M | NA |  |
| DRLCCC3 | Is the StartRandomizeMinutes attribute supported? | [R2]/D.2.3.2.2 | DRLCCC1:M | NA |  |
| DRLCCC4 | Is the StopRandomizeMinutes attribute supported? | [R2]/D.2.3.2.3 | DRLCCC1:M | NA |  |
| DRLCCC5 | Is the DeviceClassValue attribute supported? | [R2]/D.2.3.2.4 | DRLCCC1:M | NA |  |
| DRLCCC5.1 | Is it permitted to externally write the DeviceClassValue attribute? | [R2]/D.2.3.2.4 | DRLCCC1:O | NA |  |
| DRLCCC6 | Is the reception of Load Control Event command supported? | [R2]/D.2.3.4 / D.2.2.3.1 | DRLCCC1:M | NA |  |
| DRLCCC7 | Is the reception of Cancel Load Control Event command supported? | [R2]/D.2.3.4 / D.2.2.3.2 | DRLCCC1:M | NA |  |
| DRLCCC8 | Is the reception of Cancel All Load Control Events command supported? | [R2]/D.2.3.4 / D.2.2.3.3 | DRLCCC1:M | NA |  |
| DRLCCC9 | Is the generation of Report Event Status command supported? | [R2]/D.2.3.3.1 | DRLCCC1:M | NA |  |
| DRLCCC10 | Is the generation of Get Scheduled Events command supported? | [R2]/D.2.3.3.2 | DRLCCC1:M | NA |  |
| MECS1 | Is the Metering Cluster supported as a server? | [R2]/D.3 | O | Y [Int: EP# 2] | Smart Energy Application Specific Cluster function capabilities. Metering cluster server capabilities |
| MECS2 | Is the CurrentSummationDelivered attribute supported? | [R2]/D.3.2.2.1.1 | MECS1:M | Y [Int: EP# 2] |  |
| MECS3 | Is the CurrentSummationReceived attribute supported? | [R2]/D.3.2.2.1.2 | MECS1:O | N |  |
| MECS4 | Is the CurrentMaxDemandDelivered attribute supported? | [R2]/D.3.2.2.1.3 | MECS1:O | N |  |
| MECS5 | Is the CurrentMaxDemandReceived attribute supported? | [R2]/D.3.2.2.1.4 | MECS1:O | N |  |
| MECS6 | Is the DFTSummation attribute supported? | [R2]/D.3.2.2.1.5 | MECS1:O | N |  |
| MECS7 | Is the DailyFreezeTime attribute supported? | [R2]/D.3.2.2.1.6 | MECS1:O | N |  |
| MECS8 | Is the PowerFactor attribute supported? | [R2]/D.3.2.2.1.7 | MECS1:O | N |  |
| MECS9 | Is the ReadingSnapShotTime attribute supported? | [R2]/D.3.2.2.1.8 | MECS1:O | N |  |
| MECS10 | Is the CurrentMaxDemandDeliveredTime attribute supported? | [R2]/D.3.2.2.1.9 | MECS1:O | N |  |
| MECS11 | Is the CurrentMaxDemandReceivedTime attribute supported? | [R2]/D.3.2.2.1.10 | MECS1:O | N |  |
| MECS12 | Is the DefaultUpdatePeriod attribute supported? | [R2]/D.3.2.2.1.11 | MECS1:O | N |  |
| MECS13 | Is the FastPollUpdatePeriod attribute supported? | [R2]/D.3.2.2.1.12 | MECS1:O | N |  |
| MECS14 | Is the CurrentBlockPeriodConsumptionDelivered attribute supported? | [R2]/D.3.2.2.1.13 | MECS132:M | N |  |
|  |  |  | MECS133:M |  |  |
| MECS15 | Is the DailyConsumptionTarget attribute supported? | [R2]/D.3.2.2.1.14 | MECS1:O | N |  |
| MECS16 | Is the CurrentBlock attribute supported? | [R2]/D.3.2.2.1.15 | MECS132:O | N |  |
|  |  |  | MECS133:O |  |  |
| MECS17 | Is the CurrentTier1SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | Y [Int: EP# 2] |  |
| MEC18 | Is the CurrentTier1SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS19 | Is the CurrentTier2SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | Y [Int: EP# 2] |  |
| MECS20 | Is the CurrentTier2SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS21 | Is the CurrentTier3SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | Y [Int: EP# 2] |  |
| MECS22 | Is the CurrentTier3SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS23 | Is the CurrentTier4SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | Y [Int: EP# 2] |  |
| MECS24 | Is the CurrentTier4SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS25 | Is the CurrentTier5SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS26 | Is the CurrentTier5SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS27 | Is the CurrentTier6SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS28 | Is the CurrentTier6SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS29 | Is the CurrentTier7SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS30 | Is the CurrentTier7SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS31 | Is the CurrentTier8SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS32 | Is the CurrentTier8SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS33 | Is the CurrentTier9SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS34 | Is the CurrentTier9SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS35 | Is the CurrentTier10SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS36 | Is the CurrentTier10SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS37 | Is the CurrentTier11SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS38 | Is the CurrentTier11SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS39 | Is the CurrentTier12SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS40 | Is the CurrentTier12SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS41 | Is the CurrentTier13SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS42 | Is the CurrentTier13SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS43 | Is the CurrentTier14SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS44 | Is the CurrentTier14SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS45 | Is the CurrentTier15SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS46 | Is the CurrentTier15SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS47 | Is the Meter Status attribute supported? | [R2]/D.3.2.2.3.1 | MECS1:M | Y [Int: EP# 2] |  |
| MECS48 | Is the UnitofMeasure attribute supported? | [R2]/D.3.2.2.4.1 | MECS1:M | Y [Int: EP# 2] |  |
| MECS49 | Is the Multiplier attribute supported? | [R2]/D.3.2.2.4.2 | MECS1:O | Y [Int: EP# 2] |  |
| MECS50 | Is the Divisor attribute supported? | [R2]/D.3.2.2.4.3 | MECS1:O | Y [Int: EP# 2] |  |
| MECS51 | Is the SummationFormatting attribute supported? | [R2]/D.3.2.2.4.4 | MECS1:M | Y [Int: EP# 2] |  |
| MECS52 | Is the DemandFormatting attribute supported? | [R2]/D.3.2.2.4.5 | MECS1:O | N |  |
| MECS53 | Is the HistoricalConsumptionFormatting attribute supported? | [R2]/D.3.2.2.4.6 | MECS1:O | N |  |
| MECS54 | Is the MeteringDeviceType attribute supported? | [R2]/D.3.2.2.4.7 | MECS1:M | Y [Int: EP# 2] |  |
| MECS54a | Is the MeteringDeviceType: Electric Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54b | Is the MeteringDeviceType: Gas Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | Y [Int: EP# 2] |  |
| MECS54c | Is the MeteringDeviceType: Water Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54d | Is the MeteringDeviceType: Pressure Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54e | Is the MeteringDeviceType: Heat Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54f | Is the MeteringDeviceType: Cooling Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54g | Is the MeteringDeviceType: End Use Measurement Device (EUMD)? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54h | Is the MeteringDeviceType: PV Generation Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54i | Is the MeteringDeviceType: Wind Turbine Generation Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54j | Is the MeteringDeviceType: Water Turbine Generation Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54k | Is the MeteringDeviceType: Micro Generation Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54l | Is the MeteringDeviceType: Solar Hot Water Generation Metering? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54m | Is the MeteringDeviceType: Electric Metering Element/Phase1 supported? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54n | Is the MeteringDeviceType: Electric Metering Element/Phase2 supported? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS54o | Is the MeteringDeviceType: Electric Metering Element/Phase3 supported? | [R2]/D.3.2.2.4.7 | MECS54:O.1 | N |  |
| MECS55 | Is the SiteID attribute supported? | [R2]/D.3.2.2.4.8 | MECS1:O | Y [Int: EP# 2] |  |
| MECS56 | Is the MeterSerialNumber attribute supported? | [R2]/D.3.2.2.4.9 | MECS1:O | N |  |
| MECS57 | Is the InstantaneousDemand attribute supported? | [R2]/D.3.2.2.5.1 | MECS1:O | N |  |
| MECS58 | Is the CurrentDayConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.2 | MECS1:O | N |  |
| MECS59 | Is the CurrentDayConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.3 | MECS1:O | N |  |
| MECS60 | Is the PreviousDayConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.4 | MECS1:O | N |  |
| MECS61 | Is the PreviousDayConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.5 | MECS1:O | N |  |
| MECS62 | Is the CurrentPartialProfileIntervalStartTimeDelivered attribute supported? | [R2]/D.3.2.2.5.6 | MECS1:O | N |  |
| MECS63 | Is the CurrentPartialProfileIntervalStartTimeReceived attribute supported? | [R2]/D.3.2.2.5.7 | MECS1:O | N |  |
| MECS64 | Is the CurrentPartialProfileIntervalValueDelivered attribute supported? | [R2]/D.3.2.2.5.8 | MECS1:O | N |  |
| MECS65 | Is the CurrentPartialProfileIntervalValueReceived attribute supported? | [R2]/D.3.2.2.5.9 | MECS1:O | N |  |
| MECS66 | Is the MaxNumberOfPeriodsDelivered attribute supported? | [R2]/D.3.2.2.6.1 | MECS1:O | N |  |
| MECS67 | Is the CurrentDemandDelivered attribute supported? | [R2]/D.3.2.2.7.1 | MECS1:O | N |  |
| MECS68 | Is the DemandLimit attribute supported? | [R2]/D.3.2.2.7.2 | MECS1:O | N |  |
| MECS69 | Is the DemandIntegrationPeriod attribute supported? | [R2]/D.3.2.2.7.3 | MECS1:O | N |  |
| MECS70 | Is the NumberOfDemandSubintervals attribute supported? | [R2]/D.3.2.2.7.4 | MECS1:O | N |  |
| MECS71 | Is the reception of Get Profile command supported? | [R2]/D.3.3.3.1.1 | MECS1:O | N |  |
| MECS72 | Is the reception of Request Mirror Response command supported? | [R2]/D.3.3.3.1.2 | MECS1:O | N |  |
| MECS73 | Is the reception of Mirror Removed command supported? | [R2]/D.3.3.3.1.3 | MECS1:O | N |  |
| MECS74 | Is the generation of Get Profile Response command supported? | [R2]/D.3.2.3.1.1 | MECS1:O | N |  |
| MECS75 | Is the generation of Request Mirror command supported? | [R2]/D.3.2.3.1.2 | MECS1:O | N |  |
| MECS76 | Is the generation of Remove Mirror command supported? | [R2]/D.3.2.3.1.3 | MECS1:O | N |  |
| MECS77 | Is the ProfileIntervalPeriod attribute supported? | [R2]/D.3.2.2.1.16 | MECS1:O | N |  |
| MECS78 | Is the IntervalReadReportingPeriod attribute supported? | [R2]/D.3.2.2.1.17 | MECS1:O | N |  |
| MECS79 | Is the PresetReadingTime attribute supported? | [R2]/D.3.2.2.1.18 | MECS1:O | N |  |
| MECS80 | Is the VolumePerReport attribute supported? | [R2]/D.3.2.2.1.19 | MECS1:O | N |  |
| MECS81 | Is the FlowRestriction attribute supported? | [R2]/D.3.2.2.1.20 | MECS1:O | N |  |
| MECS82 | Is the Supply Status attribute supported? | [R2]/D.3.2.2.1.21 | MECS1:O | Y [Int: EP# 2] |  |
| MECS83 | Is the CurrentDayMaxPressure attribute supported? | [R2]/D.3.2.2.5.10 | MECS1:O | N |  |
| MECS84 | Is the CurrentDayMinPressure attribute supported? | [R2]/D.3.2.2.5.12 | MECS1:O | N |  |
| MECS85 | Is the PreviousDayMaxPressure attribute supported? | [R2]/D.3.2.2.5.11 | MECS1:O | N |  |
| MECS86 | Is the PreviousDayMinPressure attribute supported? | [R2]/D.3.2.2.5.13 | MECS1:O | N |  |
| MECS87 | Is the CurrentDayMaxDemand attribute supported? | [R2]/D.3.2.2.5.14 | MECS1:O | N |  |
| MECS88 | Is the PreviousDayMaxDemand attribute supported? | [R2]/D.3.2.2.5.15 | MECS1:O | N |  |
| MECS89 | Is the Meter Status (Gas) attribute supported? | [R2]/D.3.2.2.3.1 | MECS1:O | Y [Int: EP# 2] |  |
| MECS90 | Is the Meter Status (Water) attribute supported? | [R2]/D.3.2.2.3.1 | MECS1:O | N |  |
| MECS91 | Is the RemainingBatteryLife attribute supported? | [R2]/D.3.2.2.3.2 | MECS1:O | N |  |
| MECS93 | Is the CurrentInletEnergyCarrierSummation attribute supported? | [R2]/D.3.2.2.1.22 | MECS54e:M | N |  |
|  |  |  | MECS54f:M MECS1:O |  |  |
| MECS94 | Is the CurrentOutletEnergyCarrierSummation attribute supported? | [R2]/D.3.2.2.1.23 | MECS1:O | N |  |
| MECS95 | Is the InletTemperature attribute supported? | [R2]/D.3.2.2.1.24 | MECS54e:M | N |  |
|  |  |  | MECS54f:M MECS1:O |  |  |
| MECS96 | Is the OutletTemperature attribute supported? | [R2]/D.3.2.2.1.25 | MECS54e:M | N |  |
|  |  |  | MECS54f:M MECS1:O |  |  |
| MECS97 | Is the ControlTemperature attribute supported? | [R2]/D.3.2.2.1.26 | MECS1:O | N |  |
| MECS98 | Is the CurrentInletEnergyCarrierDemand attribute supported? | [R2]/D.3.2.2.1.27 | MECS1:O | N |  |
| MECS99 | Is the CurrentOutletEnergyCarrierDemand attribute supported? | [R2]/D.3.2.2.1.28 | MECS1:O | N |  |
| MECS100 | Is the EnergyCarrierUnitOfMeasure attribute supported? | [R2]/D.3.2.2.4.10 | MECS54e:M | N |  |
|  |  |  | MECS54f:M MECS1:O |  |  |
| MECS101 | Is the EnergyCarrierSummationFormatting attribute supported? | [R2]/D.3.2.2.4.11 | MECS93:M | N |  |
|  |  |  | MECS94:M |  |  |
| MECS102 | Is the EnergyCarrierDemandFormatting attribute supported? | [R2]/D.3.2.2.4.12 | MECS98:M | N |  |
|  |  |  | MECS99:M |  |  |
|  |  |  | MECS107:M |  |  |
|  |  |  | MECS108:M |  |  |
|  |  |  | MECS109:M |  |  |
|  |  |  | MECS110:M |  |  |
|  |  |  | MECS111:M |  |  |
|  |  |  | MECS112:M |  |  |
| MECS103 | Is the TemperatureUnitOfMeasure attribute supported? | [R2]/D.3.2.2.4.13 | MECS54e:M | N |  |
|  |  |  | MECS54f:M |  |  |
| MECS104 | Is the TemperatureFormatting attribute supported? | [R2]/D.3.2.2.4.14 | MECS54e:M | N |  |
|  |  |  | MECS54f:M |  |  |
| MECS105 | Is the CurrentMonthMaxDemand attribute supported? | [R2]/D.3.2.2.5.16 | MECS1:O | N |  |
| MECS106 | Is the CurrentYearMaxDemand attribute supported? | [R2]/D.3.2.2.5.17 | MECS1:O | N |  |
| MECS107 | Is the CurrentDayMaxEnergyCarrierDemand attribute supported? | [R2]/D.3.2.2.5.18 | MECS1:O | N |  |
| MECS108 | Is the PreviousDayMaxEnergyCarrierDemand attribute supported? | [R2]/D.3.2.2.5.19 | MECS1:O | N |  |
| MECS109 | Is the CurrentMonthMaxEnergyCarrierDemand attribute supported? | [R2]/D.3.2.2.5.20 | MECS1:O | N |  |
| MECS110 | Is the CurrentMonthMinEnergyCarrierDemand attribute supported? | [R2]/D.3.2.2.5.21 | MECS1:O | N |  |
| MECS111 | Is the CurrentYearMaxEnergyCarrierDemand attribute supported? | [R2]/D.3.2.2.5.22 | MECS1:O | N |  |
| MECS112 | Is the CurrentYearMinEnergyCarrierDemand attribute supported? | [R2]/D.3.2.2.5.23 | MECS1:O | N |  |
| MECS113 | Is the HoursInOperation attribute supported? | [R2]/D.3.2.2.3.3 | MECS54e:M | N |  |
|  |  |  | MECS54f:M |  |  |
| MECS114 | Is the HoursInFault attribute supported? | [R2]/D.3.2.2.3.4 | MECS1:O | N |  |
| MECS115 | Is the Generic AlarmMask attribute supported? | [R2]/D.3.2.2.9.2 | MECS1:O | N |  |
| MECS116 | Is the Electricity AlarmMask attribute supported? | [R2]/D.3.2.2.9.2 | MECS1:O | N |  |
| MECS117 | Is the GenericFlow/Pressure AlarmMask attribute supported? | [R2]/D.3.2.2.9.2 | MECS1:O | N |  |
| MECS118 | Is the Water Specific AlarmMask attribute supported? | [R2]/D.3.2.2.9.2 | MECS1:O | N |  |
| MECS119 | Is the Heating Specific AlarmMask attribute supported? | [R2]/D.3.2.2.9.2 | MECS1:O | N |  |
| MECS120 | Is the Cooling Specific AlarmMask attribute supported? | [R2]/D.3.2.2.9.2 | MECS1:O | N |  |
| MECS121 | Is the Gas Specific AlarmMask attribute supported? | [R2]/D.3.2.2.9.2 | MECS1:O | N |  |
| MECS122 | Is the reception of Request Fast Poll Mode command supported? | [R2]/D.3.3.3.1.4 | MECS1:O | N |  |
| MECS123 | Is the generation of Request Fast Poll Mode Response supported? | [R2]/D.3.2.3.1.4 | MECS1:O | N |  |
| MECS124 | Is the Mapping of the Status Attribute (Electricity) supported? | [R2]/D.3.2.2.3.1 Table D.16 | MECS54a:M | N |  |
| MECS125 | Is the Meter Status Attribute (Gas) mapping supported? | [R2]/D.3.2.2.3.1 Table D.17 | MECS54b:M | Y [Int: EP# 2] |  |
| MECS126 | Is the Meter Status Attribute (Water) mapping supported? | [R2]/D.3.2.2.3.1 Table D.18 | MECS54c:M | N |  |
| MECS127 | RESERVED |  |  | NA |  |
| MECS128 | Is the Meter Status Attribute (Heat and Cooling) mapping? | [R2]/D.3.2.2.3.1 Table D.19 | MECS54e:M MECS54f:M | N |  |
| MECS129 | RESERVED |  |  | NA |  |
| MECS130 | Does the device generate fragmented Get Profile Response commands? |  | MECS74:O | N |  |
| MECS131 | Is the PreviousBlockPeriodConsumptionDelivered attribute supported? | [R2]/D.3.2.2.1.29 | MECS132:OMECS133:O | N |  |
| MECS132 | Does the device support Block Charging only? | [R2]/D.4.4.3.2 | MECS1:O | Y [Int: EP# 2] |  |
| MECS133 | Does the device support Block/TOU Combination Charging? | [R2]/D.4.4.3.3 | MECS1:O | Y [Int: EP# 2] |  |
| MECS134 | Are any Block Information ‘No Tier’ attributes (0x00 to 0x0F) supported? | [R2]/D.3.2.2.8 | MECS132:M | Y [Int: EP# 2] |  |
| MECS135 | Are any Block Information ‘TierxBlocky’ attributes (0x10 to 0xFF) supported | [R2]/D.3.2.2.8 | MECS133:O | N |  |
| MECS136 | Is the CurrentBlockPeriodConsumptionReceived attribute supported? | [R2]/D.3.2.2.1.30 | MECS1:O | N |  |
| MECS137 | Is the CurrentBlockReceived attribute supported? | [R2]/D.3.2.2.1.31 | MECS1:O | N |  |
| MECS138 | Is the DFTSummationReceived attribute supported? | [R2]/D.3.2.2.1.32 | MECS1:O | N |  |
| MECS139 | Is the ActiveRegisterTierDelivered attribute supported? | [R2]/D.3.2.2.1.33 | MECS1:O | N |  |
| MECS140 | Is the ActiveRegisterTierReceived attribute supported? | [R2]/D.3.2.2.1.34 | MECS1:O | N |  |
| MECS141 | Is the LastBlockSwitchTime attribute supported? | [R2]/D.3.2.2.1.35 | MECS1:O | N |  |
| MECS142 | Is the CurrentTier16SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS143 | Is the CurrentTier16SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS144 | Is the CurrentTier17SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS145 | Is the CurrentTier17SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS146 | Is the CurrentTier18SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS147 | Is the CurrentTier18SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS148 | Is the CurrentTier19SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS149 | Is the CurrentTier19SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS150 | Is the CurrentTier20SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS151 | Is the CurrentTier20SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS152 | Is the CurrentTier21SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS153 | Is the CurrentTier21SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS154 | Is the CurrentTier22SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS155 | Is the CurrentTier22SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS156 | Is the CurrentTier23SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS157 | Is the CurrentTier23SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS158 | Is the CurrentTier24SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS159 | Is the CurrentTier24SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS160 | Is the CurrentTier25SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS161 | Is the CurrentTier25SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS162 | Is the CurrentTier26SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS163 | Is the CurrentTier26SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS164 | Is the CurrentTier27SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS165 | Is the CurrentTier27SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS166 | Is the CurrentTier28SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS167 | Is the CurrentTier28SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS168 | Is the CurrentTier29SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS169 | Is the CurrentTier29SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS170 | Is the CurrentTier30SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS171 | Is the CurrentTier30SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS172 | Is the CurrentTier31SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS173 | Is the CurrentTier31SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS174 | Is the CurrentTier32SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS175 | Is the CurrentTier32SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS176 | Is the CurrentTier33SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS177 | Is the CurrentTier33SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS178 | Is the CurrentTier34SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS179 | Is the CurrentTier34SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS180 | Is the CurrentTier35SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS181 | Is the CurrentTier35SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS182 | Is the CurrentTier36SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS183 | Is the CurrentTier36SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS184 | Is the CurrentTier37SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS185 | Is the CurrentTier37SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS186 | Is the CurrentTier38SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS187 | Is the CurrentTier38SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS188 | Is the CurrentTier39SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS189 | Is the CurrentTier39SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS190 | Is the CurrentTier40SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS191 | Is the CurrentTier40SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS192 | Is the CurrentTier41SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS193 | Is the CurrentTier41SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS194 | Is the CurrentTier42SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS195 | Is the CurrentTier42SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS196 | Is the CurrentTier43SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS197 | Is the CurrentTier43SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS198 | Is the CurrentTier44SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS199 | Is the CurrentTier44SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS200 | Is the CurrentTier45SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS201 | Is the CurrentTier45SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS202 | Is the CurrentTier46SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS203 | Is the CurrentTier46SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS204 | Is the CurrentTier47SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS205 | Is the CurrentTier47SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS206 | Is the CurrentTier48SummationDelivered attribute supported? | [R2]/D.3.2.2.2.1 | MECS1:O | N |  |
| MECS207 | Is the CurrentTier48SummationReceived attribute supported? | [R2]/D.3.2.2.2.2 | MECS1:O | N |  |
| MECS208 | Is the CPP1SummationDelivered attribute supported? | [R2]/D.3.2.2.2.3 | MECS1:O | N |  |
| MECS209 | Is the CPP2SummationDelivered attribute supported? | [R2]/D.3.2.2.2.4 | MECS1:O | N |  |
| MECS210 | Is the Extended Status attribute supported? | [R2]/D.3.2.2.3.5 | MECS1:M | N |  |
| MECS211 | Is the RemainingBatteryLifeinDays attribute supported? | [R2]/D.3.2.2.3.6 | MECS1:O | N |  |
| MECS212 | Is the CurrentMeterID attribute supported? | [R2]/D.3.2.2.3.7 | MECS1:O | N |  |
| MECS213 | Is the AmbientConsumptionIndicator attribute supported? | [R2]/D.3.2.2.3.8 | MECS1:O | N |  |
| MECS214 | Is the ModuleSerialNumber attribute supported? | [R2]/D.3.2.2.4.15 | MECS1:O | N |  |
| MECS215 | Is the OperatingTariffLabelDelivered attribute supported? | [R2]/D.3.2.2.4.16 | MECS1:O | N |  |
| MECS216 | Is the OperatingTariffLabelReceived attribute supported? | [R2]/D.3.2.2.4.17 | MECS1:O | N |  |
| MECS217 | Is the PreviousDay2ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.24 | MECS1:O | N |  |
| MECS218 | Is the PreviousDay2ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.25 | MECS1:O | N |  |
| MECS219 | Is the PreviousDay3ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.24 | MECS1:O | N |  |
| MECS220 | Is the PreviousDay3ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.25 | MECS1:O | N |  |
| MECS221 | Is the PreviousDay4ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.24 | MECS1:O | N |  |
| MECS222 | Is the PreviousDay4ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.25 | MECS1:O | N |  |
| MECS223 | Is the PreviousDay5ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.24 | MECS1:O | N |  |
| MECS224 | Is the PreviousDay5ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.25 | MECS1:O | N |  |
| MECS225 | Is the PreviousDay6ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.24 | MECS1:O | N |  |
| MECS226 | Is the PreviousDay6ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.25 | MECS1:O | N |  |
| MECS227 | Is the PreviousDay7ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.24 | MECS1:O | N |  |
| MECS228 | Is the PreviousDay7ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.25 | MECS1:O | N |  |
| MECS229 | Is the PreviousDay8ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.24 | MECS1:O | N |  |
| MECS230 | Is the PreviousDay8ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.25 | MECS1:O | N |  |
| MECS231 | Is the CurrentWeekConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.26 | MECS1:O | N |  |
| MECS232 | Is the CurrentWeekConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.27 | MECS1:O | N |  |
| MECS233 | Is the PreviousWeekConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.28 | MECS1:O | N |  |
| MECS234 | Is the PreviousWeekConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.29 | MECS1:O | N |  |
| MECS235 | Is the PreviousWeek2ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.28 | MECS1:O | N |  |
| MECS236 | Is the PreviousWeek2ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.29 | MECS1:O | N |  |
| MECS237 | Is the PreviousWeek3ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.28 | MECS1:O | N |  |
| MECS238 | Is the PreviousWeek3ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.29 | MECS1:O | N |  |
| MECS239 | Is the PreviousWeek4ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.28 | MECS1:O | N |  |
| MECS240 | Is the PreviousWeek4ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.29 | MECS1:O | N |  |
| MECS241 | Is the PreviousWeek5ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.28 | MECS1:O | N |  |
| MECS242 | Is the PreviousWeek5ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.29 | MECS1:O | N |  |
| MECS243 | Is the CurrentMonthConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.30 | MECS1:O | N |  |
| MECS244 | Is the CurrentMonthConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.31 | MECS1:O | N |  |
| MECS245 | Is the PreviousMonthConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS246 | Is the PreviousMonthConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS247 | Is the PreviousMonth2ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS248 | Is the PreviousMonth2ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS249 | Is the PreviousMonth3ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS250 | Is the PreviousMonth3ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS251 | Is the PreviousMonth4ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS252 | Is the PreviousMonth4ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS253 | Is the PreviousMonth5ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS254 | Is the PreviousMonth5ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS255 | Is the PreviousMonth6ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS256 | Is the PreviousMonth6ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS257 | Is the PreviousMonth7ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS258 | Is the PreviousMonth7ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS259 | Is the PreviousMonth8ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS260 | Is the PreviousMonth8ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS261 | Is the PreviousMonth9ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS262 | Is the PreviousMonth9ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS263 | Is the PreviousMonth10ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS264 | Is the PreviousMonth10ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS265 | Is the PreviousMonth11ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS266 | Is the PreviousMonth11ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS267 | Is the PreviousMonth12ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS268 | Is the PreviousMonth12ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS269 | Is the PreviousMonth13ConsumptionDelivered attribute supported? | [R2]/D.3.2.2.5.32 | MECS1:O | N |  |
| MECS270 | Is the PreviousMonth13ConsumptionReceived attribute supported? | [R2]/D.3.2.2.5.33 | MECS1:O | N |  |
| MECS271 | Is the HistoricalFreezeTime attribute supported? | [R2]/D.3.2.2.5.34 | MECS1:O | N |  |
| MECS272 | Is the DemandLimitArm Duration (in minutes) attribute supported? | [R2]/D.3.2.2.7.5 | MECS1:O | N |  |
| MECS273 | Is the LoadLimitSupplyState attribute supported? | [R2]/D.3.2.2.7.6 | MECS1:O | N |  |
| MECS274 | Is the LoadLimitCounter attribute supported? | [R2]/D.3.2.2.7.7 | MECS1:O | N |  |
| MECS275 | Is the SupplyTamperState attribute supported? | [R2]/D.3.2.2.7.8 | MECS1:O | N |  |
| MECS276 | Is the SupplyDepletionState attribute supported? | [R2]/D.3.2.2.7.9 | MECS1:O | N |  |
| MECS277 | Is the SupplyUncontrolled FlowState attribute supported? | [R2]/D.3.2.2.7.10 | MECS1:O | N |  |
| MECS278 | Is the Extended Generic AlarmMask attribute supported? | [R2]/D.3.2.2.9.2 | MECS1:O | N |  |
| MECS279 | Are any Block Information ‘No Tier’ Received attributes (0x00 to 0x0F) supported? | [R2]/D.3.2.2.10 | MECS132:M | N |  |
| MECS280 | Are any Block Information ‘TierxBlocky’ Received attributes (0x10 to 0xFF) supported | [R2]/D.3.2.2.10 | MECS133:O | N |  |
| MECS281 | Is the BillToDateDelivered attribute supported? | [R2]/D.3.2.2.11.1 | MECS1:O | Y [Int: EP# 2] |  |
| MECS282 | Is the BillToDateTimeStampDelivered attribute supported? | [R2]/D.3.2.2.11.2 | MECS1:O | N |  |
| MECS283 | Is the ProjectedBillDelivered attribute supported? | [R2]/D.3.2.2.11.3 | MECS1:O | N |  |
| MECS284 | Is the ProjectedBillTimeStampDelivered attribute supported? | [R2]/D.3.2.2.11.4 | MECS1:O | N |  |
| MECS285 | Is the BillDeliveredTrailingDigit attribute supported? | [R2]/D.3.2.2.11.5 | MECS1:O | Y [Int: EP# 2] |  |
| MECS286 | Is the BillToDateReceived attribute supported? | [R2]/D.3.2.2.11.6 | MECS1:O | N |  |
| MECS287 | Is the BillToDateTimeStampReceived attribute supported? | [R2]/D.3.2.2.11.7 | MECS1:O | N |  |
| MECS288 | Is the ProjectedBillReceived attribute supported? | [R2]/D.3.2.2.11.8 | MECS1:O | N |  |
| MECS289 | Is the ProjectedBillTimeStampReceived attribute supported? | [R2]/D.3.2.2.11.9 | MECS1:O | N |  |
| MECS290 | Is the BillReceivedTrailingDigit attribute supported? | [R2]/D.3.2.2.11.10 | MECS1:O | N |  |
| MECS291 | Is the ProposedChangeSupplyImplementationTime attribute supported? | [R2]/D.13.2.2.12.1 | MECS1:O | N |  |
| MECS292 | Is the ProposedChangeSupplyStatus attribute supported? | [R2]/D.13.2.2.12.2 | MECS1:O | N |  |
| MEC293 | Is the Uncontrolled Flow Threshold attribute supported? | [R2]/D.13.2.2.12.3 | MECS1:O | N |  |
| MEC294 | Is the Uncontrolled Flow Threshold Unit of Measure attribute supported? | [R2]/D.13.2.2.12.4 | MECS1:O | N |  |
| MEC295 | Is the Uncontrolled Flow Multiplier attribute supported? | [R2]/D.13.2.2.12.5 | MECS1:O | N |  |
| MEC296 | Is the Uncontrolled Flow Divisor attribute supported? | [R2]/D.13.2.2.12.6 | MECS1:O | N |  |
| MEC297 | Is the Flow Stabilisation Period attribute supported? | [R2]/D.13.2.2.12.7 | MECS1:O | N |  |
| MEC298 | Is the Flow Measurement Period attribute supported? | [R2]/D.13.2.2.12.8 | MECS1:O | N |  |
| MECS299 | Is the reception of ScheduleSnapShot command supported? | [R2]/D.3.3.3.1.5 | MECS1:O | N |  |
| MECS300 | Is the reception of TakeSnapshot command supported? | [R2]/D.3.3.3.1.6 | MECS1:O | N |  |
| MECS301 | Is the reception of GetSnapshot command supported? | [R2]/D.3.3.3.1.7 | MECS1:O | N |  |
| MECS302 | Is the reception of StartSampling command supported? | [R2]/D.3.3.3.1.8 | MECS1:O | N |  |
| MECS303 | Is the reception of GetSampledData command supported? | [R2]/D.3.3.3.1.9 | MECS1:O | Y [Int: EP# 2] |  |
| MECS304 | Is the reception of MirrorReportAttributeResponse command supported? | [R2]/D.3.3.3.1.10 | MECS1:O | N |  |
| MECS305 | Is the reception of ResetLoad Limit Counter command supported? | [R2]/D.3.3.3.1.11 | MECS1:O | N |  |
| MECS306 | Is the generation of ScheduleSnapShotResponse command supported? | [R2]/D.3.2.3.1.5 | MECS1:O | N |  |
| MECS307 | Is the generation of TakeSnapshotResponse command supported? | [R2]/D.3.2.3.1.6 | MECS1:O | N |  |
| MECS308 | Is the generation of Publish Snapshot command supported? | [R2]/D.3.2.3.1.7 | MECS1:O | N |  |
| MECS309 | Is the generation of GetSampledDataResponse command supported? | [R2]/D.3.2.3.1.8 | MECS1:O | Y [Int: EP# 2] |  |
| MECS310 | Is the generation of ConfigureMirror command supported? | [R2]/D.3.2.3.1.9 | MECS1:O | N |  |
| MECS311 | Is the generation of ConfigureNotificationScheme command supported? | [R2]/D.3.2.3.1.10 | MECS1:O | N |  |
| MECS312 | Is the generation of ConfigureNotificationFlags command supported? | [R2]/D.3.2.3.1.11 | MECS1:O | N |  |
| MECS313 | Is the generation of GetNotificationFlag command supported? | [R2]/D.3.2.3.1.12 | MECS1:O | N |  |
| MECS314 | Is the generation of Supply Status Response command supported? | [R2]/D.3.2.3.1.13 | MECS1:O | N |  |
| MECC1 | Is the Metering Cluster supported as a client? | [R2]/D.3 | O | Y [Int: EP# 2,3] | Smart Energy Application Specific Cluster function capabilities. Metering cluster client capabilities |
| MECC2 | Is the reception of Get Profile Response command supported? | [R2]/D.3.2.3.1.1 | MECC1:O | N |  |
| MECC3 | Is the reception of Request Mirror command supported? | [R2]/D.3.2.3.1.2 | MECC1:O | Y [Int: EP# 3] |  |
| MECC4 | Is the reception of Remove Mirror command supported? | [R2]/D.3.2.3.1.3 | MECC1:O | N |  |
| MECC5 | Is the generation of Get Profile command supported? | [R2]/D.3.3.3.1.1 | MECC1:O | N |  |
| MECC6 | Is the generation of Request Mirror Response command supported? | [R2]/D.3.3.3.1.2 | MECC1:O | Y [Int: EP# 3] |  |
| MECC7 | Is the generation of Mirror Removed command supported? | [R2]/D.3.3.3.1.3 | MECC1:O | N |  |
| MECC8 | Is the reception of Request Fast Poll Mode Response command supported? | [R2]/D.3.2.3.1.4 | MECC1:O | N |  |
| MECC9 | Is the generation of Request Fast Poll Mode command supported? | [R2]/D.3.3.3.1.4 | MECC1:O | N |  |
| MECC10 | Does the device support reception of fragmented Get Profile Response commands? |  | MECC5:M | N |  |
| MECC11 | Is the FunctionalNotificationFlags attribute supported? | [R2]/D.3.3.2.1.1 | MECC1:O | Y [Int: EP# 2] |  |
| MECC12 | Is the NotificationFlags2 attribute supported? | [R2]/D.3.3.2.1.2 | MECC1:O | Y [Int: EP# 2] |  |
| MECC13 | Is the NotificationFlags3 attribute supported? | [R2]/D.3.3.2.1.2 | MECC1:O | Y [Int: EP# 2] |  |
| MECC14 | Is the NotificationFlags4 attribute supported? | [R2]/D.3.3.2.1.2 | MECC1:O | Y [Int: EP# 2] |  |
| MECC15 | Is the NotificationFlags5 attribute supported? | [R2]/D.3.3.2.1.2 | MECC1:O | Y [Int: EP# 2] |  |
| MECC16 | Is the NotificationFlags6 attribute supported? | [R2]/D.3.3.2.1.2 | MECC1:O | N |  |
| MECC17 | Is the NotificationFlags7 attribute supported? | [R2]/D.3.3.2.1.2 | MECC1:O | N |  |
| MECC18 | Is the NotificationFlags8 attribute supported? | [R2]/D.3.3.2.1.2 | MECC1:O | N |  |
| MECC19 | Is the ReportProfile attribute supported? | [R2]/D.3.3.2.2.1 | MECC1:O | N |  |
| MECC20 | Is the MirrorReporting attribute supported? | [R2]/D.3.3.2.2.2 | MECC1:O | N |  |
| MECC21 | Is the NotificationScheme attribute supported? | [R2]/D.3.3.2.2.3 | MECC1:O | N |  |
| MECC22 | Is the reception of ScheduleSnapShotResponse command supported? | [R2]/D.3.2.3.1.5 | MECC1:O | N |  |
| MECC23 | Is the reception of TakeSnapshotResponse command supported? | [R2]/D.3.2.3.1.6 | MECC1:O | N |  |
| MECC24 | Is the reception of Publish Snapshot command supported? | [R2]/D.3.2.3.1.7 | MECC1:O | Y [Int: EP# 2] |  |
| MECC25 | Is the reception of GetSampledDataResponse command supported? | [R2]/D.3.2.3.1.8 | MECC1:O | Y [Int: EP# 2] |  |
| MECC26 | Is the reception of ConfigureMirror command supported? | [R2]/D.3.2.3.1.9 | MECC1:O | Y [Int: EP# 2] |  |
| MECC27 | Is the reception of ConfigureNotificationScheme command supported? | [R2]/D.3.2.3.1.10 | MECC1:O | N |  |
| MECC28 | Is the reception of ConfigureNotificationFlags command supported? | [R2]/D.3.2.3.1.11 | MECC1:O | N |  |
| MECC29 | Is the reception of GetNotificationFlag command supported? | [R2]/D.3.2.3.1.12 | MECC1:O | N |  |
| MECC30 | Is the generation of ScheduleSnapShot command supported? | [R2]/D.3.3.3.1.5 | MECC1:O | N |  |
| MECC31 | Is the generation of TakeSnapshot command supported? | [R2]/D.3.3.3.1.6 | MECC1:O | N |  |
| MECC32 | Is the generation of GetSnapshot command supported? | [R2]/D.3.3.3.1.7 | MECC1:O | Y [Int: EP# 2] |  |
| MECC33 | Is the generation of StartSampling command supported? | [R2]/D.3.3.3.1.8 | MECC1:O | N |  |
| MECC34 | Is the generation of GetSampledData command supported? | [R2]/D.3.3.3.1.9 | MECC1:O | Y [Int: EP# 2] |  |
| MECC35 | Is the generation of MirrorReportAttributeResponse command supported? | [R2]/D.3.3.3.1.10 | MECC1:O | N |  |
| MECC36 | Is the generation of ResetLoadLimitCounter command supported? | [R2]/D.3.3.3.1.11 | MECC1:O | N |  |
| MECC37 | Is the generation of Change Supply command supported? | [R2]/D.3.3.3.1.12 | MECC1:O | N |  |
| MECC38 | Is the generation of Local Change Supply command supported? | [R2]/D.3.3.3.1.13 | MECC1:O | N |  |
| MECC39 | Is the generation of SetSupplyStatus command supported? | [R2]/D.3.3.3.1.14 | MECC1:O | N |  |
| MECC40 | Is the generation of SetUncontrolledFlowThreshold command supported? | [R2]/D.3.3.3.1.15 | MECC1:O | N |  |
| PCS1 | Is the Price Cluster supported as a server? | [R2]/D.4 | O | Y [Int: EP# 3] | Smart Energy Application Specific Cluster function capabilities. Price cluster server capabilities |
| PCS2 | Is the Tier1PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS3 | Is the Tier2PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS4 | Is the Tier3PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS5 | Is the Tier4PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS6 | Is the Tier5PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS7 | Is the Tier6PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS8 | Is the reception of Get Current Price command supported? | [R2]/D.4.2.3.2 | PCS1:M | Y [Int: EP# 3] |  |
| PCS9 | Is the reception of Get Scheduled Prices command supported? | [R2]/D.4.2.3.3 | PCS1:O | N |  |
| PCS10 | Is the generation of Publish Price command supported? | [R2]/D.4.2.4.1 | PCS1:M | Y [Int: EP# 3] |  |
| PCS11 | Is the Tier7PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS12 | Is the Tier8PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS13 | Is the Tier9PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS14 | Is the Tier10PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS15 | Is the Tier11PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS16 | Is the Tier12PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS17 | Is the Tier13PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS18 | Is the Tier14PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS19 | Is the Tier15PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS20 | Are any Block Threshold attributes 0x0100 to 0x010F supported? | [R2]/D.4.2.2.2.1 | PCS42:M | Y [Int: EP# 3] |  |
|  |  |  | PCS43:M |  |  |
| PCS25 | Is the reception of Price Acknowledgement command supported? | [R2]/D.4.2.3.4 | PCS1:O | Y [Int: EP# 3] |  |
| PCS26 | Is the generation of Publish Block Period command supported? | [R2]/D.4.2.4.2 | PCS42:O | N |  |
|  |  |  | PCS43:O |  |  |
| PCS27 | Is the reception of Get Block Period(s) command support? | [R2]/D.4.2.3.5 | PCS42:O | N |  |
|  |  |  | PCS43:O |  |  |
| PCS28 | Is the Commodity Type (server) attribute supported? | [R2]/D.4.2.2.4.1 | PCS1:O | Y [Int: EP# 3] |  |
| PCS29 | Is the Standing Charge attribute supported? | [R2]/D.4.2.2.4.2 | PCS1:O | N |  |
| PCS30 | Is the ConversionFactor attribute supported? | [R2]/D.4.2.2.4.3 | PCS1:O | Y [Int: EP# 3] |  |
| PCS31 | Is the ConversionFactorTrailingDigit supported? | [R2]/D.4.2.2.4.4 | PCS1:O | Y [Int: EP# 3] |  |
| PCS32 | Is the CalorificValue attribute supported? | [R2]/D.4.2.2.4.5 | PCS1:O | Y [Int: EP# 3] |  |
| PCS33 | Is the CalorificValueUnit attribute supported? | [R2]/D.4.2.2.4.6 | PCS1:O | Y [Int: EP# 3] |  |
| PCS34 | Is the CalorificValueTrailingDigit attribute supported? | [R2]/D.4.2.2.4.7 | PCS1:O | Y [Int: EP# 3] |  |
| PCS36 | Is the reception of the GetConversionFactor command supported? | [R2]/D.4.2.3.6 | PCS1:O | N |  |
| PCS37 | Is the reception of the GetCalorificValue command supported? | [R2]/D.4.2.3.7 | PCS1:O | N |  |
| PCS38 | Is the generation of the Publish Conversion Factor command supported? | [R2]/D.4.2.4.3 | PCS1:O | N |  |
| PCS39 | Is the generation of the Publish Calorific Value command supported? | [R2]/D.4.2.4.4 | PCS1:O | N |  |
| PCS40 | Is the CurrentBillingPeriodStart attribute supported? | [R2]/D.4.2.2.8.1 | PCS1:O | N |  |
| PCS41 | Is the CurrentBillingPeriodDuration attribute supported? | [R2]/D.4.2.2.8.2 | PCS1:O | N |  |
| PCS42 | Does the device support Block Charging only? | [R2]/D.4.4.3.2 | PCS1:O | Y [Int: EP# 3] |  |
| PCS43 | Does the device support Block/TOU Combination Charging ? | [R2]/D.4.4.3.3 | PCS1:O | Y [Int: EP# 3] |  |
| PCS44 | Is the Block Period (Delivered) attribute set supported? | [R2]/D.4.2.2.3 | PCS42:O PCS43:O | Y [Int: EP# 3] |  |
| PCS45 | Are any Block Price Information (Delivered) ‘No Tier’ attributes (0x0400 to 0x040F) supported? | [R2]/D.4.2.2.5 | PCS42:M | Y [Int: EP# 3] |  |
| PCS46 | Are any Block Price Information (Delivered) ‘TierxBlocky’ attributes (0x0410 to 0x04FF) supported? | [R2]/D.4.2.2.5 | PCS43:O | Y [Int: EP# 3] |  |
| PCS47 | Is the Tier16PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS48 | Is the Tier17PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS49 | Is the Tier18PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS50 | Is the Tier19PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS51 | Is the Tier20PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS52 | Is the Tier21PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS53 | Is the Tier22PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS54 | Is the Tier23PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS55 | Is the Tier24PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS56 | Is the Tier25PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS57 | Is the Tier26PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS58 | Is the Tier27PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS59 | Is the Tier28PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS60 | Is the Tier29PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS61 | Is the Tier30PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS62 | Is the Tier31PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS63 | Is the Tier32PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS64 | Is the Tier33PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS65 | Is the Tier34PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS66 | Is the Tier35PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS67 | Is the Tier36PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS68 | Is the Tier37PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS69 | Is the Tier38PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS70 | Is the Tier39PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS71 | Is the Tier40PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS72 | Is the Tier41PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS73 | Is the Tier42PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS74 | Is the Tier43PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS75 | Is the Tier44PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS76 | Is the Tier45PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS77 | Is the Tier46PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS78 | Is the Tier47PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS79 | Is the Tier48PriceLabel attribute supported? | [R2]/D.4.2.2.1 | PCS1:O | N |  |
| PCS80 | Is the BlockThresholdCount attribute supported? | [R2]/D.4.2.2.2.2 | PCS1:O | N |  |
| PCS81 | Are any TierNBlockMThreshold attributes supported? | [R2]/D.4.2.2.2.3 | PCS43:O | N |  |
| PCS82 | Are any TierNBlockThresholdCount attributes supported? | [R2]/D.4.2.2.2.4 | PCS43:O | N |  |
| PCS83 | Are any PriceTierN attributes supported? | [R2]/D.4.2.2.6.1 | PCS1:O | N |  |
| PCS84 | Is the CPP1 Price attribute supported? | [R2]/D.4.2.2.6.2 | PCS1:O | N |  |
| PCS85 | Is the CPP2 Price attribute supported? | [R2]/D.4.2.2.6.3 | PCS1:O | N |  |
| PCS86 | Is the TariffLabel attribute supported? | [R2]/D.4.2.2.7.1 | PCS1:O | N |  |
| PCS87 | Is the NumberofPriceTiersInUse attribute supported? | [R2]/D.4.2.2.7.2 | PCS1:O | N |  |
| PCS88 | Is the NumberofBlockThresholdsInUse attribute supported? | [R2]/D.4.2.2.7.3 | PCS1:O | Y [Int: EP# 3] |  |
| PCS89 | Is the TierBlockMode attribute supported? | [R2]/D.4.2.2.7.4 | PCS1:O | N |  |
| PCS90 | Is the Unit of Measure attribute supported? | [R2]/D.4.2.2.7.5 | PCS1:O | Y [Int: EP# 3] |  |
| PCS91 | Is the Currency attribute supported? | [R2]/D.4.2.2.7.6 | PCS1:O | Y [Int: EP# 3] |  |
| PCS92 | Is the Price Trailing Digit attribute supported? | [R2]/D.4.2.2.7.7 | PCS1:O | Y [Int: EP# 3] |  |
| PCS93 | Is the TariffResolutionPeriod attribute supported? | [R2]/D.4.2.2.7.8 | PCS1:O | N |  |
| PCS94 | Is the CO2 attribute supported? | [R2]/D.4.2.2.7.9 | PCS1:O | N |  |
| PCS95 | Is the CO2Unit attribute supported? | [R2]/D.4.2.2.7.10 | PCS1:O | N |  |
| PCS96 | Is the CO2TrailingDigit attribute supported? | [R2]/D.4.2.2.7.11 | PCS1:O | N |  |
| PCS97 | Is the LastBillingPeriodStart attribute supported? | [R2]/D.4.2.2.8.3 | PCS1:O | N |  |
| PCS98 | Is the LastBillingPeriodDuration attribute supported? | [R2]/D.4.2.2.8.4 | PCS1:O | N |  |
| PCS99 | Is the LastBillingPeriodConsolidatedBill attribute supported? | [R2]/D.4.2.2.8.5 | PCS1:O | N |  |
| PCS100 | Is the CreditPaymentDueDate attribute supported? | [R2]/D.4.2.2.9.1 | PCS1:O | N |  |
| PCS101 | Is the CreditPaymentStatus attribute supported? | [R2]/D.4.2.2.9.2 | PCS1:O | N |  |
| PCS102 | Is the CreditPaymentOverDueAmount attribute supported? | [R2]/D.4.2.2.9.3 | PCS1:O | N |  |
| PCS103 | Is the PaymentDiscount attribute supported? | [R2]/D.4.2.2.9.4 | PCS1:O | N |  |
| PCS104 | Is the PaymentDiscountPeriod attribute supported? | [R2]/D.4.2.2.9.5 | PCS1:O | N |  |
| PCS105 | Is the CreditPayment#1 attribute supported? | [R2]/D.4.2.2.9.6 | PCS1:O | N |  |
| PCS106 | Is the CreditPaymentDate#1 attribute supported? | [R2]/D.4.2.2.9.7 | PCS1:O | N |  |
| PCS107 | Is the CreditPaymentRef#1 attribute supported? | [R2]/D.4.2.2.9.8 | PCS1:O | N |  |
| PCS108 | Is the CreditPayment#2 attribute supported? | [R2]/D.4.2.2.9.6 | PCS1:O | N |  |
| PCS109 | Is the CreditPaymentDate#2 attribute supported? | [R2]/D.4.2.2.9.7 | PCS1:O | N |  |
| PCS110 | Is the CreditPaymentRef#2 attribute supported? | [R2]/D.4.2.2.9.8 | PCS1:O | N |  |
| PCS111 | Is the CreditPayment#3 attribute supported? | [R2]/D.4.2.2.9.6 | PCS1:O | N |  |
| PCS112 | Is the CreditPaymentDate#3 attribute supported? | [R2]/D.4.2.2.9.7 | PCS1:O | N |  |
| PCS113 | Is the CreditPaymentRef#3 attribute supported? | [R2]/D.4.2.2.9.8 | PCS1:O | N |  |
| PCS114 | Is the CreditPayment#4 attribute supported? | [R2]/D.4.2.2.9.6 | PCS1:O | N |  |
| PCS115 | Is the CreditPaymentDate#4 attribute supported? | [R2]/D.4.2.2.9.7 | PCS1:O | N |  |
| PCS116 | Is the CreditPaymentRef#4 attribute supported? | [R2]/D.4.2.2.9.8 | PCS1:O | N |  |
| PCS117 | Is the CreditPayment#5 attribute supported? | [R2]/D.4.2.2.9.6 | PCS1:O | N |  |
| PCS118 | Is the CreditPaymentDate#5 attribute supported? | [R2]/D.4.2.2.9.7 | PCS1:O | N |  |
| PCS119 | Is the CreditPaymentRef#5 attribute supported? | [R2]/D.4.2.2.9.8 | PCS1:O | N |  |
| PCS120 | Are any ReceivedTierNPriceLabel attributes supported? | [R2]/D.4.2.2.10 | PCS1:O | N |  |
| PCS121 | Are any ReceivedBlockNThreshold attributes supported? | [R2]/D.4.2.2.11 | PCS42:O | N |  |
|  |  |  | PCS43:O |  |  |
| PCS122 | Is the ReceivedStartofBlockPeriod attribute supported? | [R2]/D.4.2.2.12.1 | PCS1:O | N |  |
| PCS123 | Is the ReceivedBlockPeriodDuration attribute supported? | [R2]/D.4.2.2.12.2 | PCS1:O | N |  |
| PCS124 | Is the ReceivedThresholdMultiplier attribute supported? | [R2]/D.4.2.2.12.3 | PCS1:O | N |  |
| PCS125 | Is the ReceivedThresholdDivisor attribute supported? | [R2]/D.4.2.2.12.4 | PCS1:O | N |  |
| PCS126 | Are any Received Block Price Information ‘RxTierMBlockNPrice’ attributes supported? | [R2]/D.4.2.2.13 | PCS42:O | N |  |
|  |  |  | PCS43:O |  |  |
| PCS127 | Are any ReceivedPriceTierN attributes supported? | [R2]/D.4.2.2.2.14 | PCS1:O | N |  |
| PCS128 | Is the ReceivedTariffLabel attribute supported? | [R2]/D.4.2.2.15.1 | PCS1:O | N |  |
| PCS129 | Is the ReceivedNumberofPriceTiersInUse attribute supported? | [R2]/D.4.2.2.15.2 | PCS1:O | N |  |
| PCS130 | Is the ReceivedNumberofBlockThresholdsInUse attribute supported? | [R2]/D.4.2.2.15.3 | PCS1:O | N |  |
| PCS131 | Is the ReceivedTierBlockMode attribute supported? | [R2]/D.4.2.2.15.4 | PCS1:O | N |  |
| PCS132 | Is the ReceivedTariffResolutionPeriod attribute supported? | [R2]/D.4.2.2.15.5 | PCS1:O | N |  |
| PCS133 | Is the ReceivedCO2 attribute supported? | [R2]/D.4.2.2.15.6 | PCS1:O | N |  |
| PCS134 | Is the ReceivedCO2Unit attribute supported? | [R2]/D.4.2.2.15.7 | PCS1:O | N |  |
| PCS135 | Is the ReceivedCO2TrailingDigit attribute supported? | [R2]/D.4.2.2.15.8 | PCS1:O | N |  |
| PCS136 | Is the ReceivedCurrentBillingPeriodStart attribute supported? | [R2]/D.4.2.2.16.1 | PCS1:O | N |  |
| PCS137 | Is the ReceivedCurrentBillingPeriodDuration attribute supported? | [R2]/D.4.2.2.16.2 | PCS1:O | N |  |
| PCS138 | Is the ReceivedLastBillingPeriodStart attribute supported? | [R2]/D.4.2.2.16.3 | PCS1:O | N |  |
| PCS139 | Is the ReceivedLastBillingPeriodDuration attribute supported? | [R2]/D.4.2.2.16.4 | PCS1:O | N |  |
| PCS140 | Is the ReceivedLastBillingPeriodConsolidatedBill attribute supported? | [R2]/D.4.2.2.16.5 | PCS1:O | N |  |
| PCS141 | Is the reception of the GetTariffInformation command supported? | [R2]/D.4.2.3.8 | PCS1:O | Y [Int: EP# 3] |  |
| PCS142 | Is the reception of the GetPriceMatrix command supported? | [R2]/D.4.2.3.9 | PCS1:O | Y [Int: EP# 3] |  |
| PCS143 | Is the reception of the GetBlockThresholds command supported? | [R2]/D.4.2.3.10 | PCS1:O | Y [Int: EP# 3] |  |
| PCS144 | Is the reception of the GetCO2Value command supported? | [R2]/D.4.2.3.11 | PCS1:O | N |  |
| PCS145 | Is the reception of the GetTierLabels command supported? | [R2]/D.4.2.3.12 | PCS1:O | N |  |
| PCS146 | Is the reception of the GetBillingPeriod command supported? | [R2]/D.4.2.3.13 | PCS1:O | N |  |
| PCS147 | Is the reception of the GetConsolidatedBill command supported? | [R2]/D.4.2.3.14 | PCS1:O | N |  |
| PCS148 | Is the reception of the CPPEventResponse command supported? | [R2]/D.4.2.3.15 | PCS1:O | N |  |
| PCS149 | Is the reception of the GetCreditPayment command supported? | [R2]/D.4.2.3.16 | PCS1:O | N |  |
| PCS150 | Is the reception of the GetCurrencyConversion command supported? | [R2]/D.4.2.3.17 | PCS1:O | N |  |
| PCS151 | Is the reception of the GetTariffCancellation command supported? | [R2]/D.4.2.3.18 | PCS1:O | N |  |
| PCS152 | Is the generation of the PublishTariffInformation command supported? | [R2]/D.4.2.4.5 | PCS1:O | Y [Int: EP# 3] |  |
| PCS153 | Is the generation of the PublishPriceMatrix command supported? | [R2]/D.4.2.4.6 | PCS1:O | Y [Int: EP# 3] |  |
| PCS154 | Is the generation of the PublishBlockThresholds command supported? | [R2]/D.4.2.4.7 | PCS1:O | Y [Int: EP# 3] |  |
| PCS155 | Is the generation of the PublishCO2Value command supported? | [R2]/D.4.2.4.8 | PCS1:O | N |  |
| PCS156 | Is the generation of the PublishTierLabels command supported? | [R2]/D.4.2.4.9 | PCS1:O | N |  |
| PCS157 | Is the generation of the PublishBillingPeriod command supported? | [R2]/D.4.2.4.10 | PCS1:O | N |  |
| PCS158 | Is the generation of the PublishConsolidatedBill command supported? | [R2]/D.4.2.4.11 | PCS1:O | N |  |
| PCS159 | Is the generation of the PublishCPPEvent command supported? | [R2]/D.4.2.4.12 | PCS1:O | N |  |
| PCS160 | Is the generation of the PublishCreditPayment command supported? | [R2]/D.4.2.4.13 | PCS1:O | N |  |
| PCS161 | Is the generation of the PublishCurrencyConversion command supported? | [R2]/D.4.2.4.14 | PCS1:O | N |  |
| PCS162 | Is the generation of the CancelTariff command supported? | [R2]/D.4.2.4.15 | PCS1:O | N |  |
| PCC1 | Is the Price Cluster supported as a client? | [R2]/D.4 | O | N | Smart Energy Application Specific Cluster function capabilities. Price cluster client capabilities |
| PCC2 | Is the reception of Publish Price command supported? | [R2]/D.4.2.4.1 | PCC1:M | NA |  |
| PCC3 | Is the generation of Get Current Price command supported? | [R2]/D.4.2.3.2 | PCC1:M | NA |  |
| PCC4 | Is the generation of Get Scheduled Prices command supported? | [R2]/D.4.2.3.3 | PCC1:O | NA |  |
| PCC5 | Is the PriceIncreaseRandomizeMinutes attribute supported? | [R2]/D.4.3.2.1 | PCC1:O | NA |  |
| PCC6 | Is the PriceDecreaseRandomizeMinutes attribute supported? | [R2]/D.4.3.2.2 | PCC1:O | NA |  |
| PCC7 | Is the Commodity Type (client) attribute supported? | [R2]/D.4.3.2.3 | PCC1:O | NA |  |
| PCC8 | Is the generation of Price Acknowledgement command supported? | [R2]/D.4.2.3.4 | PCC1:O | NA |  |
| PCC9 | Is the reception of Publish Block Period command supported? | [R2]/D.4.2.4.2 | PCC12:O | NA |  |
|  |  |  | PCC13:O |  |  |
| PCC10 | Is the generation of Get Block Period(s) command supported? | [R2]/D.4.2.3.5 | PCC12:O | NA |  |
|  |  |  | PCC13:O |  |  |
| PCC11 | Is the TOU charging behavior supported? | [R2]/D.4.4.3.1 | PCC1:O | NA |  |
| PCC12 | Is the Block Tariffs Block Charging ONLY behavior supported? | [R2]/D.4.4.3.2 | PCC1:O | NA |  |
| PCC13 | Is the Block Tariffs Block/TOU Combination Charging supported? | [R2]/D.4.4.3.3 | PCC1:O | NA |  |
| PCC14 | Is the Block Tariffs guideline for extended non-communication supported? | [R2]/D.4.4.3.4 | PCC12:O | NA |  |
|  |  |  | PCC13:O |  |  |
| PCC15 | Is the Block Tariffs guideline for meter installation or swap-out supported? | [R2]/D.4.4.3.4 | PCC12:O | NA |  |
|  |  |  | PCC13:O |  |  |
| PCC16 | Is the generation of the GetConversionFactor command supported? | [R2]/D.4.2.3.6 | PCC1:O | NA |  |
| PCC17 | Is the generation of the GetCalorificValue command supported? | [R2]/D.4.2.3.7 | PCC1:O | NA |  |
| PCC18 | Is the reception of the Publish Conversion Factor command supported? | [R2]/D.4.2.4.3 | PCC1:O | NA |  |
| PCC19 | Is the reception of the Publish Calorific Value command supported? | [R2]/D.4.2.4.4 | PCC1:O | NA |  |
| PCC20 | Is the reception of the PublishTariffInformation command supported? | [R2]/D.4.2.4.5 | PCC1:O | NA |  |
| PCC21 | Is the reception of the PublishPriceMatrix command supported? | [R2]/D.4.2.4.6 | PCC1:O | NA |  |
| PCC22 | Is the reception of the PublishBlockThresholds command supported? | [R2]/D.4.2.4.7 | PCC1:O | NA |  |
| PCC23 | Is the reception of the PublishCO2Value command supported? | [R2]/D.4.2.4.8 | PCC1:O | NA |  |
| PCC24 | Is the reception of the PublishTierLabels command supported? | [R2]/D.4.2.4.9 | PCC1:O | NA |  |
| PCC25 | Is the reception of the PublishBillingPeriod command supported? | [R2]/D.4.2.4.10 | PCC1:O | NA |  |
| PCC26 | Is the reception of the PublishConsolidatedBill command supported? | [R2]/D.4.2.4.11 | PCC1:O | NA |  |
| PCC27 | Is the reception of the PublishCPPEvent command supported? | [R2]/D.4.2.4.12 | PCC1:O | NA |  |
| PCC28 | Is the reception of the PublishCreditPayment command supported? | [R2]/D.4.2.4.13 | PCC1:O | NA |  |
| PCC29 | Is the reception of the PublishCurrencyConversion command supported? | [R2]/D.4.2.4.14 | PCC1:O | NA |  |
| PCC30 | Is the reception of the CancelTariff command supported? | [R2]/D.4.2.4.15 | PCC1:O | NA |  |
| PCC31 | Is the generation of the GetTariffInformation command supported? | [R2]/D.4.2.3.8 | PCC1:O | NA |  |
| PCC32 | Is the generation of the GetPriceMatrix command supported? | [R2]/D.4.2.3.9 | PCC1:O | NA |  |
| PCC33 | Is the generation of the GetBlockThresholds command supported? | [R2]/D.4.2.3.10 | PCC1:O | NA |  |
| PCC34 | Is the generation of the GetCO2Value command supported? | [R2]/D.4.2.3.11 | PCC1:O | NA |  |
| PCC35 | Is the generation of the GetTierLabels command supported? | [R2]/D.4.2.3.12 | PCC1:O | NA |  |
| PCC36 | Is the generation of the GetBillingPeriod command supported? | [R2]/D.4.2.3.13 | PCC1:O | NA |  |
| PCC37 | Is the generation of the GetConsolidatedBill command supported? | [R2]/D.4.2.3.14 | PCC1:O | NA |  |
| PCC38 | Is the generation of the CPPEventResponse command supported? | [R2]/D.4.2.3.15 | PCC1:O | NA |  |
| PCC39 | Is the generation of the GetCreditPayment command supported? | [R2]/D.4.2.3.16 | PCC1:O | NA |  |
| PCC40 | Is the generation of the GetCurrencyConversion command supported? | [R2]/D.4.2.3.17 | PCC1:O | NA |  |
| PCC41 | Is the generation of the GetTariffCancellation command supported? | [R2]/D.4.2.3.18 | PCC1:O | NA |  |
| MCS1 | Is the Messaging Cluster supported as a server? | [R2]/D.5 | O | Y [Int: EP# 3] | Smart Energy Application Specific Cluster function capabilities. Messaging cluster server capabilities |
| MCS2 | Is the reception of Get Last Message command supported? | [R2]/D.5.3.3.1 | MCS1:M | Y [Int: EP# 3] |  |
| MCS5 | Is the reception of Message Confirmation command supported? | [R2]/D.5.3.3.2 | MCS1:M | Y [Int: EP# 3] |  |
| MCS3 | Is the generation of Display Message command supported? | [R2]/D.5.2.3.1 | MCS1:M | Y [Int: EP# 3] |  |
| MCS4 | Is the generation of Cancel Message command supported? | [R2]/D.5.2.3.2 | MCS1:M | Y [Int: EP# 3] |  |
| MCS5 | Is the generation of Display Protected Message command supported? | [R2]/D.5.2.3.3 | MCS1:O | N |  |
| MCS6 | Is the generation of Cancel All Messages command supported? | [R2]/D.5.2.3.4 | MCS1:O | N |  |
| MCS7 | Is the reception of GetMessageCancellation command supported? | [R2]/D.5.3.3.3 | MCS1:O | N |  |
| MCC1 | Is the Messaging Cluster supported as a client? | [R2]/D.5 | O | N | Smart Energy Application Specific Cluster function capabilities. Messaging cluster client capabilities |
| MCC2 | Is the reception of Display Message command supported? | [R2]/D.5.2.3.1 | MCC1:M | NA |  |
| MCC3 | Is the reception of Cancel Message command supported? | [R2]/D.5.2.3.2 | MCC1:M | NA |  |
| MCC4 | Is the generation of Get Last Message command supported? | [R2]/D.5.3.3.1 | MCC1:M | NA |  |
| MCC5 | Is the generation of Message Confirmation command supported? | [R2]/D.5.3.3.2 | MCC1:M | NA |  |
| MCC6 | Is the reception of Display Protected Message command supported? | [R2]/D.5.2.3.3 | MCC1:O | NA |  |
| MCC7 | Is the reception of Cancel All Messages command supported? | [R2]/D.5.2.3.4 | MCC1:O | NA |  |
| MCC8 | Is the generation of GetMessageCancellation command supported? | [R2]/D.5.3.3.3 | MCC1:M | NA |  |
| TUS1 | Is the Tunneling Cluster supported as a server? | [R2]/D.6 | O | Y [Int: EP# 1] | Smart Energy Application Specific Cluster function capabilities. Tunneling cluster server capabilities |
| TUS2 | Is the reception of RequestTunnel command supported? | [R2]/D.6.2.4.1 | TUS1:M | Y [Int: EP# 1] |  |
| TUS3 | Is the reception of CloseTunnel command supported? | [R2]/D.6.2.4.2 | TUS1:M | Y [Int: EP# 1] |  |
| TUS4 | Is the reception of TransferData command supported? | [R2]/D.6.2.4.3 | TUS1:M | Y [Int: EP# 1] |  |
| TUS5 | Is the reception of TransferDataError command supported? | [R2]/D.6.2.4.4 | TUS1:M | Y [Int: EP# 1] |  |
| TUS6 | Is the reception of AckTransferData command supported? | [R2]/D.6.2.4.5 | TUS1:O | N |  |
| TUS7 | Is the reception of ReadyData command supported? | [R2]/D.6.2.4.6 | TUS1:O | N |  |
| TUS8 | Is the generation of RequestTunnelResponse command supported? | [R2]/D.6.2.5.1 | TUS1:M | Y [Int: EP# 1] |  |
| TUS9 | Is the generation of TransferData command supported? | [R2]/D.6.2.5.2 | TUS1:M | Y [Int: EP# 1] |  |
| TUS10 | Is the generation of TransferDataError command supported? | [R2]/D.6.2.5.3 | TUS1:M | Y [Int: EP# 1] |  |
| TUS11 | Is the generation of AckTransferData command supported? | [R2]/D.6.2.5.4 | TUS1:O | N |  |
| TUS12 | Is the generation of ReadyData command supported? | [R2]/D.6.2.5.5 | TUS1:O | N |  |
| TUS13 | Is the reception of the GetSupportedTunnelProtocols supported? | [R2]/D.6.2.4.7 | TUS1:O | N |  |
| TUS14 | Is the generation of the Supported Tunnel Protocols Response command supported? | [R2]/D.6.2.5.6 | TUS1:O | N |  |
| TUS15 | Is the generation of the TunnelClosureNotification command supported? | [R2]/D.6.2.5.7 | TUS1:O | N |  |
| TUS16 | Is the CloseTunnelTimeout attribute supported? | [R2]/D.6.2.2.1 | TUS1:M | Y [Int: EP# 1] |  |
| TUC1 | Is the Tunneling Cluster supported as a client? | [R2]/D.6 | O | [Y/N] [Int: EP# x] | Smart Energy Application Specific Cluster function capabilities. Tunneling cluster client capabilities |
| TUC2 | Is the reception of RequestTunnelResponse command supported? | [R2]/D.6.3.3 /D.6.2.2.5.1 | TUC1:M | Y [Int: EP# 1] |  |
| TUC3 | Is the reception of TransferData command supported? | [R2]/D.6.3.3 /D.6.2.2.5.2 | TUC1:M | Y [Int: EP# 1] |  |
| TUC4 | Is the reception of TransferDataError command supported? | [R2]/D.6.3.3 /D.6.2.2.5.3 | TUC1:M | Y [Int: EP# 1] |  |
| TUC5 | Is the reception of AckTransferData command supported? | [R2]/D.6.3.3 /D.6.2.2.5.4 | TUC1:O | N |  |
| TUC6 | Is the reception of ReadyData command supported? | [R2]/D.6.3.3 /D.6.2.2.5.5 | TUC1:O | N |  |
| TUC7 | Is the generation of RequestTunnel command supported? | [R2]/D.6.3.4 /D.6.2.2.4.1 | TUC1:M | Y [Int: EP# 1] |  |
| TUC8 | Is the generation of CloseTunnel command supported? | [R2]/D.6.3.4 /D.6.2.2.4.2 | TUC1:M | Y [Int: EP# 1] |  |
| TUC9 | Is the generation of TransferData command supported? | [R2]/D.6.3.4 /D.6.2.2.4.3 | TUC1:M | Y [Int: EP# 1] |  |
| TUC10 | Is the generation of TransferDataError command supported? | [R2]/D.6.3.4 /D.6.2.2.4.4 | TUC1:M | Y [Int: EP# 1] |  |
| TUC11 | Is the generation of AckTransferData command supported? | [R2]/D.6.3.4 /D.6.2.2.4.5 | TUC1:O | N |  |
| TUC12 | Is the generation of ReadyData command supported? | [R2]/D.6.3.4 /D.6.2.2.4.6 | TUC1:O | N |  |
| TUC13 | Is the generation of the GetSupportedTunnelProtocols supported? | [R2]/D.6.2.4 /D.6.2.2.4.7 | TUC1:O | N |  |
| TUC14 | Is the reception of the Supported Tunnel Protocols Response command supported? | [R2]/D.6.3.3 /D.6.2.5.6 | TUC1:O | N |  |
| TUC15 | Is the reception of the TunnelClosureNotification command supported? | [R2] /D.6.3.3 /D.6.2.5.7 | TUC1:O | N |  |
| PPCS1 | Is the Prepayment Cluster supported as a server? | [R2]/D.7 | O | Y [Int: EP# 2] | Smart Energy Application Specific Cluster function capabilities. Prepayment cluster server capabilities |
| PPCS2 | Is the reception of Select Available Emergency Credit command supported? | [R2]/D.7.2.3.1 | PPCS1:O | N |  |
| PPCS3 | RESERVED |  |  | NA |  |
| PPCS4 | RESERVED |  |  | NA |  |
| PPCS7 | Is the PaymentControlConfiguration attribute supported? | [R2]/D.7.2.2.1.1 | PPCS1:M | Y [Int: EP# 2] |  |
| PPCS8 | Is the Credit Remaining attribute supported? | [R2]/D.7.2.2.1.2 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS9 | Is the Emergency Credit Remaining attribute supported? | [R2]/D.7.2.2.1.3 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS10 | Is the Credit Status attribute supported? | [R2]/D.7.2.2.1.4 | PPCS1:O | N |  |
| PPCS11 | Are the Top up Date/Time attributes supported? If so, list supported attributes #1-5. | [R2]/D.7.2.2.2.1 | PPCS1:O | N |  |
| PPCS12 | Are the Top up Amount attributes supported? If so, list supported attributes #1-5. | [R2]/D.7.2.2.2.2 | PPCS1:O | N |  |
| PPCS13 | Are the Originating Device attributes supported? If so, list supported attributes #1-5. | [R2]/D.7.2.2.2.3 | PPCS1:O | N |  |
| PPCS14 | RESERVED |  |  | NA |  |
| PPCS15 | RESERVED |  |  | NA |  |
| PPCS16 | RESERVED |  |  | NA |  |
| PPCS17 | RESERVED |  |  | NA |  |
| PPCS18 | RESERVED |  |  | NA |  |
| PPCS19 | RESERVED |  |  | NA |  |
| PPCS20 | RESERVED |  |  | NA |  |
| PPCS21 | RESERVED |  |  | NA |  |
| PPCS22 | RESERVED |  |  | NA |  |
| PPCS23 | RESERVED |  |  | NA |  |
| PPCS24 | RESERVED |  |  | NA |  |
| PPCS25 | Is the CreditRemainingTimeStamp attribute supported? | [R2]/D.7.2.2.1.5 | PPCS1:O | N |  |
| PPCS26 | Is the AccumulatedDebt attribute supported? | [R2]/D.7.2.2.1.6 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS27 | Is the OverallDebtCap attribute supported? | [R2]/D.7.2.2.1.7 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS28 | Is the EmergencyCredit Limit/Allowance attribute supported? | [R2]/D.7.2.2.1.8 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS29 | Is the EmergencyCredit Threshold attribute supported? | [R2]/D.7.2.2.1.9 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS30 | Is the TotalCreditAdded attribute supported? | [R2]/D.7.2.2.1.10 | PPCS1:O | N |  |
| PPCS31 | Is the MaxCreditLimit attribute supported? | [R2]/D.7.2.2.1.11 | PPCS1:O | N |  |
| PPCS32 | Is the FriendlyCredit Warning attribute supported? | [R2]/D.7.2.2.1.12 | PPCS1:O | N |  |
| PPCS33 | Is the LowCreditWarning attribute supported? | [R2]/D.7.2.2.1.13 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS34 | Is the IHDLowCreditWarning attribute supported? | [R2]/D.7.2.2.1.14 | PPCS1:O | N |  |
| PPCS35 | Is the InterruptSuspend Time attribute supported? | [R2]/D.7.2.2.1.15 | PPCS1:O | N |  |
| PPCS36 | Is the RemainingFriendlyCreditTime attribute supported? | [R2]/D.7.2.2.1.16 | PPCS1:O | N |  |
| PPCS37 | Is the NextFriendlyCreditPeriod attribute supported? | [R2]/D.7.2.2.1.17 | PPCS1:O | N |  |
| PPCS38 | Is the CutOffValue attribute supported? | [R2]/D.7.2.2.1.18 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS39 | Is the TokenCarrierID attribute supported? | [R2]/D.7.2.2.1.19 | PPCS1:O | N |  |
| PPCS40 | Are the Top up Code attributes supported? If so, list supported attributes #1-5. | [R2]/D.7.2.2.2.4 | PPCS1:O | N |  |
| PPCS41 | Are the DebtLabel attributes supported? If so, list supported attributes #1-3. | [R2]/D.7.2.2.3.1 | PPCS1:O | N |  |
| PPCS42 | Are the DebtAmount attributes supported? If so, list supported attributes #1-3. | [R2]/D.7.2.2.3.2 | PPCS1:O | Y [Int: EP# 2] [Int: ATTR# 1,2,3] |  |
| PPCS43 | Are the DebtRecoveryMethod attributes supported? If so, list supported attributes #1-3. | [R2]/D.7.2.2.3.3 | PPCS1:O | N |  |
| PPCS44 | Are the DebtRecoveryStartTime attributes supported? If so, list supported attributes #1-3. | [R2]/D.7.2.2.3.4 | PPCS1:O | N |  |
| PPCS45 | Are the DebtRecoveryCollectionTime attributes supported? If so, list supported attributes #1-3. | [R2]/D.7.2.2.3.5 | PPCS1:O | N |  |
| PPCS46 | Are the DebtRecoveryFrequency attributes supported? If so, list supported attributes #1-3. | [R2]/D.7.2.2.3.6 | PPCS1:O | Y [Int: EP# 2] [Int: ATTR# 1,2] |  |
| PPCS47 | Are the DebtRecoveryAmount attributes supported? If so, list supported attributes #1-3. | [R2]/D.7.2.2.3.7 | PPCS1:O | Y [Int: EP# 2] [Int: ATTR# 1,2] |  |
| PPCS48 | Are the DebtRecoveryVendPercentage attributes supported? If so, list supported attributes #1-3. | [R2]/D.7.2.2.3.8 | PPCS1:O | N |  |
| PPCS49 | Is the PrepaymentAlarmStatus attribute supported? | [R2]/D.7.2.2.5.1 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS50 | Is the PrepayGenericAlarmMask attribute supported? | [R2]/D.7.2.2.5.2 | PPCS1:O | N |  |
| PPCS51 | Is the PrepaySwitchAlarmMask attribute supported? | [R2]/D.7.2.2.5.2 | PPCS1:O | N |  |
| PPCS52 | Is the PrepayEventAlarmMask attribute supported? | [R2]/D.7.2.2.5.2 | PPCS1:O | N |  |
| PPCS53 | Is the HistoricalCostConsumption Formatting attribute supported? | [R2]/D.7.2.2.6.1 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS54 | Is the ConsumptionUnitofMeasurement attribute supported? | [R2]/D.7.2.2.6.2 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS55 | Is the CostUnitofMeasurement attribute supported? | [R2]/D.7.2.2.6.3 | PPCS1:O | N |  |
| PPCS56 | Is the Currency attribute supported? | [R2]/D.7.2.2.6.4 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS57 | Is the CurrentDayCostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.5 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS58 | Is the CurrentDayCostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.6 | PPCS1:O | N |  |
| PPCS59 | Is the PreviousDayCostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.7 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS60 | Is the PreviousDayCostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.8 | PPCS1:O | N |  |
| PPCS61 | Is the PreviousDay2CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.7 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS62 | Is the PreviousDay2CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.8 | PPCS1:O | N |  |
| PPCS63 | Is the PreviousDay3CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.7 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS64 | Is the PreviousDay3CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.8 | PPCS1:O | N |  |
| PPCS65 | Is the PreviousDay4CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.7 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS66 | Is the PreviousDay4CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.8 | PPCS1:O | N |  |
| PPCS67 | Is the PreviousDay5CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.7 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS68 | Is the PreviousDay5CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.8 | PPCS1:O | N |  |
| PPCS69 | Is the PreviousDay6CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.7 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS70 | Is the PreviousDay6CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.8 | PPCS1:O | N |  |
| PPCS71 | Is the PreviousDay7CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.7 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS72 | Is the PreviousDay7CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.8 | PPCS1:O | N |  |
| PPCS73 | Is the PreviousDay8CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.7 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS74 | Is the PreviousDay8CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.8 | PPCS1:O | N |  |
| PPCS75 | Is the CurrentWeekCostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.9 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS76 | Is the CurrentWeekCostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.10 | PPCS1:O | N |  |
| PPCS77 | Is the PreviousWeekCostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.11 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS78 | Is the PreviousWeekCostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.12 | PPCS1:O | N |  |
| PPCS79 | Is the PreviousWeek2CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.11 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS80 | Is the PreviousWeek2CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.12 | PPCS1:O | N |  |
| PPCS81 | Is the PreviousWeek3CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.11 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS82 | Is the PreviousWeek3CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.12 | PPCS1:O | N |  |
| PPCS83 | Is the PreviousWeek4CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.11 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS84 | Is the PreviousWeek4CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.12 | PPCS1:O | N |  |
| PPCS85 | Is the PreviousWeek5CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.11 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS86 | Is the PreviousWeek5CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.12 | PPCS1:O | N |  |
| PPCS87 | Is the CurrentMonthCostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.13 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS88 | Is the CurrentMonthCostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.14 | PPCS1:O | N |  |
| PPCS89 | Is the PreviousMonthCostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS90 | Is the PreviousMonthCostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS91 | Is the PreviousMonth2CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS92 | Is the PreviousMonth2CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS93 | Is the PreviousMonth3CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS94 | Is the PreviousMonth3CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS95 | Is the PreviousMonth4CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS96 | Is the PreviousMonth4CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS97 | Is the PreviousMonth5CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS98 | Is the PreviousMonth5CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS99 | Is the PreviousMonth6CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS100 | Is the PreviousMonth6CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS101 | Is the PreviousMonth7CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS102 | Is the PreviousMonth7CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS103 | Is the PreviousMonth8CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS104 | Is the PreviousMonth8CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS105 | Is the PreviousMonth9CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS106 | Is the PreviousMonth9CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS107 | Is the PreviousMonth10CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS108 | Is the PreviousMonth10CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS109 | Is the PreviousMonth11CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS110 | Is the PreviousMonth11CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS111 | Is the PreviousMonth12CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS112 | Is the PreviousMonth12CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS113 | Is the PreviousMonth13CostConsumptionDelivered attribute supported? | [R2]/D.7.2.2.6.15 | PPCS1:O | Y [Int: EP# 2] |  |
| PPCS114 | Is the PreviousMonth13CostConsumptionReceived attribute supported? | [R2]/D.7.2.2.6.16 | PPCS1:O | N |  |
| PPCS115 | Is the HistoricalFreezeTime attribute supported? | [R2]/D.7.2.2.6.17 | PPCS1:O | N |  |
| PPCS116 | Is the reception of Change Debt command supported? | [R2]/D.7.2.3.3 | PPCS1:O | N |  |
| PPCS117 | Is the reception of Emergency Credit Setup command supported? | [R2]/D.7.2.3.4 | PPCS1:O | N |  |
| PPCS118 | Is the reception of Consumer Top Up command supported? | [R2]/D.7.2.3.5 | PPCS1:O | N |  |
| PPCS119 | Is the reception of CreditAdjustment command supported? | [R2]/D.7.2.3.6 | PPCS1:O | N |  |
| PPCS120 | Is the reception of Change Payment Mode command supported? | [R2]/D.7.2.3.7 | PPCS1:O | N |  |
| PPCS121 | Is the reception of Get Prepay Snapshot command supported? | [R2]/D.7.2.3.8 | PPCS1:O | N |  |
| PPCS122 | Is the reception of Get Top Up Log command supported? | [R2]/D.7.2.3.9 | PPCS1:O | N |  |
| PPCS123 | Is the reception of Set Low Credit Warning Level command supported? | [R2]/D.7.2.3.10 | PPCS1:O | N |  |
| PPCS124 | Is the reception of Get Debt Repayment Log command supported? | [R2]/D.7.2.3.11 | PPCS1:O | N |  |
| PPCS125 | Is the reception of Set Maximum Credit Limit command supported? | [R2]/D.7.2.3.12 | PPCS1:O | N |  |
| PPCS126 | Is the reception of Set Overall Debt Cap command supported? | [R2]/D.7.2.3.13 | PPCS1:O | N |  |
| PPCS127 | Is the generation of Publish Prepay Snapshot command supported? | [R2]/D.7.2.4.2 | PPCS1:O | N |  |
| PPCS128 | Is the generation of Change Payment Mode Response command supported? | [R2]/D.7.2.4.3 | PPCS1:O | N |  |
| PPCS129 | Is the generation of Consumer Top Up Response command supported? | [R2]/D.7.2.4.4 | PPCS1:O | N |  |
| PPCS130 | Is the generation of Get Commands command supported? | [R2]/D.7.2.4.5 | PPCS1:O | N |  |
| PPCS131 | Is the generation of Publish Top Up Log command supported? | [R2]/D.7.2.4.6 | PPCS1:O | N |  |
| PPCS132 | Is the generation of Publish Debt Log command supported? | [R2]/D.7.2.4.7 | PPCS1:O | N |  |
| PPCC1 | Is the Prepayment Cluster supported as a client? | [R2]/D.7 | O | Y [Int: EP# 2] | Smart Energy Application Specific Cluster function capabilities. Prepayment cluster client capabilities |
| PPCC2 | Is the generation of Select Available Emergency Credit command supported? | [R2]/D.7.3.4 /D.7.2.3.1 | PPCC1:O | N |  |
| PPCC3 | RESERVED |  | PPCC1:O | NA |  |
| PPCC4 | Deleted |  |  | NA |  |
| PPCC5 | Is the generation of Change Debt command supported? | [R2]/D.7.3.4 /D.7.2.3.3 | PPCC1:O | N |  |
| PPCC6 | Is the generation of Emergency Credit Setup command supported? | [R2]/D.7.3.4 /D.7.2.3.4 | PPCC1:O | N |  |
| PPCC7 | Is the generation of Consumer Top Up command supported? | [R2]/D.7.3.4 /D.7.2.3.5 | PPCC1:O | N |  |
| PPCC8 | Is the generation of CreditAdjustment command supported? | [R2]/D.7.3.4 /D.7.2.3.6 | PPCC1:O | N |  |
| PPCC9 | Is the generation of Change Payment Mode command supported? | [R2]/D.7.3.4 /D.7.2.3.7 | PPCC1:O | N |  |
| PPCC10 | Is the generation of Get Prepay Snapshot command supported? | [R2]/D.7.3.4 /D.7.2.3.8 | PPCC1:O | Y [Int: EP# 2] |  |
| PPCC11 | Is the generation of Get Top Up Log command supported? | [R2]/D.7.3.4 /D.7.2.3.9 | PPCC1:O | Y [Int: EP# 2] |  |
| PPCC12 | Is the generation of Set Low Credit Warning Level command supported? | [R2]/D.7.3.4 /D.7.2.3.10 | PPCC1:O | N |  |
| PPCC13 | Is the generation of Get Debt Repayment Log Level command supported? | [R2]/D.7.3.4 /D.7.2.3.11 | PPCC1:O | Y [Int: EP# 2] |  |
| PPCC14 | Is the generation of Set Maximum Credit Limit Level command supported? | [R2]/D.7.3.4 /D.7.2.3.12 | PPCC1:O | N |  |
| PPCC15 | Is the generation of Set Overall Debt Cap Level command supported? | [R2]/D.7.3.4 /D.7.2.3.13 | PPCC1:O | N |  |
| PPCC16 | Is the reception of Publish Prepay Snapshot command supported? | [R2]/D.7.3.3 /D.7.2.4.2 | PPCC1:O | Y [Int: EP# 2] |  |
| PPCC17 | Is the reception of Change Payment Mode Response command supported? | [R2]/D.7.3.3 /D.7.2.4.3 | PPCC1:O | N |  |
| PPCC18 | Is the reception of Consumer Top Up Response command supported? | [R2]/D.7.3.3 /D.7.2.4.4 | PPCC1:O | N |  |
| PPCC19 | Is the reception of Get Commands command supported? | [R2]/D.7.3.3 /D.7.2.4.5 | PPCC1:O | N |  |
| PPCC20 | Is the reception of Publish Top Up Log command supported? | [R2]/D.7.3.3 /D.7.2.4.6 | PPCC1:O | Y [Int: EP# 2] |  |
| PPCC21 | Is the reception of Publish Debt Log command supported? | [R2]/D.7.3.3 /D.7.2.4.7 | PPCC1:O | Y [Int: EP# 2] |  |
| TCSW1 | Is the device a Trust Center supporting Trust Center Swap-out? | [R2]/5.4.2.2.3 | O | N | Smart Energy Application Specific Cluster function capabilities. Trust Center Swap-out capabilities |
| TCSW2 | Is the generation of Trust Center keep-alive command supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT1:M |  |  |
|  |  |  | FDT2:M |  |  |
| TCSW3 | Is the backup of the Extended PAN ID to an off-chip device supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT1:M |  |  |
| TCSW4 | Is the backup of the registered device EUI-64 to an off-chip device supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT1:M |  |  |
| TCSW5 | Is the backup of the registered device Install Code to an off-chip device supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT1:M |  |  |
| TCSW6 | Is the backup of the registered device hashed CBKE derived link key to an off-chip device supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT1:M |  |  |
| TCSW7 | Is the restore of the Extended PAN ID from an off-chip device supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT1:M |  |  |
| TCSW8 | Is the restore of the registered device EUI-64 from an off-chip device supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT1:M |  |  |
| TCSW9 | Is the restore of the registered device Install Code from an off-chip device supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT1:M |  |  |
| TCSW10 | Is the restore of the registered device hashed CBKE derived link key from an off-chip device supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT1:M |  |  |
| TCSW11 | Is the discovery of the new Trust Center based on the Extended PAN ID supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT2:M |  |  |
| TCSW12 | Is the rejoin using the CBKE derived link key supported? |  | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT2:M |  |  |
| TCSW13 | Is the Recommision of device supported? |  | FDT1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT2:M |  |  |
|  |  |  | FDT3:M |  |  |
| TCSW14 | Does the device support the Trust Center Swap-Out parameters? | [R2] 5.4.2.2.3.7 | TCSW1:M | [NA or Y/N] [Int: EP# x] |  |
|  |  |  | FDT1:M |  |  |
| MESC1 | Is Multiple ESI supported? | [R2]/5.7 | O | [Y/N] [Int: EP# x] | Smart Energy Application Specific Cluster function capabilities. Multiple ESI Client capabilities |
| MESC2 | Is the discovery of all ESIs in a HAN supported? |  | MESC1:M | [NA or Y/N] [Int: EP# x] |  |
| MESC3 | Is the generation of bindings on discovered ESIs supported? |  | MESC1:M | [NA or Y/N] [Int: EP# x] |  |
| MESC4 | Is determination of the authoritative ESI supported? |  | MESC1:M | [NA or Y/N] [Int: EP# x] |  |
| MESC5 | Is processing of events from multiple ESIs supported? |  | MESC1:M | [NA or Y/N] [Int: EP# x] |  |
| MESC6 | Is resolution of conflicting events received from multiple ESIs supported? |  | MESC1:M | [NA or Y/N] [Int: EP# x] |  |
| MESC7 | Is the notification message for an event sent to at least one ESI that sent the event? |  | MESC1:M | [NA or Y/N] [Int: EP# x] |  |
| MESC8 | Is the event processing based on the authoritative time? |  | MESC1:M | [NA or Y/N] [Int: EP# x] |  |
| MESS1 | Is Multiple ESI supported? | [R2]/5.7 | O | [Y/N] [Int: EP# x] | Smart Energy Application Specific Cluster function capabilities. Multiple ESI Server capabilities |
| MESS2 | Is the TimeStatus attribute supported? |  | MESS1:M | [NA or Y/N] [Int: EP# x] |  |
| DELETED | Is the LastSynchronizedTime attribute supported? |  | MESS1:M | [NA or Y/N] [Int: EP# x] |  |
| MESS3 |  |  |  |  |  |
| MESS4 | Is the ValidUntilTime attribute supported? |  | MESS1:M | [NA or Y/N] [Int: EP# x] |  |
| OTAS1 | Is the OTA Upgrade Cluster supported as a server? | [R9] | O | Y [Int: EP# 1] | Smart Energy Application Specific Cluster function capabilities. OTA Upgrade cluster server capabilities. If supporting OTA upgrade cluster client or server, need to complete OTA Upgrade Cluster PICS document in addition to this document for certification. |
| OTAC1 | Is the OTA Upgrade Cluster supported as a client? | [R9] | O | N | Smart Energy Application Specific Cluster function capabilities. OTA Upgrade cluster client capabilities. If supporting OTA upgrade cluster client or server, need to complete OTA Upgrade Cluster PICS document in addition to this document for certification. |
| TOUCS1 | Is the TOU Calendar Cluster supported as a server? | [R2]/D.9 | O | Y [Int: EP# 3] | Smart Energy Application Specific Cluster function capabilities. Calendar cluster server capabilities |
| TOUCS2 | Is the AuxSwitch1Label attribute supported? | [R2]/D.9.2.2.1.1 | TOUCS1:O | N |  |
| TOUCS3 | Is the AuxSwitch2Label attribute supported? | [R2]/D.9.2.2.1.1 | TOUCS1:O | N |  |
| TOUCS4 | Is the AuxSwitch3Label attribute supported? | [R2]/D.9.2.2.1.1 | TOUCS1:O | N |  |
| TOUCS5 | Is the AuxSwitch4Label attribute supported? | [R2]/D.9.2.2.1.1 | TOUCS1:O | N |  |
| TOUCS6 | Is the AuxSwitch5Label attribute supported? | [R2]/D.9.2.2.1.1 | TOUCS1:O | N |  |
| TOUCS7 | Is the AuxSwitch6Label attribute supported? | [R2]/D.9.2.2.1.1 | TOUCS1:O | N |  |
| TOUCS8 | Is the AuxSwitch7Label attribute supported? | [R2]/D.9.2.2.1.1 | TOUCS1:O | N |  |
| TOUCS9 | Is the AuxSwitch8Label attribute supported? | [R2]/D.9.2.2.1.1 | TOUCS1:O | N |  |
| TOUCS10 | Is the generation of PublishCalendar command supported? | [R2]/D.9.2.3.1 | TOUCS1:O | Y [Int: EP# 3] |  |
| TOUCS11 | Is the generation of PublishDayProfile command supported? | [R2]/D.9.2.3.2 | TOUCS1:M | Y [Int: EP# 3] |  |
| TOUCS12 | Is the generation of PublishWeekProfile command supported? | [R2]/D.9.2.3.3 | TOUCS1:M | Y [Int: EP# 3] |  |
| TOUCS13 | Is the generation of PublishSeasons command supported? | [R2]/D.9.2.3.4 | TOUCS1:M | Y [Int: EP# 3] |  |
| TOUCS14 | Is the generation of PublishSpecialDays command supported? | [R2]/D.9.2.3.5 | TOUCS1:M | Y [Int: EP# 3] |  |
| TOUCS15 | Is the generation of CancelCalendar command supported? | [R2]/D.9.2.3.6 | TOUCS1:O | N |  |
| TOUCS16 | Is the reception of GetCalendar command supported? | [R2]/D.9.2.4.1 | TOUCS1:O | Y [Int: EP# 3] |  |
| TOUCS17 | Is the reception of GetDayProfiles command supported? | [R2]/D.9.2.4.2 | TOUCS1:O | Y [Int: EP# 3] |  |
| TOUCS18 | Is the reception of GetWeekProfiles command supported? | [R2]/D.9.2.4.3 | TOUCS1:O | Y [Int: EP# 3] |  |
| TOUCS19 | Is the reception of GetSeasons command supported? | [R2]/D.9.2.4.4 | TOUCS1:O | Y [Int: EP# 3] |  |
| TOUCS20 | Is the reception of GetSpecialDays command supported? | [R2]/D.9.2.4.5 | TOUCS1:O | Y [Int: EP# 3] |  |
| TOUCS21 | Is the reception of GetCalendarCancellation command supported? | [R2]/D.9.2.4.6 | TOUCS1:O | N |  |
| TOUCC1 | Is the TOU Calendar Cluster supported as a client? | [R2]/D.9 | O | N | Smart Energy Application Specific Cluster function capabilities. Calendar cluster client capabilities |
| TOUCC2 | Is the reception of PublishCalendar command supported? | [R2]/D.9.3.3 /D.9.2.3.1 | TOUCC1:M | NA |  |
| TOUCC3 | Is the reception of PublishDayProfile command supported? | [R2]/D.9.3.3 /D.9.2.3.2 | TOUCC1:M | NA |  |
| TOUCC4 | Is the reception of PublishWeekProfile command supported? | [R2]/D.9.3.3 /D.9.2.3.3 | TOUCC1:M | NA |  |
| TOUCC5 | Is the reception of PublishSeasons command supported? | [R2]/D.9.3.3 /D.9.2.3.4 | TOUCC1:M | NA |  |
| TOUCC6 | Is the reception of PublishSpecialDays command supported? | [R2]/D.9.3.3 /D.9.2.3.5 | TOUCC1:M | NA |  |
| TOUCC7 | Is the reception of CancelCalendar command supported? | [R2]/D.9.3.3 /D.9.2.3.6 | TOUCC1:O | NA |  |
| TOUCC8 | Is the generation of GetCalendar command supported? | [R2]/D.9.3.4 /D.9.2.4.1 | TOUCC1:O | NA |  |
| TOUCC9 | Is the generation of GetDayProfiles command supported? | [R2]/D.9.3.4 /D.9.2.4.2 | TOUCC1:O | NA |  |
| TOUCC10 | Is the generation of GetWeekProfiles command supported? | [R2]/D.9.3.4 /D.9.2.4.3 | TOUCC1:O | NA |  |
| TOUCC11 | Is the generation of GetSeasons command supported? | [R2]/D.9.3.4 /D.9.2.4.4 | TOUCC1:O | NA |  |
| TOUCC12 | Is the generation of GetSpecialDays command supported? | [R2]/D.9.3.4 /D.9.2.4.5 | TOUCC1:O | NA |  |
| TOUCC13 | Is the generation of GetCalendarCancellation command supported? | [R2]/D.9.3.4 /D.9.2.4.6 | TOUCC1:O | NA |  |
| DMCS1 | Is the Device Management Cluster supported as a server? | [R2]/D.10 | O | Y [Int: EP# 3] | Smart Energy Application Specific Cluster function capabilities. Device Management cluster server capabilities |
| DMCS2 | Is the ProviderID attribute supported? | [R2]/D.10.2.2.1.1 | DMCS1:O | N |  |
| DMCS3 | Is the ProviderName attribute supported? | [R2]/D.10.2.2.1.2 | DMCS1:O | Y [Int: EP# 3] |  |
| DMCS4 | Is the ProposedProviderID attribute supported? | [R2]/D.10.2.2.1.3 | DMCS1:O | N |  |
| DMCS5 | Is the ProposedProviderName attribute supported? | [R2]/D.10.2.2.1.4 | DMCS1:O | N |  |
| DMCS6 | Is the ProposedProviderChangeDate/Time attribute supported? | [R2]/D.10.2.2.1.5 | DMCS1:O | N |  |
| DMCS7 | Is the ProposedProviderChangeControl attribute supported? | [R2]/D.10.2.2.1.6 | DMCS1:O | N |  |
| DMCS8 | Is the ReceivedProviderID attribute supported? | [R2]/D.10.2.2.1.7 | DMCS1:O | N |  |
| DMCS9 | Is the ReceivedProviderName attribute supported? | [R2]/D.10.2.2.1.8 | DMCS1:O | N |  |
| DMCS10 | Is the ReceivedProposedProviderID attribute supported? | [R2]/D.10.2.2.1.9 | DMCS1:O | N |  |
| DMCS11 | Is the ReceivedProposedProviderName attribute supported? | [R2]/D.10.2.2.1.10 | DMCS1:O | N |  |
| DMCS12 | Is the ReceivedProposedProviderChangeDate/Time attribute supported? | [R2]/D.10.2.2.1.11 | DMCS1:O | N |  |
| DMCS13 | Is the ReceivedProposedProviderChangeControl attribute supported? | [R2]/D.10.2.2.1.12 | DMCS1:O | N |  |
| DMCS14 | Is the ChangeofTenancyUpdateDate/Time attribute supported? | [R2]/D.10.2.2.2.1 | DMCS1:O | N |  |
| DMCS15 | Is the ProposedTenancyChangeControl attribute supported? | [R2]/D.10.2.2.2.2 | DMCS1:O | N |  |
| DMCS16 | Is the WAN Status attribute supported? | [R2]/D.10.2.2.3.1 | DMCS1:O | N |  |
| DMCS17 | Is the LowMediumThreshold attribute supported? | [R2]/D.10.2.2.4.1 | DMCS1:O | N |  |
| DMCS18 | Is the MediumHighThreshold attribute supported? | [R2]/D.10.2.2.4.2 | DMCS1:O | N |  |
| DMCS19 | Is the reception of Get Change of Tenancy command supported? | [R2]/D.10.2.3.1 | DMCS1:O | N |  |
| DMCS20 | Is the reception of Get Change of Supplier command supported? | [R2]/D.10.2.3.2 | DMCS1:O | N |  |
| DMCS21 | Is the reception of RequestNewPassword command supported? | [R2]/D.10.2.3.3 | DMCS1:O | N |  |
| DMCS22 | Is the reception of GetSiteID command supported? | [R2]/D.10.2.3.4 | DMCS1:O | N |  |
| DMCS23 | Is the reception of Report Event Configuration command supported? | [R2]/D.10.2.3.5 | DMCS1:O | N |  |
| DMCS24 | Is the generation of Publish Change of Tenancy command supported? | [R2]/D.10.2.4.1 | DMCS1:O | N |  |
| DMCS25 | Is the generation of Publish Change of Supplier command supported? | [R2]/D.10.2.4.2 | DMCS1:O | N |  |
| DMCS26 | Is the generation of Request New Password Response command supported? | [R2]/D.10.2.4.3 | DMCS1:O | N |  |
| DMC27 | Is the generation of UpdateSiteID command supported? | [R2]/D.10.2.4.4 | DMCS1:O | N |  |
| DMCS28 | Is the generation of SetEventConfiguration command supported? | [R2]/D.10.2.4.5 | DMCS1:O | N |  |
| DMCS29 | Is the generation of GetEventConfiguration command supported? | [R2]/D.10.2.4.6 | DMCS1:O | N |  |
| DMCC1 | Is the Device Management Cluster supported as a client? | [R2]/D.10 | O | N | Smart Energy Application Specific Cluster function capabilities. Device Management cluster client capabilities |
| DMCC2 | Is the Provider ID attribute supported? | [R2]/D.10.3.2.1.1 | DMCS1:O | NA |  |
| DMCC3 | Is the ReceivedProviderID attribute supported? | [R2]/D.10.3.2.1.2 | DMCS1:O | NA |  |
| DMCC4 | Is the Price Event Configuration attribute set supported? | [R2]/D.10.3.2.2 | DMCS1:O | NA |  |
| DMCC5 | Is the Metering Event Configuration attribute set supported? | [R2]/D.10.3.2.3 | DMCS1:O | NA |  |
| DMCC6 | Is the Messaging Event Configuration attribute set supported? | [R2]/D.10.3.2.4 | DMCS1:O | NA |  |
| DMCC7 | Is the Prepayment Event Configuration attribute set supported? | [R2]/D.10.3.2.5 | DMCS1:O | NA |  |
| DMCC8 | Is the Calendar Event Configuration attribute set supported? | [R2]/D.10.3.2.6 | DMCS1:O | NA |  |
| DMCC9 | Is the Device Management Event Confguration attribute set supported? | [R2]/D.10.3.2.7 | DMCS1:O | NA |  |
| DMCC10 | Is the Tunnel Event Configuration attribute set supported? | [R2]/D.10.3.2.8 | DMCS1:O | NA |  |
| DMCC11 | Is the OTA Event Configuration attribute set supported? | [R2]/D.10.3.2.9 | DMCS1:O | NA |  |
| DMCC12 | Is the reception of Publish Change of Tenancy command supported? | [R2]/D.10.3.3 /D.10.2.4.1 | DMCS1:O | NA |  |
| DMCC13 | Is the reception of Publish Change of Supplier command supported? | [R2]/D.10.3.3 /D.10.2.4.2 | DMCS1:O | NA |  |
| DMCC14 | Is the reception of Request New Password Response command supported? | [R2]/D.10.3.3 /D.10.2.4.3 | DMCS1:O | NA |  |
| DMCC15 | Is the reception of UpdateSiteID command supported? | [R2]/D.10.3.3 /D.10.2.4.4 | DMCS1:O | NA |  |
| DMCC16 | Is the reception of SetEventConfiguration command supported? | [R2]/D.10.3.3 /D.10.2.4.5 | DMCS1:O | NA |  |
| DMCC17 | Is the reception of GetEventConfiguration command supported? | [R2]/D.10.3.3 /D.10.2.4.6 | DMCS1:O | NA |  |
| DMCC18 | Is the generation of Get Change of Tenancy command supported? | [R2]/D.10.3.4 /D.10.2.3.1 | DMCS1:O | NA |  |
| DMCC19 | Is the generation of Get Change of Supplier command supported? | [R2]/D.10.3.4 /D.10.2.3.2 | DMCS1:O | NA |  |
| DMCC20 | Is the generation of RequestNewPassword command supported? | [R2]/D.10.3.4 /D.10.2.3.3 | DMCS1:O | NA |  |
| DMCC21 | Is the generation of GetSiteID command supported? | [R2]/D.10.3.4 /D.10.2.3.4 | DMCS1:O | NA |  |
| DMCC22 | Is the generation of Report Event Configuration command supported? | [R2]/D.10.3.4 /D.10.2.3.5 | DMCS1:O | NA |  |
| EVCS1 | Is the Events Cluster supported as a server? | [R2]/D.11 | O | Y [Int: EP# 2] | Smart Energy Application Specific Cluster function capabilities. Events cluster server capabilities |
| EVCS2 | Is the reception of GetEventLog command supported? | [R2]/D.11.2.3.1 | EVCS1:O | Y [Int: EP# 2] |  |
| EVCS3 | Is the reception of ClearEventLog command supported? | [R2]/D.11.2.3.2 | EVCS1:O | N |  |
| EVCS4 | Is the generation of PublishEvent command supported? | [R2]/D.11.2.4.1 | EVCS1:O | Y [Int: EP# 2] |  |
| EVCS5 | Is the generation of PublishEventLog command supported? | [R2]/D.11.2.4.2 | EVCS1:O | Y [Int: EP# 2] |  |
| EVCC1 | Is the Events Cluster supported as a client? | [R2]/D.11 | O | N | Smart Energy Application Specific Cluster function capabilities. Events cluster client capabilities |
| EVCC2 | Is the reception of PublishEvent command supported? | [R2]/D.11.3.3 /D.11.2.4.1 | DMCS1:O | NA |  |
| EVCC3 | Is the reception of PublishEventLog command supported? | [R2]/D.11.3.3 /D.11.2.4.2 | DMCS1:O | NA |  |
| EVCC4 | Is the generation of GetEventLog command supported? | [R2]/D.11.3.4 /D.11.2.3.1 | DMCS1:O | NA |  |
| EVCC5 | Is the generation of ClearEventLog command supported? | [R2]/D.11.3.4 /D.11.2.3.2 | DMCS1:O | N |  |
| EMCS1 | Is the Energy Management Cluster supported as a server? | [R2]/D.12 | O | N | Smart Energy Application Specific Cluster function capabilities. Energy Management cluster server capabilities |
| EMCS2 | Is the LoadControlState attribute supported? | [R2]/D.12.2.2.1 | EMCS1:M | NA |  |
| EMCS3 | Is the CurrentEventID attribute supported? | [R2]/D.12.2.2.2 | EMCS1:M | NA |  |
| EMCS4 | Is the CurrentEventStatus attribute supported? | [R2]/D.12.2.2.3 | EMCS1:M | NA |  |
| EMCS5 | Is the ConformanceLevel attribute supported? | [R2]/D.12.2.2.4 | EMCS1:M | NA |  |
| EMCS6 | Is the MinimumOffTime attribute supported? | [R2]/D.12.2.2.5 | EMCS1:M | NA |  |
| EMCS7 | Is the MinimumOnTime attribute supported? | [R2]/D.12.2.2.5 | EMCS1:M | NA |  |
| EMCS8 | Is the MinimumCyclePeriod attribute supported? | [R2]/D.12.2.2.5 | EMCS1:M | NA |  |
| EMCS9 | Is the reception of ManageEvent command supported? | [R2]/D.12.2.4.1 | EMCS1:M | NA |  |
| EMCS10 | Is the generation of ReportEventStatus command supported? | [R2]/D.12.2.5.1 | EMCS1:M | NA |  |
| EMCC1 | Is the Energy Management Cluster supported as a client? | [R2]/D.12 | O | N | Smart Energy Application Specific Cluster function capabilities. Energy Management cluster client capabilities |
| EMCC2 | Is the reception of ReportEventStatus command supported? | [R2]/D.12.3.3 /D.11.2.5.1 | EMCC1:M | NA |  |
| EMCC3 | Is the generation of ManageEvent command supported? | [R2]/D.12.3.4 /D.11.2.4.1 | EMCC1:M | NA |  |
| MDUCS1 | Is the MDU Pairing Cluster supported as a server? | [R2]/D.13 | O | N | Smart Energy Application Specific Cluster function capabilities. MDU Pairing cluster server capabilities |
| MDUCS2 | Is the generation of Pairing Response command supported? | [R2]/D.13.2.3.1 | MDUCS1:O | NA |  |
| MDUCS3 | Is the reception of Pairing Request command supported? | [R2]/D.13.3.3.1 | MDUCS1:M | NA |  |
| MDUCC1 | Is the MDU Pairing Cluster supported as a client? | [R2]/D.13 | O | N | Smart Energy Application Specific Cluster function capabilities. MDU Pairing cluster client capabilities |
| MDUCC2 | Is the reception of Pairing Response command supported? | [R2]/D.13.2.3.1 | MDUCC1:O | NA |  |
| MDUCC3 | Is the generation of Pairing Request command supported? | [R2]/D.13.3.3.1 | MDUCC1:M | NA |  |